## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Issues of System Level Simulation]
Date Submitted: [16 January 2013]
Source: [Seung-Hoon Park, Sungjin Lee, Sangkyu Baek, Yongbin Chang, Daegyun Kim and Won-il Roh]1, [Marco Hernandez]2, [Sungrae Cho]3
Company [Samsung Electronics]1, [NICT]2, [Chung-Ang University]3
Address [416, Maetan-3Dong, Yeongtong-Gu, Suwon-Si, Gyeonggi-Do, 443-742, Korea]1
Voice:[+82-10-9349-9845]1, FAX: [+82-31-279-0813]1, E-Mail:[shannon.park@samsung.com]1
Re: [.]
Abstract: [Issues and proposed compromised scenario & parameters for system-level simulation]
Purpose: [To discuss system-level simulation scenario and drive to good texts for TGD]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Issues of System Level Simulation
January 16, 2013
Samsung

## Slide 3: Simulation condition (Common)
Simulation condition (Common)
Long-term fading | Pathloss: the value depends on center frequency (refer to DCN12-459-3 TG8 channel model document) . Propagation between terminals located below roof-top height at UHF from ITU-R P-1411-6 for 300 MHZ-3000MHz (mandatory) (refer to DCN13-0075-00) . Other pathloss model can be added up to proposers.
Short-term fading | Not considered.
Channel bandwidth | [TBD] MHz (to calculate noise value e.g. -174dBm/Hz x bandwidth)
Maximum TX. power | 20 dBm
Tx/Rx antenna gain | -2.5 dB
Rx noise figure | 7 dB
Receiver sensitivity | -76 dBm (for channel sensing)

## Slide 4: Scenarios & parameters for just PDs (Discovery)
Simulation condition
PD deployment | Uniform drop in 500x500 m2 area The number of PDs : 100, 500, 1000, 5000, 10000
Simulation time | over 10 sec
Iteration | over 1000 rounds
PHY Abstraction | BPSK, 1/2 coding rate Common PHY mode is referred to DCN13-0058 Additional PHY mode is up to proposers
Discovery ID length | 16 bytes
Discovery transmission interval | It depends on proposers.

## Slide 5: Scenarios & parameters for just PDs (Discovery)
Performance metric
  Average number of discovered PDs for the simulation time
  CDF of the discovery latency according to the number of PDs
  Average power consumption [mW/s]
    [comment] we needs power consumption value for TX, RX, IDLE state.

## Slide 6: Issues of Traffic Model for Communication Simulation
Full buffer
  Simple, but latency measurement is not natural
Periodic arrival
  Simple & latency can be assessed easily
  Like voice traffic
  Full buffer case can be simulated by setting short period
Statistical model
  Interrupted Poisson process, or interrupted discrete process, or interrupted renewal process
  More realistic model for burst traffic with more simulation burden
  Needs long time for simulation
    Due to statistically generated inter-arrival time

## Slide 7: Issues of Connectivity Model for Communication Simulation
UDG (unit disk graph):
  Assuming 10% of nodes pairing links (Tx and Rx), according to a transmission range including at most 2 hops.
Link class-based model
  At first Tx is deployed uniform randomly
  Peered Rx of the Tx is deployed under a specific distance from Tx with the probability of link class selection as follows: (for 1-hop case)
    5 m link distance (a%) (e.g. for connectivity)
    10 m link distance (b%) (e.g. for gaming)
    20 m link distance (c%) (e.g. for SNS)
    40 m link distance (d%) (e.g. for advertising)
    80 m link distance (e%) (e.g. public safety)
  This model can be extended to multi-hop by repeating deployment

## Slide 8: Scenarios & parameters for PD links (Comm.)
For communication phase
  Including unicast, multicast, broadcast, groupcast, or multi-hop.
  Only unicast with 1 hop is mandatory link type
Simulation condition
PD deployment | Link class-based model
Traffic | Poisson - Inter arrival time : mean 100 msec
Simulation time | at least 10 sec
Iteration | until getting smooth curve
PHY Abstraction | Perfect rate adaptation with target PER 0.1 Common PHY mode is referred to DCN13-0058 Additional PHY mode is up to proposers
Packet (MPDU) length | 256 bytes (for low data rate) 1024 bytes (for high data rate)

## Slide 9: 9.5. Simulation scenarios & parameters (MAC)
Scenarios & parameters for PD links (Comm.)
  Performance metric (y-axis)
    Areal sum goodput* [bps/km2]
      In packets, the average amount of received packets in, say 100 rounds, per node
    Data packet reception efficiency [ratio]
      The index for data throughput, the data packets successfully received to total data packets transmitted ratio.
      [1 – the total number of successfully received packet to the total number of transmitted packet] including retransmission procedure
    Jain’s fairness index
    Latency [sec]
      Time until success per message, is the average time a node needs to transmit successfully a complete message.
*Goodput is the number of bits in the payload delivered by the network to a certain destination per unit of time.

## Slide 10: Suggestion of Test Scenario for Communication
Density analysis (mandatory)
  The number of links is increasing as
    1, 2, 4, …, up to 512
Packet(MPDU) length analysis (optional)
  Packet length is increasing as
    256, 512, 1024, …, up to 4096 bytes
Packet(MPDU) arrival analysis (optional)
  Mean of inter arrival time is increasing as
    100, 200, 400, … up to 800 msec

## Slide 11: 9.5. Simulation scenarios & parameters (MAC)
Proposed reference system (optional)
  For calibration and convenience of comparison
  Simplified IEEE802.11g
    Most of parameters are borrowed from IEEE802.11g
    The following condition is proposed for simplicity
 | Discovery, Multicast, Groupcast | Unicast
RTS/CTS | Disable | Enable
NAV | Disable | Disable
ACK/NACK | Disable | Enable
CSMA/CA | No increase of CW* | Exponential increase of CW*
Carrier Sensing | Enable | Enable
CWmin | 24 | 24
CWmax | - | 210
Retry Count | Disable | Disable
* CW (Contention Window)
!the number of OFDM tones is 48.

## Slide 12: Items to be integrated to TGD
Item | Abstract | Slide no.
Simulation condition (common) | Long-term fading and related parameters | 3
Simulation condition for discovery | Discovery ID length : 16 bytes | 4
Performance metric for discovery | Average number of discovered PDs CDF of discovery latency Average power consumption | 5
Link type for communication | Only unicast with 1 hop | 8
Simulation condition for communication | Link class-based model Traffic model : Poisson MPDU length : 256, 1024 bytes | 8
Performance metric for communication | Areal sum goodput Data packet reception efficiency Jain’s fairness index Latency | 9
Test scenario for communication | Density analysis | 10