## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Applications and Channels for ULP Communications
Date Submitted: Jan 15, 2013
Source: Jinesh P Nair1, Kiran Bynam1 and Youngsoo Kim1;
1Samsung Electronics
Phone: +918041819999-464, Fax: +918041819999
E-Mail: jinesh.p@samsung.com
Abstract: Approach to select suitable channel models from application scenarios
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Jinesh P Nair, Kiran Bynam and Youngsoo Kim

## Slide 2
Applications and Channels for
ULP Communications

## Slide 3: Outline
Objective
Considerations from Application Scenarios
Observations
Path loss Model
  Path loss Model Example
Small Scale Fading
  Choosing power delay profiles
References

## Slide 4: Objective
Categorize Applications
  Based on Channel Characteristics
Approach to identifying channel models
  Path loss models
  Impulse Response
Purpose
  Fair comparison of the proposals
  System Evaluation

## Slide 5: Considerations from Application Scenarios
No | Applications | Indoor | Outdoor | LOS | NLOS | Shadowing | Range (m) | Comments
1 | Smart Utility | Yes | Yes | Yes | Yes | Low | < 50m | 
2 | Building Automation | Yes | No | Yes | Yes | Low | 5 m to 50 m | 
3 | Inventory and Warehouse Management | Yes | No | Yes | Yes | Low | < 100 m | Corridor Fading
4 | Medical and Healthcare | Yes | Yes | Yes | No | Low | Typ: < 5m Max: ~ 10m | 
5 | Retail Service | Yes | No | Yes | Yes | High | 5 m to 100 m | Good cases of NLOS, Corridor Fading
6 | Telecom Services | Yes | Yes | Yes | No | Low | 2m to 10m | 
7 | Industrial and Infrastructure Monitoring | Yes | Yes | Yes | Yes | Moderate to High | ~ 100 m | Account losses due Industrial environment
8 | Environmental Monitoring | No | Yes | Yes | Yes | Moderate | ~ 100 m | 

## Slide 6: Observations
Range
  Max Range to be supported is around 100 m
  In most cases it is below 30 m
Outdoor/Indoor
  Both exist in many cases
  In Indoor cases the clustering phenomena occurs
LOS/NLOS
  LOS cases exist in all scenarios
  NLOS cases most severe in Retail Service Outlets
Shadowing
  Low to moderate in most cases
  High in cases like Retail Outlets etc.
Frequency bands
  2.4 GHz and 900 MHz

## Slide 7: Path Loss Models
Outdoor Path loss Models
  LOS Model
  NLOS Model
Indoor Path loss Models
  LOS Model
  NLOS Model
Applicable for 900 MHz and 2.4 GHz
Accommodate shadowing losses

## Slide 8: Path Loss Model Example
LoS in Street Canyons (900 MHz and 2.4 GHz)
  Outdoor path loss model (ITU-R P.1411-6 )
  Valid in general but we are interested in below roof top heights
  Median Path Loss Model

## Slide 9: Considerations for Small Scale Fading
Specify Power Delay Profiles
  Identify time after which multi-paths become significant
Flat fading in good number of cases
  Ricean/Rayleigh
  Medical/Healthcare, Telecom Services, Building Automation, Retail Service
Mobility may be pedestrian or below
  Less than 5km/hr
  Doppler spectrum : Classic/Flat

## Slide 10: Choosing Power Delay Profiles
For a signal of BW 3MHz,
Let us take this 3 MHz as the 75 % channel coherence bandwidth
Beyond this frequency selectivity becomes important
Corresponding channel delay spreads
  στ ≈ 1/(30 ×3 ×106) ≈ 10ns
Look for PDPs with significant multi-paths beyond 10 ns
  Corresponding distances at which multi-paths become significant is 3m ( d =st = 3×108×10×10-9)

## Slide 11: Power Delay Profile Example
ITU Models
Tap | Relative delay (ns) | Average power (dB) | Doppler spectrum
1 | 0 | 0 | flat
2 | 50 | -3 | flat
3 | 110 | -10 | flat
4 | 170 | -18 | flat
5 | 290 | -26 | flat
6 | 310 | -32 | flat
ITU Indoor Model
Tap | Relative delay (ns) | Average power (dB) | Doppler spectrum
1 | 0 | 0 | classic
2 | 110 | -9.7 | classic
3 | 190 | -19.2 | classic
4 | 410 | -22.8 | classic
ITU Indoor to Outdoor and Pedestrian

## Slide 12: Summary
Categorized applications based on channel characteristics
Approach to identifying
  Path loss models
  Impulse Response
Future Work
  Specify suitable channel models for IEEE 802.15.4q

## Slide 13: References
1. ITU-R P.1411-6 “Propagation methods for the planning of short range outdoor radiocommunication systems and radio local area networks in the frequency range 300 MHz to 100 GHz” 02/2012
ITU-R P.1238-7 “Propagation data and prediction methods for the planning of indoor radiocommunication systems and radio local area networks in the frequency range 900 MHz to 100 GHz” 02/2012
Marco Hernandez et al, “Channel models for TG8” IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs), Sept 2012
Seidel P and Rappaport T.S, “914 MHz Path Loss Prediction Models for Indoor Wireless Communications in Multi-floored Buildings” IEEE Transactions on Antennas and Propagation, vol. 40, no. 2, Feb. 1992
Chunhui (Allan) Zhu , Betty Zhao, Hou-Cheng Tang “Applications of ULP Wireless Sensors” ” IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs), May 2012