## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PAC Synchronous Operation]
Date Submitted: [11 March 2013]
Source: [Seung-Hoon Park, Kyungkyu Kim, Chiwoo Lim, Hyunseok Ryu, Daegyun Kim and Won-il Roh]
Company [Samsung Electronics]
Address [416, Maetan-3Dong, Yeongtong-Gu, Suwon-Si, Gyeonggi-Do, 443-742, Korea]
Voice:[+82-10-9349-9845]1, FAX: [+82-31-279-0813]1, E-Mail:[shannon.park@samsung.com]
Re: [.]
Abstract: [Introduction of PAC synchronous operation with the benefits]
Purpose: [To issue and discuss about synchronous operation]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PAC Synchronous Operation
March, 2013
Samsung

## Slide 3: What is Synchronization?
Refer from Wikipedia,
  Synchronization is the coordination of events to operate a system in unison.
Refer from the paper [1],
  Synchronization is enabling a common time scale among the participating nodes

## Slide 4: Network-wise Synchronization
A single link synchronization
  Symbol-level synchronization by preamble
  A Tx-Rx link synchronization is not sufficient for PAC.
    PAC operations such as discovery and communication are participated by multiple devices.
Network-wise synchronization
  Synchronization accuracy
    Frame-level or symbol-level
  Time to synchrony
  Scalability

## Slide 5: Centralized vs. Distributed Synchronization
Centralized synchronization
  Unidirectional(Master-slave) synchronization
  Synchronization of a distant clock to a reference time
    A central coordinator or a sync-signal generator sends reference sync-signal such as beacon.
Distributed synchronization
  Mutual(multi point to multi point) synchronization
  Synchronization to a common time base via the exchange of local time information among nodes
 | Centralized | Distributed
Time to synchrony | Fast | Slow
Scalability | No | Yes
Accuracy | Very high | Low to High

## Slide 6: Message-based vs. Pulse-based Distributed Synchronization
Message-based approach
  Exchange time information via MAC-layer packet
Pulse-based approach
  Exchange time information via physical layer
Why pulse-based?
  Message-based approach is based on asynchronous network  time to synchrony is large, low accuracy
  Synchronization before discovery phase should be supported for PAC.

## Slide 7: Pros from Synchronization
Low duty cycling for discovery
  A small portion of time is consumed for discovery
High capacity
  Channel access upon common time base
  Scheduling and interference management

## Slide 8: Synchronous Operation
Synchronization
  Initial, and background operation
Peer discovery
  Discovery of peer’s ID in the synchronized interval
  Refer : IEEE 802. 15-12-0534-00-0008
Peering
  Link establishment
Communication
  Synchronous channel access & interference management

## Slide 9: Conclusion
Synchronous operation
  It is required for IEEE 802.15.8 PAC system
Pulse-based distributed synchronization
  It is a reasonable way to achieve synchronization as considering PAC features

## Slide 10: References
[1] Distributed synchronization in wireless networks, Simeone, Osvaldo ; Spagnolini, Umberto ; Bar-Ness, Yesheskel ; Strogatz, Steven H., Signal Processing Magazine, IEEE Volume: 25 , Issue: 5, Digital Object Identifier: 10.1109/MSP.2008.926661, Publication Year: 2008 , Page(s): 81 - 97

## Slide 11: Comparison of two ways for Peer Discovery
Peer discovery with peering (post-peering)
PD2
PD1
Device
Discovery
Peering
* Terminologies are temporally used for explanation
Peer
Discovery
Beacon
Beacon
Discovery of device identifications such as device address
Discovery of peer identities
Beacon
Beacon
PD3
Beacon
Beacon
Peering Request
Peering Response
Peering Request
Peering Response
Peering Request
Peering Response
Peer Discovery Request
Peer Discovery Response
Peer Discovery Request
Peer Discovery Response
Peer Discovery Request
Peer Discovery Response
Peer discovery storm!!!

## Slide 12: Comparison of two ways for Peer Discovery
Peer discovery without peering (pre-peering)
PD2
PD1
Peer
Discovery
Peering
* Terminologies are temporally used for explanation
Beacon
Beacon
Discovery of peer identities
Beacon
Beacon
PD3
Beacon
Beacon
Peering Request
Peering Response
PD1 and PD2 can obtain the device identification (e.g. device address) during peering, if required.
PD1 identifies peer from peer identity information from PD2
PD1 sends Peering Request with ID which PD2 can understand