## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [SRU by Radio Resource Measurement & Management for the enhanced reliability]
Date Submitted: [1 Mar. 2013]
Source: [Shusaku Shimada] Company [Schubiquist Technologies Guild]
Address [1-28 Nishiarai, Chuoh-shi, Yamanashi, 409-3802 Japan]
Voice:[+81-55-274-1266], FAX: [+81-3-468-0625], E-Mail:[shusaku@ieee.org]
Re: [Next Steps for IG SRU (IEEE802.15-13-0009-00-0sru)]
Abstract: [SG activity focusing on “Radio resource measurement & management (RRMM)” is requested, in order to reflect the needs of broad potential markets of IEEE802.15 standards including medical and hospital, social infrastructure and industrial control systems.]
Purpose: [To support, reinforce and accelerate the planned next step of IG-SRU commencing swift SG activity by focusing on RRMM toward the diverse and flexible solutions of better spectral resource utilization.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
SRU by “Radio resource measurement & management” for enhanced reliability
Date: 2013-03-20
Authors:

## Slide 3: Radio resource measurement & management (RRMM) for enhanced reliability
The better spectral resource utilization (SRU) is obviously inevitable challenge to achieve the enhanced reliability of IEEE802.15 wireless networks, especially for social infrastructure, medical and healthcare, and industrial control systems using 2.4GHz ISM band.
To achieve such SRU, the standardized RRMM capability should be an imperative element and may facilitate the diverse and flexible solution of SRU.
A well-defined radio resource measurement procedures and resulting information bases are prerequisite elements provided multiple wireless networks in user’s radio sphere and physical environment.

## Slide 4: Radio resource measurement & management (RRMM) for enhanced reliability
< Shared Radio Resource Information >
Radio Resource Management
Entity
Common Media or
Co-located node with plural wireless networks
RM Report
RM
Request
Media Agnostic
Media Agnostic
Media Agnostic
Media Agnostic

## Slide 5: Common network management by shared information
Common network manager is going to be feasible by sharing each information of co-existing network in same area, e.g. hospitals, social facilities and industrial plants using 2.4GHz ISM band.
RRMM reporting system facilitates arbitrating, controlling and managing the radio resource usage in time, frequency and space domains.
Media agnostic approach to share the network information is preferred for eventual network management whatever scheme is employed, e.g. centralized human intervention based on areal policy, fully adaptive autonomous management, or cognitive approach of management.

## Slide 6: Diverse media for network information sharing
Dedicated common wireless channel.
  Classic but seldom available
Information sharing via Internet.
  WPAN tend to take IP reachability which may be common practice in large scale networks near future.
Virtual common channel over multiple networks using Combo-chip.
  Growing trend due to recent VLSI availability, even for small network
Media agnostic approach of common network management is able to sit on top of diverse media for sharing each network information.

## Slide 7: Diverse media for network information sharing
WPANs may opt to have IP gateways which connect to the internet.
WPANs may be organized to have a common back-haul network.
Combo-chips are available which integrate 802.15.4, 15.1 or 802.11
  Co-located node with plural wireless networking is common practice.
Internet
WLAN
WPAN
WPAN
WPAN
Common
IEEE802.11
Back haul
WPAN
WLAN
AP
AP
PAN Coordinator
Combo-chip
< Shared Radio Resource Information >
Common Media or
Co-located node with plural wireless networks

## Slide 8: Examples of measurement procedures to be defined
Existing channel Scan (ED/Passive/Active) has to be a base.
  However the set of statistics with either time-stamped record or synchronized-trap measurement may be instrumental as well.
New measurement
  Noise and interference measurement
  (Hidden node detection)
  Node statistics measurement (error count, timeout count, etc.)
  Media sensing histogram (CCA value, CA count, etc.)
  Channel occupancy measurement (e.g. frame air time statistics)
  Others

## Slide 9: Examples of management reports to be defined
Beacon report
Slotframe report
Data/Ack report
Hopping channel set report
Noise and interference histogram report
(Hidden node report)
Node statistics report
Media sensing histogram report
Channel occupancy report
PANID list report

## Slide 10
Stair up to SG from IG-SRU by focusing on
Radio Resource Measurement & Management (RRMM) for drafting PAR and 5C.
  Because the standardized and explicitly defined
  methods for performing RRMM within IEEE802.15.4
  were a common part of past submissions of SRU and
  the enhanced reliability requirements in various
  applications, e.g. medical/hospital, industrial plant, etc.
Proposal to SC-WNG from IG-SRU

## Slide 11
Straw Poll
Do you agree to propose the stair up of IG-SRU to SG by focusing on Radio Resource Measurement & Management (RRMM) for crafting PAR and 5C.
Yes: 8/ No: 0/Abstain: 0

## Slide 12
References
[1] 15-10-0739r1 “A Proposal toward Better Use of Spectrum Resources in future WPAN”
[2] 15-10/886r0 “Experimental results of High traffic-load situation”
[3] 15-11/161r1 “Current situation in 2.4GHz ISM band”
[4] 15-11/528r0 “Intelligent Spectrum Sensing for vehicular Communications in the ISM Bands”
[5] 15-12/183r0 “Cooperative Channel Segmentation for Interference Mitigation in the 2.4GHz Band”
[6] 15-12/184r1 “IG SRU Technical Document”
[7] 15-12/603r1 “Conceptual proposal of autonomously distributed wireless system based on dynamic multi-layer control”
[8] 15-13/056r0 “Wireless coexistence for industrial automation”