## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Comment Resolution Suggestions
Date Submitted: 19 March 2013
Source: Benjamin A. Rolfe (BCA),
Company: Blind Creek Associates
Address: PO Box 798 Los Gatos CA 95031
Voice: +1 408 332 0725, E-Mail: ben @ blindcreek.com
Re: LB#87 Comment resolution
Abstract: Proposed disposition of CIDs #: 126 127 144 145 148 149 152 153 154 155 156 157 162 170 171 190 208 209 213 216 239 240 assigned to Ben
Purpose: Prepare draft for sponsor balloting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposed Resolutions LB #87 Comments Assigned to Ben
Summary
CIDs #: 126 127 144 145 148 149 152 153 154 155 156 157 162 170 171 190 208 209 213 216 239 240
Re-assign: 163 209 213 216
Accept: 127 148 162 239
Accept in Principle: 149 157 170 190 208
Reject: 240
Duplicates: 145 155 156 171

## Slide 3: Re-assign Grouping
#213, #216: New parameters in the MAC SAP primitives that are not used in the text
Re-assign to appropriate groups (spans more than one)
#153: re-assign to coexistence

## Slide 4: Accept
Accept:
#127 The Ranging Response IE is only included if the request is for two way ranging.
Proposed resolution: Complete the sentence by including, "...Ranging Response IE is included in the Acknowledgment if two way ranging is requested“
#162 Include a table for TVWS OFDM PHY supported features. Make changes to the table numbers.
#239 Insert the parameter "RangingMethod"

## Slide 5: Reject
Reject:
#240: Insert the parameter "Timestamp"
  Reason: Timestamp is already defined in 6.3.13 of the base standard.
Ref: page 57 line 29

## Slide 6: AP # 149
For Mode = 5, the modulation index = 0.33, so it shall not set to zero. Need to assign two bits and set the value accordingly.
Proposed resolution: AP
Details: Change description of Modulation index option field:
  When the FSK Mode field value is 1, 2 or 3:
    0 indicates modulation index is 0.5
    1 = modulation index is 1.0
  When the FSK Mode field value is 4 or 5, reserved.
Rational: Per table 133 FSK modes 4 and 5 have exactly one possible modulation index. For mode 1,2 and 3, there are two modulation index values, so 1 bit is adequate to enumerate which is used.
Ref: page 27 line 25

## Slide 7: AP: #157
Include "Alternating spreading pattern supported" and "Non-Alternating spreading pattern supported"
Accept in Principle (AP)
Add two bit field for spreading patterns supported to table 4id and change Figure 48nq to make the Supported PHY features field 1/2 octets. Also need fields for: 5 bits for FSK modulation modes (table 133), 2 bits for possible mod index (for modes 1-3); remove interleaving field.
Ref: page 29 line 6

## Slide 8: AP #190
Comment summary: To support 1-way ranging the ranging request IE needs a TX timestamp field.
Resolution: Add “Request TX Timestamp” field to figure 48nab; add the field description: “The TX Timestamp field shall be set to the time in nanoseconds, in the senders time reference, when packet containing this IE is transmitted.
Ref: page 36 line 1

## Slide 9: AP #208
Comment: I don't understand this statement "Information on the list of locations of particular valid channel is contained in the IE specified in 5.2.4.33.3." This clause only refers to a geo-location not a channel
Resolved by the resolution of CID #167 per doc #159r1 which revise this format
Ref: page 42 line 28

## Slide 10: #152, 154, 155,156
Comments: List of supported bands includes non-TVWS bands. The table in 5.2.4.32 is based on input from the PHY contributors.
Discussion: This represents what can be encoded in the over-the-air capabilities IE, and allows communication of what a device can do. It doesn’t specify that an particular band be supported or that all bands in this list make sense for all the PHYs and PHY operating parameters.
Resolution: AP 152, 154, 155,156
Ref: page 28 line 20

## Slide 11: AP #126
Comment: Should this be a "shall"? - "The Timestamp parameter will be included…"
Proposed resolution: Delete sentence as it is redundant and incomplete. The correct and complete description is in a following paragraph.
Ref: page 42 line 28

## Slide 12: AP #144, 145: Power Saving IE
Comment: suggests increasing size of the Periodic listening interval field to allow an interval longer than 224 – 1 milliseconds.
Suggested resolution: AP. Change field length to 4 octets and adjust text by removing “with a range of from 0 to
16777215 milliseconds.”
Discussion: Adding 1 octet to the field provides a maximum interval of ~ 50 days. That’s a long nap!
Ref: page 25 line 7

## Slide 13: AP # 209
Comment: Does this sentence refer to "deployment of a peer-to-peer link" or "deployment of peer-to-peer links"?
Suggested resolution Detail:
Change sentence
  “Information required for possible deployment of peer-to-peer link is exchanged in the IE as specified in 5.2.4.33.5.”
  to
  “A device that has access to channel availability information advertises that fact using the Channel information source description IE as specified in 5.2.4.33.5.”
Ref: page 42 line 30

## Slide 14: Need Discussion: #170, 171
Comment: Specify the use of the Generic Implementation specific value. Explain how it is used (at transmitter and receiver), how its use can guarantee interoperability between multiple vendor devices.
Note: Commenter used “generic” but the draft uses the word “general (implementation specific)” so we are assuming the commenter is asking for elaboration of “general”. The description “implementation specific” means the specific content and usage of the ID string when type=6 is outside the scope of this standard;
Discussion: The intended use of this field was to provide for indicating that the contained identification string is implementation and/or vendor specific. ID is encoded as a counted string (figure 48nu). To achieve this, we can define a container, but we can’t define how it is used.
Suggested resolution: To clarify, change “general (implementation specific)” to “Vendor specific” in table 4ih and add before the sentence following figure 48nt as follows: “For other non-reserved values in table 4ih, the Device ID field contains only the ID string field.”
#171 is duplicate of #170
Ref: page 31 table 4ih