## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: FSK and PPM PHY Proposal for IEEE802.15.4q
Date Submitted: March 20, 2013
Source: Guido Dolmans, Maarten Lont, Jac Romme – Holst Centre / Imec-NL, Peng Zhang – Eindhoven University of Technology
Abstract: PHY Proposal for TG4q (ULP) Task Group
Purpose: Provide PHY proposal for IEEE 802.15.4q.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
15-13-0059-03-004q-considerations-for-parameters-for-ulp (K. Byran)
  Minimum Transmit Power of 7 dBm
  Minimum Range required is 30 m
  Data rates scalable from 250 kbps to 1 Mbps
15-13-0052-00-004q-low-power-transceiver-data-rate-analysis (A. Bottomley)
    Maximum payload data rate between 200kbps and 500 kbps
    500 kHz wide channels ; 200ksps symbol rate; 25 to 400 kbps with 2- and 4-FSK
Summary Jan. proposals

## Slide 3: This proposal
4q proposal : modulation, channel spacings, symbol rates, bit rates,Tx power for 400/900/2400MHz band proposal
Wideband and Narrowband modes
FSK and PPM modulation (follow-up of 15-12-0634)
Sensitivity for long range (>30m)

## Slide 4: PPM and DSSS Scaling Rate Comparison
k: information bits number conveyed by -position PPM, from 1 to 8
SF: Spreading Factor= 1, 2, 3… 8.
For example: k=4 PPM results rate 1/4, which is equivalent to SF=4.
Date rate scaling by using different (2^k)- position PPM patterns.
For, x-PPM, assume k information bits is conveyed. So x=2^k, and 2^k positions are used for one PPM symbol.
Then, the code rate can be expressed as r= k/2^k.
Eample:.
For example, if k=4, we have 16-position PPM and rate is 4/16=1/4. It is equivalent to using Spreading factor (SF) k equals to 4, which scales the data rate to 1/4 of the symbol rate (k in here is SF).

## Slide 5: Bandwidth, Symbol Rates, Channels, and Data Rates
Data Rates: 25kbps (SF DSSS = 8 / 2-FSK) to 400kbps (SF =1 / 4-FSK), or PPM equivalents
Spacing / Bandwidth multiples of 100kHz
Two Bandwidths: ~100kHz (narrowband devices; regions/bands when wideband is not possible, or to save power) and ~ 600kHz (DSSS wideband devices)
Two Channel Spacings: 200kHz (narrowband devices) and 1MHz (wideband devices)
Spacing (kHz) | Symbol rates (ksps) | # channels/400MHz | # channels/900MHz | # channels/2400MHz
1000 | 200 | - | China (8), Europe (1) USA (26), Japan (7) | Worldwide (85)
200 | 100 | MICS (15), China (99), US-Europe (10) | China (40), Europe (35) USA (130), Japan (38) | Worldwide (425)

## Slide 6: Motivation
The channel spacing is intentionally chosen larger than the bandwidth for two ULP reasons: it relaxes the channel selection filter specifications and the proposed channel spacing is supported in all regions relaxing the requirement on PLL tuning
When narrowband modulation is used without spreading (e.g FHSS or DSSS) the maximal transmit power (EIRP) is 14dBm (Europe). It is proposed to support a transmit power up to 13dBm, since it is allowed in all regions except in the USA

## Slide 7: Channel Plan 400 MHz Band
Data Rates: 100/200/50/50/25 kbps with 2FSK/4FSK/2PPM/4PPM/16PPM
One Symbol Rate: 100ksps (narrowband devices)
One Channel Spacing: 200kHz (narrowband devices)
  Fc=402 + .2k, k= 0, ….., 14, MICS worldwide
  Fc=470 + .2k, k= 0, ….., 98, China
  Fc=433 + .2k, k= 0, ….., 9, USA/Europe

## Slide 8: Proposed 400 MHz Bands
Frequency Band (MHz) | Region | Symbol rate (ksps) | Modulation | Bit Rate (kb/s)
402-405 | Worldwide (MICS) | 100 | 2FSK/4FSK 2PPM/4PPM/16PPM | 100/200/50/50/25
433 | Europe/USA | 100 | 2FSK/4FSK 2PPM/4PPM/16PPM | 100/200/50/50/25
470-510 | China | 100 | 2FSK/4FSK 2PPM/4PPM/16PPM | 100/200/50/50/25

## Slide 9: Channel Plan 900 MHz Band
Data Rates:25 to 400 kbps
Two Symbol Rates: 100ksps (narrowband devices) and 200 ksps (wideband devices)
Two Channel Spacings: 200kHz (narrowband devices) and 1MHz (wideband devices)
Overall Operation Frequency Band: 779-930 MHz
  Fc=779 + .2k, k= 0, ….., 39, China Narrowband
  Fc=779 + 1k, k= 0 ,…. , 7, China Wideband
  Fc=863 + .2k, k= 0, ….., 34, Europe Narrowband
  Fc=863, k= 0, Europe Wideband
  Fc=902 + .2k, k= 0, ….., 39, USA/Canada/Australia Narrowband
  Fc=902 + 1k, k= 0 ,…. ,25, USA/Canada/Australia Wideband
  Fc=916 + .2k, k= 0, ….., 37, Japan Narrowband
  Fc=916+1k, k= 6, Japan Wideband

## Slide 10: Proposed 900 MHz Bands – Narrowband Devices
Freq. Band (MHz) | Region | Modulation | Bit Rate (kbps) | Symbol Rate (ksymbol/s) | Transmit Power (dBm)
779-787 | China | 2FSK/4FSK/2PPM/4PPM/16PPM | 100/200/50/50/25 | 100 | -11, -5 , 1, 7, 10
863-870 | Europe | 2FSK/4FSK/2PPM/4PPM/16PPM | 100/200/50/50/25 | 100 | -11, -5 , 1, 7, 10, 13
902-928 | USA, Canada, Australia | 2FSK/4FSK/2PPM/4PPM/16PPM | 100/200/50/50/25 | 100 | -11, -5
916-930 | Japan | 2FSK/4FSK/2PPM/4PPM/16PPM | 100/200/50/50/25 | 100 | -11, -5 , 1, 7, 10, 13

## Slide 11: Proposed 900 MHz Bands – DSSS Wideband Devices
Frequency Band (MHz) | Data Rate Mode | Spreading Factor | FSK Modulation | Bit Rate (kb/s) | Symbol Rate (ksps) | Transmit Power (dBm)
779-787 / China 863-870 /Europe 902-928 / USA 916-930 / Japan | 0 | 1 | 4FSK | 400 | 200 | -11, -5 , 1, 7, 10, 13
 | 1 | 1 | 2FSK | 200 | 200 | -11, -5 , 1, 7, 10, 13
 | 2 | 2 | 2FSK | 100 | 200 | -11, -5 , 1, 7, 10, 13
 | 3 | 4 | 2FSK | 50 | 200 | -11, -5 , 1, 7, 10, 13

## Slide 12: Transmit Power
Transmit power (ERP) (dBm) | Supported in
13 | China, Europe, Japan (920-930MHz) US with DSSS
7 | China, Europe, Japan (920-930MHz) US with DSSS
1 | China, Europe, Japan (920-930MHz) US with DSSS
-5 | All
-11 | All

## Slide 13: Channel Plan 2400 MHz Band
Data Rates:50 to 400 kbps
Two Symbol Rates: 100ksps (narrowband devices) and 200 ksps (wideband devices)
Two Channel Spacings: 200kHz (narrowband devices) and 1MHz (wideband devices)
Overall Operation Frequency Band: 2400 MHz ISM band
  Fc= 2400 + .2k, k= 0, ….., 424, Worldwide
  Fc= 2400 + 1k, k= 0 ,…. , 84, Worldwide

## Slide 14: Proposed 2400MHz Bands
Frequency Band (MHz) | Region | Modulation | Bit Rate (kbps) | Symbol Rate (ksymbol/s)
2400-2485 | Worldwide | 2FSK/4FSK 2PPM/4PPM/16PPM | 100/200/50/50/25 | 100
2400-2485 | Worldwide | 2FSK/4FSK SF=1-4 | 50/100/200/400 | 200

## Slide 15: First estimate of receiver sensitivity
Proposal to overcome at least a link budget of 130 dB
Sensitivity:
  -106dBm @ 25kbps (900 MHz)
  -95dBm @ 400kbps (900 MHz)
Is feasible with relaxed noise figure when channel BW is smaller than channel spacing

## Slide 16: Conclusion
PHY proposal for ULP 4q with FSK and PPM modulation
Narrowband FSK/PPM modes and DSSS FSK wideband modes
Data rates 25 kbps to 400 kbps