## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Integration of Ranging Capabilities with PHY supporting CMB
Date Submitted: January 14, 2013
Source: Wolfram Kluge, Dietmar Eggert, Liang Li
Company: [Atmel, Vinno]
Address: [Atmel, Koenigsbruecker Strasse 61, 01099 Dresden, Germany; Vinnotech, Suite 202, Building D, No.2 Xinxi Lu, Beijing, China,]
Re: [Response to Call for Tech Proposals]
Purpose: [To present the method of performing ranging in a narrow-band transceiver using phase measurements]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Motivation
Existing Methods to retrieve Ranging Information
Proposal – Phase Difference Measurement
Overview

## Slide 3: Motivation
Location becomes more and more desired in daily life
Examples: locate medical equipment in hospitals, trace movements of patients and medical personal
Basics for location is ranging: determining the distance between two (or more) devices
Most approaches use different node classes, like anchors, and tags, for example
IEEE 802.15.4 basic paradigm: “low cost and low power devices”
“Know where your devices are …”

## Slide 4: Status - Existing Methods
What does already exist within IEEE 802.15.4?
802.15.4a added UWB and CSS based methods; meanwhile merged into 802.15.4-2011
802.15.4f added LRP UWB (Low Rate Pulse repetition frequency), and ranging based on it; pulse trains in the frequency range of 6.2 through 9.2 GHz are used here
Annex E discusses various concepts and topics around location and ranging
Many PIB attributes and primitive parameters have been added addressing both PHY and MAC level functionality

## Slide 5: Why yet another method?
Standardized methods require either
Significant bandwidth (more than any of the bands for CMB can support)
come with significant complexity
Not suitable for battery operation
or
Provided limited accuracy in indoor as they use the magnitude of the radio signal (RRSI based)
Phase Difference Measurement Technology
supports bands available under CMB
provides scalable accuracy and range
scalable power consumption to support battery operation
Low complexity

## Slide 6: Phase Difference Measurement
Transmitter transmits various carrier signals, receiver takes phase-angle snapshot values for them
Since transmitter and receiver are not locked to a single, common master frequency, the receiver will always see variations in phase
By transmitting on a number of adjacent frequencies, the frequency offset between transmitter and receiver can be eliminated, and as a result, the distance between both calculated from the snapshot values taken
Interaction between originator and responder is needed in a tightly timed loop
Requires new lean PHY
See presentations “15-13-0054-02-004n Proposal of Ranging Capabilities with PHY supporting CMB” “15-12-0651-01-004n Ranging with IEEE 802.15.4 Narrow-Band PHY”

## Slide 7: Phase Difference Measurement
Primitives to allow for adding ranging features that are not accompanied by MCPS-DATA services
MLME-RANGING.request: Requests a ranging measurement between to nodes
Parameters:
  OrigAddrMode Addressing mode of the ranging originator (*)
  OrigPANId PAN Identifier of the ranging originator
  OrigAddr Individual device address of the ranging originator
  RespAddrMode Addressing mode of the ranging responder (*)
  RespPANId PAN Identifier of the ranging responder
  RespAddr Individual device address of the ranging responder
  RangingMode Enumeration, such as PM_RANGING, indicating the actually used ranging algorithm (*)
(*) See next slide

## Slide 8: Phase Difference Measurement
Notes on MLME-RANGING.request
OrigAddrMode & RespAddrMode:
  NO_ADDRESS:
    The current node is the ranging originator of the ranging measurement
    The current node requests a ranging measurement with the responder using the responder address information as destination address for any outgoing frame
  SHORT_ADDRESS, EXTENDED_ADDRESS:
    The current is not the originator of the ranging measurement
    The ranging request is forwarded to the intended ranging originator using the originator address information as destination address for any outgoing frame
    The responder address information is contained within the frame payload
RangingMode:
  PM_RANGING: Phase Difference Measurement
  Further Ranging methods and/or modes could be added later

## Slide 9: Phase Difference Measurement
Primitives to allow for adding ranging features that are not accompanied by MCPS-DATA services (cont.)
MLME-RANGING.confirm: Reports the result of a ranging request
Parameters:
  Status Enumeration indicating the status of the previous request to perform a ranging measurement, such as SUCCESS, RANGING_REJECTED, INVALID_PARAMETER, CHANNEL_ACCESS_FAILURE, etc.
  Distance Measured distance between originator and responder unsigned integer unit: mm
  Distance Quality unsigned integer indicating the confidence level of the ranging measurement in %

## Slide 10: Phase Difference Measurement
PIB attributes:
macPMRangingEnabled: Indicates whether the node currently supports Phase Difference Measurement ranging (both as originator or responder)
phyPMStartFreq, phyPMStopFreq, phyPMStep: start frequency, stop frequency, frequency step for Phase Difference measurement unsigned integer unit: 100 kHz (thus, 16 bits allow for frequencies up to 6.5 GHz) All three parameters define the actually used frequency range for the entire Phase Difference Measurement
PICS may be impacted by defining ranging specific feature sets

## Slide 11: Phase Difference Measurement Loops
Initial Setup Phase for each freq
Measurement
Phase 2
Measurement
Phase 1
phyPMFreqSettleDuration
phyPMTxSetupDurationA
phyPMSamplingDurationB
phyPMTxSetupDurationB
phyPMSamplingDurationA
Inner loop (phyPMInnerLoopRepetitions)
Outer loop (phyPMOuterLoopRepetitions)

## Slide 12: Phase Difference Measurement
PIB attributes (cont.):
phyPMFreqShift: Transmit frequency shift between phase 1 and phase 2 signed integer unit: 100 kHz fPhase2 = fPhase1 + phyPMFreqShift
phyPMFreqSettleDuration Settle duration required for initializing a new frequency unsigned integer unit: us

## Slide 13: Phase Difference Measurement
PIB attributes (cont.):
phyPMTxSetupDurationA Time required for transmitter settling of node A within measurement phase 1 unsigned integer; unit: us
phyPMSamplingDurationB Time required for actual phase measurement of node B within measurement phase 1 unsigned integer; unit: us
phyPMTxSetupDurationB Time required for transmitter settling of node B within measurement phase 2 unsigned integer; unit: us
phyPMSamplingDurationA Time required for actual phase measurement of node A within measurement phase 2 unsigned integer; unit: us

## Slide 14: Phase Difference Measurement
PIB attributes (cont.):
Note: Actual role A or B of originator and responder to be negotiated using initial ranging frame exchange
phyPMOuterLoopRepetitions Repetition count for outer measurement loop including
  phyPMFreqSettleDuration
  phyPMTxSetupDurationA & phyPMTxSetupDurationB
  phyPMSamplingDurationA & phyPMSamplingDurationB
unsigned integer
phyPMInnerLoopRepetitions Repetition count for inner measurement loop including
  phyPMTxSetupDurationA & phyPMTxSetupDurationB
  phyPMSamplingDurationA & phyPMSamplingDurationB
unsigned integer

## Slide 15: Phase Difference Measurement Time
Measurement time required for one frequency = tSingleFreq [us]
tSingleFreq =
phyPMOuterLoopRepetitions * (phyPMFreqSettleDuration + phyPMInnerLoopRepetitions * (phyPMTxSetupDurationA + phyPMSamplingDurationB + phyPMTxSetupDurationB + phyPMSamplingDurationA)) [us]
Actual number of frequencies used during Phase Difference Measurement:
nFreq = (phyPMStopFreq – phyPMStartFreq) / phyPMStep + 1
Overall Phase Difference Measurement time = tPM [us]
tPM = tSingleFreq * nFreq

## Slide 16: Summary
New Method can be integrated in 802.15.4 leveraging the PHY/MAC approach established by existing wide band technologies
Some adjustments required in PIB attributes and primitives