## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Comment Resolution Suggestions
Date Submitted: 19 March 2013
Source: Benjamin A. Rolfe (BCA), James P. K. Gilb (Tensorcom)
Address: PO Box 798 Los Gatos CA 95031
Voice: +1 408 332 0725, E-Mail: ben @ blindcreek.com
Re: LB#87 Comment resolution
Abstract: Resolution detail for CID # 102
Purpose: Prepare draft for sponsor balloting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
CID 102 Delete subclause 5.1.6.7.4 (broadcast is already handled in 802.15.4-2011, reference 5.1.6.1 for transmission and 5.1.6.2 for reception) Delete subclause 6.1.6.7.5. To fix the base standard, make the following changes: 5.1.6.4 (in base standard) Change "Similarly, any frame that is broadcast shall be sent with its AR field set to indicate no acknowledgment requested." to be "Similarly, any frame that is broadcast or has a group address, as defined in IEEE Std 802-2013, shall be sent with its AR field set to indicate no acknowledgement requested."

## Slide 3
5.1.6.2 (in base standard) Change the second sentence of the fourth dashed item from: "Otherwise, if an extended destination address is included in the frame, it shall match macExtendedAddress" to be "Otherwise, if an extended destination address is included in the frame, it shall match either macExtendedAddress or, if macGroupRXMode is set to TRUE, an EUI-64 group address, as defined in IEEE Std 802-2013." 6.4.2 Add the following entry: Attribute: macGroupRXMode Type: Boolean Range: TRUE, FALSE Description: Enables the reception of EUI-64 group addresses. Default: FALSE