## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Technical Proposal for IEEE 802.15.8]
Date Submitted: [6 May, 2013]
Source: [Jeongseok Yu, Woongsoo Na, Hyoungchul Bae, Taejin Kim, Yunseong Lee, Juho Lee, Zeynep Vatandas, Sungrae Cho, and Junbeom Hur] Company [Chung-Ang University, Korea]
Address [Chung-Ang University 221 Heukseok, Dongjak, Seoul 156-756 South Korea]
Voice:[+82-2-824-1394], FAX: [+82-2-824-1394], E-Mail:[jsyu@uclab.re.kr, wsna@uclab.re.kr, hcbae@uclab.re.kr, tjkim@uclab.re.kr, yslee@uclab.re.kr, jhlee@uclab.re.kr, zvatandas@uclab.re.kr, srcho@cau.ac.kr, jbhur@cau.ac.kr]
Re: [This is the original document]
Abstract: []
Purpose: [Technical Proposal for IEEE 802.15.8.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Technical Proposal for IEEE 802.15.8
Jeongseok Yu, Woongsoo Na, Hyoungchul Bae, Taejin Kim, Yunseong Lee, Juho Lee, Zeynep Vatandas, Sungrae Cho, and Junbeom Hur
Chung-Ang University

## Slide 3: Contents (1/2)
Multicast Group Management
  Finding/Joining Multicast Group
  Device Group ID Creation
  Multicast Group Notification Frame (MGNF)
    How to reduce MGNF traffic
    Redundant MGNF Transmission
    UMA-based MGNF Transmission
  Creation and Management of Routing Table
  Leaving Multicast Group
  Mobility Support for Multicast
  Merging Multicast Groups
Multicast/Unicast Routing
  Multicast/Unicast Data Transmission
    Prevention Loopback Problem

## Slide 4: Contents (2/2)
Reliability
  Reliability Support
  Reliable Multicast
Multicast Protocol using Directional Antenna
Peer Discovery
  Energy-Fairness Peer Discovery
  Energy-Efficiency Peer Discovery
Security Mechanism
  Security Modes
  Authentication
  Authorization

## Slide 5: Terminologies
Full-Function PD
  A PD which supports whole spec. including routing table.
  Always relay-enabled
Reduced-Function PD
  Relay-enabled: A reduced-function PD which supports routing table for specific multicast group.
  Relay-disabled: A reduced-function PD which does not support routing table.

## Slide 6: Finding/Joining Multicast Group (1/2)
A multicast group consists of two or more PDs with the same group ID.
A multicast group can be formed only if two or more PDs can recognize themselves.
Multicast Group Finding Process (Support multi-hop)
  Before a PD joins a multicast group, it has to find the multicast group.
Multicast Group Joining Process (Support multi-hop)
  Broadcasts an Advertisement Command Frame (ACF).
  If a PD in the group receives the ACF replies an ARCF (Advertisement Reply Command Frame) to the PD sending the ACF.
  Then, the PD can join the group.

## Slide 7: Finding/Joining Multicast Group (2/2)
Assume the following topology.
If PD A want to join the multicast group, it broadcasts an ACF.
PD B replies with an ARCF to A.
Now, PD A can join the multicast group.
C
E
A
B
G
: Adv Command Frame
: Adv Reply Command Frame
: Candidate PD
: Non-member PD
: Member PD

## Slide 8: Device Group ID Creation (1/2)
A multicast group is determined by application type ID, application specific ID, and application specific group ID.
Therefore, it is inefficient if transmitting all IDs in a frame and managing routing table.
Therefore, we propose a device group ID creation scheme.
  Device group ID should be unique and distributed by a PD sending the first ARCF in the group.
  The PD manages/updates group keys for secure and dynamic multicast group communications after authentication procedures described in security section.
  The PD generates device group ID based on its unicast ID.
  Since a PD’s unicast ID is unique, prefix concatenated by PD’s unicast ID is also unique.

## Slide 9: Device Group ID Creation (2/2)
When two or more multicast groups are merged, the device group ID should be same.
The PD recognizing the existence of two or more multicast groups randomly determines the device group ID for those groups.
Then, the PD notifies to the group that does not have the selected group ID to update multicast group ID.
A may send rekeying messages to update an existing group key for backward secrecy.
A
D
E
: Member PD
B
C
Group ID Notification Frame
Group ID: 5 8
Group ID: 8

## Slide 10: Multicast Group Notification Frame (MGNF) (1/3)
In order to support management of the group, we use MGNF are
  Limiting duplicate ARCF,
  Management of routing table,
  Notifying leaving multicast group,
  Device group ID creation,
  Request for unicast routing,
  Reply for unicast routing,
  Mobility support, and
  Local repair,
  for relay-enabled PDs.
The MGNF has following eight notification types for above purposes.
0  Limiting duplicate ARCF
1  Management of routing table
2  Notifying leaving multicast
3  Device group ID creation
4  Request for unicast routing
5  Reply for unicast routing
  6  Mobility support
  7  Local repair
Notification Type

## Slide 11: Multicast Group Notification Frame (2/3)
Limiting duplicate ARCF
  In order to limit the duplicate ARCF, PDs replying the ARCF multicast a MGNF with type 0 after random time.
Management of routing table
  Each PD in multicast group multicasts MGNFs periodically
  Upon receiving a MGNF, PDs updates the entries of the originator of the MGNF in its routing table.
Detection and Routing Table Update for link breakage
  Due to PD’s mobility, the link can be broken.
  If PDs does not receive any MGNF until timeout, it can detect link breakage.

## Slide 12: Multicast Group Notification Frame (3/3)
Notifying leaving multicast group
  Will be explained in later section
Request for unicast routing
  Will be explained in later section
Reply for unicast routing
  Will be explained in later section
Mobility support
  Will be explained in later section
Local repair
  Will be explained in later section

## Slide 13: Management of MGNF
When a PD belongs to multiple multicast groups, it multicasts MGNF multiple times.
In order to resolve the above problem, a PD may set Destination Address field of MGNF as United Multicast Address (UMA).
The UMA unifies multiple different groups into a single one.
B
D
A
E
C
: Group1 Member PD
: Group2 Member PD
: Group1 and 2 Member PD
MGNF
It can transmit
MGNF to group 1&2
just once
<B’s MGNF>
Destination Address | ……
UMA | ……

## Slide 14: Management of Routing Table (1/2)
In order to support the multi-hop communication, relay-enabled PD maintains routing table.
Whenever a relay-enabled PD receives ACF or ARCF, a routing entry is created in the routing table.
Also, the routing table is updated by receiving MGNF.
A routing table contains
  Destination address
  Next-hop address
  Expiration timer
  Number of hops
  Current_SN
  Device Group ID
  Bitmap
  Last ACF reception time()

## Slide 15: Management of Routing Table (2/2)
PD A’s Routing Table
B
A
C
E
D
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …
B | C |  | 3 | ACF Tx Time | …
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …
B | C |  | 3 | ACF Tx Time | …
PD C’s Routing Table
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | D |  | 1 | ACF Tx Time | …
B | E |  | 2 | ACF Tx Time | …
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | D |  | 1 | ACF Tx Time | …
B | E |  | 2 | ACF Tx Time | …
Example of routing table.

## Slide 16: Leaving Multicast Group
There are several reasons for a PD to leave from the network: (1) by its intention, (2) by mobility, (3) by limited resources.
If a PD wants to leave from a multicast group, it multicasts a MGNF with notification type set to 2. A recipient of MGNF may send rekeying messages to valid group members for forward secrecy.
  Upon receiving the MGNF, a forwarding PD deletes the entry of the originator of the MGNF, and forward the MGNF.
  Upon receiving the MGNF, a non-forwarding PD deletes the entry of the originator of the MGNF, but does not forward the MGNF.

## Slide 17: Mobility Support for Multicast (1/2)
The PDs’ routing table can be changed due to their mobility.
If a PD recognizes that routing table needs to change, it transmits MGNF (notification type = 6) to other PD which needs to change its routing table.
A PD receiving that MGNF changes its routing table.
B
A
A
C
B
Multicast Group Notification Frame
Move

## Slide 18: Mobility Support for Multicast (2/2)
A PD starts local repair if it detects link breakage between multicast group members (due to expiration timer).
Then, the PD multicasts MGNF (notification type = 7) in order to block multiple path with local repair in same group.
And, the PD performing local repair broadcasts an ACF within K-hop coverage.
Therefore, Local repair can mobility support based on finding/joining procedure.
Link
Break
PD
Disappear
Link
Break
Local
Repair
Start
Local
Repair
Start
Advertisement Command Frame

## Slide 19: Multicast Data Transmission
If a PD receives a multicast data frame, it has to decide forwarding the frame or not.
The PD receiving the multicast data frame compares the source address of the data frame and next-hop address entries of its routing table.
For the multicast data transmission, we have to know the following information from multicast data frame:
  Destination address
  Source address
  Originator address
  Sequence number
  Time To Live(TTL)
This information should be included in all multicast data frames.

## Slide 20: Unicast Data Transmission
When a PD want to unicast data frame, the PD finds routing entry of destination address in its routing table.
If the PD finds routing entry of destination address, the PD start to unicast immediately.
If the PD does not finds routing entry of destination address, the PD multicasts a MGNF (Notification type = 4) to group.
If a PD receiving MGNG finds routing entry of destination address , the PD unicasts a MGNF (notification type = 5) to the PD which want to unicast.

## Slide 21: Prevention Loopback Problem
PD prevents multicast/broadcast loopback problem by using SN (Sequence Number) of data frames.
When a PD receives the data frames first time, PD forwards the data frames.
Otherwise, the PD discards the data frames.

## Slide 22: Reliability Support (1/3)
The role of a transmitting PD is to complete successful transmission of its multicast data frame to its multicast members in its routing table within K-hop coverage.
Our reliable multicast uses an implicit ACK mechanism,
  To effectively reduce the unnecessary error control messages.
  i.e., on successful receipt of the multicast data frame, each receiver acts as a transmitter by forwarding the multicast data frame to its 1-hop PDs.
  If this forwarded multicast data frame is overheard by the original transmitter of the multicast data frame, the original transmitter considers it as a successful transmission.
  PDs that does not have any more PDs to multicast transmits an ACK frame instead of forwarding multicast data frame.

## Slide 23: Reliability Support (2/3)
Timeout Mechanism
  To avoid ACK implosion, transmitters send the ACK at random time.
  Randomized timer for ACK transmission to substantially reduce the possibility of contentions.
  If an implicit ACK does not arrive within retransmission timeout, the transmitter retransmits the multicast data frame until R (a maximum retransmit limit) times.
Bitmap
  To support Implicit ACK mechanism, a bitmap is included in a routing table for a relay-enabled PD.
  Bitmap still exists for a relay-disabled PD for only for one-hop PDs.
  The bitmap indicates whether a PD received an ACK from a particular one-hop PD.

## Slide 24: Reliability Support (3/3)
  If immediate ACK is employed,
    If the bitmaps are all set (Tx received all ACKs) before DT expires, the transmitter multicasts the next multicast data frame.
    If any of the bitmaps are not set after DT expires, the transmitter retransmits the multicast data frame.
  If n-block ACK is employed,
    Although the bitmaps are not all set (Tx received all ACKs) before DNT expires, the transmitter can multicast n unacknowledged multicast data frames.
    If any of the bitmaps are not set after DNT expires, the transmitter retransmits the unacknowledged multicast data frames.
For reliable unicast, the role of a transmitting PD is to complete successful transmission of its unicast data frame to its destination.
Every receiving PD along the route from the source to destination shall send ACK to the transmitter in the unicast routing.
The reliable unicast shall using immediate ACK or n-block ACK mechanism.

## Slide 25: Directional Antenna Support (1/2)
If a PD can support directional antenna, it has to additional routing table field which is describes its beam number forwarding to destination in order to transmit frame.
That routing table contains
  Destination address
  Next-hop address
  Expiration timer
  Number of hops
  Current_SN
  Device Group ID
  Bitmap
  Last ACF reception time()
  Beam Number

## Slide 26: Directional Antenna Support (2/2)
If each PD wants to join a multicast group, it performs finding/joining procedure by using all of beams.
During finding/joining procedure, PDs receiving a ACF check the SNR per beams and saves the specific beam with the highest SNR measured in order to find communication beam.
  ACF Transmission  Transmitted by using all beams.
  ARCF Transmission  Transmitted by using specific beam.
  Multicast Data Transmission  Transmitted by using multiple beams by using routing table.

## Slide 27: Energy-Fairness Peer Discovery (1/3)
In order to consider energy fairness, the PD which performs peer discovery shall distinguish other PDs’ loads.
  E.g., A can distinguish other PDs’ load.
A
B
D
E
C
Peer
The PD discovering peer
Load: 0%
Load: 30%
Load: 0%
Load: 70%

## Slide 28: Energy-Fairness Peer Discovery (2/3)
When a PD starting peer discovery transmits a peer discovery frame.
If PDs receive the request frame, they reply response preamble.
  Preamble made by considering load (by using Zadoff-Chu sequence)
A PD receiving response preamble can distinguish PDs’ load and notifies the corresponding PD group.
Then, corresponding PD group, it responses after random time (to avoid collision).
Finally, the PD confirms a specific PD.
Peer Discovery
Discovery Response
Peer ID Notify
Random Access
Confirm
S
1
2
3
4
Discovery Response
Discovery Response
Discovery Response
Random Access

## Slide 29: Energy-Fairness Peer Discovery (3/3)
PDs create a ID by considering their ratio of loads.
Using Zadoff –Chu Sequence, a PD creates a preamble corresponding ID.
Ratio of load | <10% | <20% | <30% | <40% | <50% | <60% | <70% | <80% | <90%
ID | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
<Example of ID creation Table>

## Slide 30: Energy-Efficiency Peer Discovery (1/2)
If there is an appropriate PD which is located within one-hop coverage from a PD performing peer discovery, the PD does not have to discover until K-hops.
In order to energy-efficiency and save network resource, the PD performing peer discovery broadcasts Peer Discovery Request(PDREQ) frame within one-hop coverage.
If an appropriate PD receives the PDREQ frame, it unicasts Peer Discovery Reply(PDREP) frame to a PD which originator of PDREQ frame.
If the PD receives PDREP(s) then broadcasts Peer Discovery Confirm Frame(PDCON) to the appropriate PD(s) within 1-hop coverage in order to peer association.
Peer Discovery Request Frame
Peer Discovery Reply Frame
Peer Discovery Confirm Frame

## Slide 31: Energy-Efficiency Peer Discovery (2/2)
When PDs receive PDREQ, they set timer T for forward.
If a PD which did not replies PDREP receives PDCON, it does not have to forward PDREP because of the PD sending PDREQ finds a peer within one-hop. Then, the PD does not have to forward PDREP delete the timer of the PDREQ.
If the timer expired, to extend coverage of peer discovery the peer forwards PDREQ for extend the coverage of peer discovery.
Timeout
Timeout
Forwarded Peer Discovery Request Frame
Peer Discovery Request Frame
Peer Discovery Reply Frame
Peer Discovery Confirm Frame

## Slide 32: Security Modes
Security mode 1 (non-secure)
  When a PAC device is in security mode 1, it shall never initiate any security procedure
Slide 32

## Slide 33: Security Modes
Security mode 2 (service level enforced security)
  When a PAC device is in security mode 2, it shall not initiate any security procedure before a channel establishment request has been received or a channel establishment procedure has been initiated by itself
  Whether a security procedure is initiated or not depends on the security requirements of the requested channel or service
  Security mode 1 can be considered as a special case of security mode 2 where no service has registered any security requirements
Slide 33

## Slide 34: Security Modes
Security mode 2 (cont.)
  A PAC device in security mode 2 should classify the security requirements of its services using the following attributes
Authentication required | - Before connecting to the application, the remote device must be authenticated
Authorization required | - Access is only granted automatically to trusted PAC devices, or untrusted devices after an authorization procedure - Always requires authentication to verify that the device is the right one
Encryption required | - The link must be changed to encrypted mode, before access to the service is possible

## Slide 35: Security Modes
Security mode 3 (link level enforced security)
  When a PAC device is in security mode 3, it shall initiate security procedures before the channel is established

## Slide 36: Infrastructureless Architecture
No coordinator or AAA (authentication, authorization, accountability) server
Using PIN (symmetric), or certificate (asymmetric) issued by the trusted third party
  Cf) Bluetooth pairing
Slide 36

## Slide 37: Infrastructure Architecture
AAA (authentication, authorization, accountability) server
(Dynamic) Coordinator
  Intermittent connection to the AAA server
Using master key (symmetric) issued by the AAA server, or certificate issued by the AAA server
  Cf) IEEE 802.1x, Kerberos protocol
2G/3G/LTE
AAA server
Server for some services (e.g., advertising)
Authentication &
communication
flow
Communication
flow
coordinator
Slide 37

## Slide 38: Authentication
Process of verifying ‘who’ is at the other end of the link
Performed for devices (PAC_ADDR)
Achieved by authentication procedure based on the stored authentication key (AUTH_KEY) or by peering (entering a PIN)
Slide 38

## Slide 39: Authorization
Process of deciding if device X is allowed to have access to service Y
Trusted devices (authenticated) are allowed to services
Untrusted or unknown devices may require authorization based on interaction before access to services is granted
Authorization always includes authentication
Technically, key would be derived or given (established) to the authorized user
Slide 39

## Slide 40: Authorization
Device trust levels
Trusted device | The device has been previously authenticated, An AUTH_KEY is stored The device is marked as “trusted” in the device DB
Untrusted device | The device has been previously authenticated An AUTH_KEY is stored But the device is not marked as “trusted” in the device DB
Unknown device | No security information is available for this device This is also an untrusted device
Slide 40

## Slide 41: Group Key Distribution
In a network environment where the secure multicast and broadcast service (MBS) is supported, additional group key generation and delivery process is performed optionally after ENC_KEY distribution procedure
Slide 41

## Slide 42: Thank you