## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Technical proposal for PAC
Date Submitted: May 6th, 2013
Source: Jinyoung Chun, Suhwook Kim, Han Gyu Cho (LG Electronics)
Address: LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea
Voice: +82-31-450-1901, FAX: +82-31-450-4049, E-Mail: jiny.chun@lge.com
Re: Pre-proposal for discussion
Abstract: Technical proposal for PAC
Purpose: Pre-proposal for discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline
Motivation
System Assumption
Channel hopping system
  Why channel hopping?
  Details of the system
Conclusion

## Slide 3: Motivation
In these days, a user has many applications in a mobile device and wants to enjoy them simultaneously
  On average, Korean has 46 apps in his phone [1]
  Most famous apps are Gaming, SNS, Weather, Map, Music, News, etc..
We should consider multiple applications on PAC network
  Support multiple application over infrastructure network is relatively easy because it is high layer issue
  However, support multiple application over infrastructure-less network is NOT relatively easy because it is highly coupled with PHY/MAC
[1] http://www.kisa.or.kr/notice/pressView.jsp?b_No=8&d_No=1040&mode=view (written in Korean)

## Slide 4: System Assumption
Characteristics of D2D Communication
  No infrastructure link
  No global synchronization
  Fully distributed topology
System requirement
  Low overhead, low discovery & data latency
  Concurrent mode support
    PD can connect multiple applications/sessions/links at the same time.
  Interference avoidance with legacy systems in unlicensed band
    Other devices are operated by CSMA/CA protocol.
    The bands are divided by multi channels. PDs can use the channels.

## Slide 5: Channel Hopping System
Why channel hopping?
  Concurrent mode supporting
    A PD can have simultaneous communication links for same or different applications.
    Example: User A communicates with User B. But user A wants to discover new user.
  Current operation of WiFi-Direct
    User A disconnects ‘peered link’ and then discover other users.
    User B doesn’t know user A’s behavior. Maybe user B lost the connection and retry to discover.
    Discovery channels are only ch 1,6,11. If User A and User C are at other channels, both users have to move to ch 1,6,11 for discovery at the same time.
    To maintain two links, user A has to be hopping two channels or user C has to move to ch 1. But the second solution causes to converge many users to a channel.

## Slide 6: Channel Hopping System
  PAC proposal
    For multi-connections, PD can do both of discovery and communication at any channel.
    For multi-connections, PD can access multi-channels with minimum loss of the current communication.
Channel hopping system framework

## Slide 7: Channel Hopping System
Details of the system
  Slot-level synchronization
    It’s enough to make channel hopping system.
    A slot is dozens of milliseconds. In a slot, users are operated in contention-based manner.
  Two regions of discovery and communication
    Discovery region: PD can discovery PDs over channels in a discovery region. (refer IEEE 15-13-0281.ppt)
    Communication region: The region can include procedures such as sync, peering, data exchange, except discovery. PD can maintain it’s current communication links whenever the links are in other channels, respectively.
  Hopping pattern
    After/before discovery, two user shares the information of each hopping pattern.
    The hopping pattern can be changed when necessary or by long-term period.
    PD can stop channel hopping during communication frame(e.g. PPDU)if it is longer than a slot.

## Slide 8: Conclusion
We propose channel hopping system for PAC.
  PAC framework consists of discovery region and communication region.
  PD can be hopping over channels in unit of slots in communication region for supporting concurrent mode.
  PD can do both of discovery and communication at any channel.