## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Technical proposal of discovery for PAC
Date Submitted: May 6th, 2013
Source: Jinyoung Chun, Suhwook Kim, Han Gyu Cho (LG Electronics)
Address: LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea
Voice: +82-31-450-1901, FAX: +82-31-450-4049, E-Mail: jiny.chun@lge.com
Re: Pre-proposal for discussion
Abstract: Technical proposal of discovery for PAC
Purpose: Pre-proposal for discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline
System assumption
PAC framework
Discovery of WiFi Direct
Performance analysis
  Simulation assumption & parameters
  Simulation results & analysis
Conclusion

## Slide 3: System Assumption
Characteristics of D2D Communication
  No infrastructure link
  No global synchronization
  Fully distributed topology
System requirement
  Low overhead, low discovery latency
  Concurrent mode support
    PD can connect multiple applications/sessions/links at the same time.
  Interference avoidance with legacy systems in unlicensed band
    Other devices are operated by CSMA/CA protocol.
    The bands are divided by multi channels. PDs can use the channels.

## Slide 4: PAC Framework
Proposed Framework
  Slot-level synchronization
    The length of a slot is dozens of milliseconds.
  It consists of discovery region and communication region.
    Each region consists of more than 1 slot.
    Channel-hopping algorithm can be used in communication region for supporting concurrent mode. (refer IEEE 15-13-0280.ppt)
  Discovery region
    PDs discover PDs over the basic channels within a discovery region. Channels can be allocated by the usage. PDs have to discover the channels it can use. The channels are called to the basic channels here.

## Slide 5: Discovery of WiFi Direct
Discovery procedure
  Scan status
    Scan the whole channels
  Listen status
    Listen others’ discovery signal at a channel selected among 1,6,11 during 1~3H, H=100TU (TU is normally millisecond.)
  Search status
    Transmit own discovery signal at each channel 1, 6, 11 sequentially and wait the response during about 30ms typically.
Weak points
  It’s separated to communication procedure. It can’t keep communication during discovery.
  Discovery is only at channel 1,6,11, but communication is at all channels.

## Slide 6: Performance analysis
Simulation assumption
  Framework
    PD’s frame consists of Discovery regions and Communication regions.
    In wifi direct, discovery region and communication region are similar to search state and listen status. But exactly, listen status is not communication status.
    PD A starts from discovery region or from communication region. PD B starts randomly.
  Discovery success condition
    nA: channel number of PD A in discovery region has the same channel number as PD B in communication region.
    nB : channel number of PD B in communication region.
    Discovery latency = the slot number when nA = nB
  Others
    Total channel number is fixed to 3. (for simple comparison with wifi direct)
    No interference. No distance/pathloss effect.

## Slide 7: Performance analysis(Cont’d)
Simulation parameters
  Channel hopping
    F: Communication region of PD B is fixed as a randomly selected channel.
    H: Communication region of PD B is randomly-hopped by a unit of slot.
  Abbreviation
    S = 1 slot (about 10ms)
    Discovery region= D, D= S
    Communication region= C, C= Randomly selected among 3S, 6S, 9S
  Simulation cases
Cases | Abbreviation | Explanation
Case 1 | F.CD | Fixed communication channel. PD A starts from communication region and then Discovery region.
Case 2 | H.CD | Same as Case 1 except hopped communication channel.
Case 3 | H.DC | Same as Case 2 except PD A starts from discovery region at first.

## Slide 8: Performance analysis(Cont’d)
Simulation results and analysis
Cases | Abbreviation | Discovery latency (S) | Analysis
Case 1 | F.CD | 24.5 | WiFi Direct case.
Case 2 | H.CD | 27.6 | Channel hopping is a solution to support concurrent mode. So it says that there is performance loss to support concurrent mode in WiFi Direct system.
Case 3 | H.DC | 9.9 | If PD A wants to discovery others, the PD has to start from discovery region. So we propose PDs starts from discovery region.

## Slide 9: Conclusion
We makes some discovery requirements for PAC compared to WiFi Direct.
  WiFi Direct
    It can’t support both of discovery and communication at the same time.
    There is performance loss to support the concurrent mode.
  PAC discovery
    PD has to discovery first when PD wakes up.
    PAC has to support discovery without the performance loss of the current communication link.