## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: SC WNG and SC Man Closing Report for May 2013
Date Submitted: 15 May 2013
Source: Pat Kinney, Kinney Consulting LLC
Contact: Pat Kinney, Kinney Consulting LLC
Voice: +1 847 960-3715, E-Mail: pat.kinney@ieee.org
Re: WNG and Maintenance Closing Reports for May 2013 Session
Abstract: WNG and Maintenance Closing Reports for Waikoloa
Purpose: Information to 802.15 WG
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Standing Committees
SC Maintenance:
SC-mag had one meeting with the objectives of presentations and discussions on the ETSI TC ERM requested changes to 802.15.4 and to hear and discuss maintenance requests from Hendricus De Ruijter, and Cristina Seibert
SC WNG:
There were no WNG meeting requests

## Slide 3: SC Maintenance Agenda
ETSI TC ERM change request presentations
ETSI TC ERM email responses
Other SC maintenance requests
  Hendricus De Ruijter
  Cristina Seibert

## Slide 4: SC Maintenance
ETSI TC ERM Change Requests
Bob Heile drafted a reply to the letter ETSI (15-13-218-00) sent to him requesting changes to IEEE Std. 802.15.4e-2012 that has been saved to Mentor (15-13-0226-00)
Presentations:
  Larry Taylor 15-13-0194-01
  Jonathan Simon 15-13-0243-01
  Ludwig Winkel 15-13-0312-00
  McInnis/Harrington 15-13-0316-03
  Tom Herbst 15-13-0326-00
  Ben Rolfe 15-13-0323-00

## Slide 5: SC Maintenance
ETSI TC ERM email responses:
Craig Harmon:
  JTC 1/SC 31 is interested in any modification of 802.15.4 and 8802.15.4, respectively. Might we see a marked up copy of the standard reflecting the changes?
  Absent the detail to see how the ETSI recommendations would be implemented, you are correct . . . there is insufficient information to accept or reject their suggestions.
Andrew Myles:
  I assume you are sending this to me based on my involvement in ISO/IEC JTC1/SC6. I am not aware of any activity in SC6 that is related in any way to 802.15.4. Hope this helps
Paul Duffy:
  Cisco Connected Energy is the Cisco business unit which has developed and is now globally deploying network solutions providing critical communications capabilities for utility grid moderation efforts. A key piece of this solution is our Field Area Network, which is based on the IEEE 802.15.4e/g MAC/PHY. Of the three issues/resolutions discussed within IEEE 802.15-<15-13-0194-01-0mag>
  Frame ID extension. Cisco agrees that the issue must be addressed and supports the proposed resolution.
  IE namespace management. Cisco agrees that the issue must be addressed, but DOES NOT support the proposed resolution. We are happy to work with IEEE to produce a satisfactory solution.
  IE Descriptor format. Cisco DOES NOT agree this is an issue that must be addressed and DOES NOT support the proposed resolution, nor any change which will break compatibility with current implementations of 802.15.4e. We see no technical merit in this proposed change, which will break compatibility with millions of devices deployed to peoples homes.

## Slide 6: SC Maintenance Request
Submission Date: 4/19/2013 Name: Henk de Ruijter Affiliation: Silicon Labs E-Mail: hendricus.deruijter@silabs.com Document's title (include revision/year): d5P802-15-4k_Draft_Standard.pdf Clause number: 9.3 PHY PIB attributes Page: 68
Issue, concern, or question: On line 27, the description in the table says: “The valid symbol rates per band are given in Table 66b.” The issue is that table 66b list the Bit Rate and not the symbol rate.
Proposed change: Insert the following sentence to the end of sub-clause 19.2.2.6 as follows: “When spreading is enabled, the spreading bit rate shall be the value of the bit rate shown in Table 66b.”
In addition, change the description of phyLECIMFSKSymbolRate in sub-clause 9.3 as follows: “When phyLECIMFSKSpreading is FALSE, the valid symbol rates per band are given as the bit rates shown in Table 66b. When phyLECIMFSKSpreading is TRUE, the valid symbol rates per band correspond to the spreading bit rates shown in Table 66b, divided by the value of phyLECIMFSKSpreadingFactor.”

## Slide 7: SC Maintenance Request
Date Submitted: 3/28/2013 Name: Cristina Seibert Affiliation: Silver Spring Networks E-Mail: cseibert@silverspringnet.com Document's title (include revision/year): 802.15.4e-2012 Clause number: 5.2.2.8.1
Page: 79
Issue, concern, or question: Figure 48m has two errors. The first one is the length of the Frame Control field which should be 2 instead of 1 (octets). This is being fixed via the 4k amendment which replaces Figure 48m. The second error is that the Sequence Number is shown as always included when in fact it can be suppressed.
Proposed change: Change Figure 48m to show a length of “0/1” octets for the Sequence Number field. Change sentence in section that states “The Sequence Number field shall be set to the current value of macDSN.” to “When the Sequence Number field is present, it shall be set to the current value of macDSN.”

## Slide 8: Resolutions to SC Maintenance Requests
SC maintenance requests
ETSI TC ERM
  As a result of numerous straw polls (Annex A) taken to determine the next actions for each of the change requests it was agreed to form three teams to work on each of the three ETSI TC ERM requests, these teams will report back to SC-mag at the July plenary
  Team addressing the extension range of values of the 802.15.4 Frame Types consists of Ben Rolfe, Larry Taylor, Tom Herbst, Jussi Haapola, Tim Harrington, and Bill Verso
  Team to define a mechanism suitable for allocation/management of 802.15.4 IE IDs for all requests including external SDOs consists of Ben Rolfe, and Larry Taylor
  Team to review the Information Element TLV structure disconnect with ETSI and propose a resolution consists of Ben Rolfe, Larry Taylor, and Tom Herbst
Hendricus De Ruijter’s and Cristina Seibert’s requests for changes were approved by the SC-mag to be recommended to the 802.15 WG for consideration during the next 802.15.4 revision.

## Slide 9: SC WNG
There was no SC WNG meeting

## Slide 10: Annex A: SC-mag Straw Polls
 | Change request 1 | Change request 2 | Change request 3
Those who support doing nothing to address the change request | 0 | 0 | 0
Those who support addressing the change request (not necessarily the ETSI change requested) | 20 | 14 | 11
 | For | Against | 
Those who support changing the order of LTV for legacy and future devices | 4 | 8 | 
Those who support changing the order of LTV for only future devices | 13 | 0 |