## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Considerations for optimal data rates
Date Submitted: May 2013
Source: Frederik Beer1, Jörg Robert1;
1Friedrich-Alexander-Universität Erlangen-Nürnberg, Information Technology
Phone: +4991318525123, Fax: +4991318525102
E-Mail: frederik.beer@fau.de
Abstract: Some basic considerations about optimal data rates based upon chosen range and sensitivity of selected transceiver chips
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Frederik Beer, Jörg Robert

## Slide 2
Considerations for optimal data rates

## Slide 3: Outline
TX-Power efficiency
Energy per bit
Path Loss
Datarate equation
Transceiver sensitivity
Results
Summary & Conclusion
Outlook

## Slide 4: Objective
Show how the efficiency of transceiver chips can easily be estimated
Derive an equation for achievable datarates based on sensitivity and range
Material for discussion about optimal datarates for 4q

## Slide 5: TX-Power consumption (1)
Transceivers usually have a basic power consumption irrespective of the actual TX-Power
At low datarates (and lower TX-Power) this basic consumption becomes dominant
At high datarates (and higher TX-Power) this basic consumption can be omitted

## Slide 6: TX-Power consumption (2)
Extracted values for several transceivers:
  AT86R231, CC2520, AT86R212, CC1101, SX1231
Example AT86R231 (2.4 GHz, 3V VDD):
PTX [dBm] | PTX [mW] | I [mA] | Ptotal [mW]
3 | 1.995 | 14 | 42
0 | 1 | 11.6 | 34.8
-17 | 0.01995 | 7.4 | 22.2

## Slide 7: TX-Power consumption (3)
Chart: PTX [mW]
| 1.9952623149688797 | 1 | 1.9952623149688792E-2
P_total [mW] | 42 | 34.8 | 22.2
If this values are plotted and a linear fitting is applied, we get a linear curve like:
For AT86RF231:

## Slide 8: TX-Power consumption (4)
Transceiver Chip |  | 
AT86RF231 | 10.017 | 22.933 mW
CC2520 | 14.809 | 58.192 mW
AT86RF212 | 3.8817 | 36.675 mW
CC1101 | 3.6122 | 48.577 mW
SX1232 | 3.9153 | 46.426 mW
Transceiver Chip |  | 
AT86RF231 | 10.017 | 22.933 mW
CC2520 | 14.809 | 58.192 mW
AT86RF212 | 3.8817 | 36.675 mW
CC1101 | 3.6122 | 48.577 mW
SX1232 | 3.9153 | 46.426 mW
Example (AT86RF231):
80 Octets @ 250 kbps, 0 dBm:
80 Octets @ 500 kbps, 3 dBm:

## Slide 9
Most considerations are based upon the Eb, i.e. the energy per bit
Energy per bit at transmitter can be expressed as:
with R being the data rate in bit/s
Energy per bit (1)

## Slide 10
For successful signal reception a certain amount of energy per bit has to be guaranteed
Energy per bit at the receiver:
With L being the path loss
Energy per bit (2)

## Slide 11
For the following considerations the path loss will be assumed to be the free space loss
= =1
Path loss

## Slide 12
Combining the former equations, the datarate can be expressed as a function of the transmit power, distance, wavelength
The minimum energy per bit () can be calculated by equations for different modulation types or derived from the sensitivity of transceiver chips
Datarate equation

## Slide 13: Transceiver sensitivity
TI CC1101:
GFSK, 1200 bps: -111dBm
1bps: -141dBm,
38,400 bps: -104dBm
1bps: -150dBm,
SX1232:
FSK, 1200 bps: -119dBm
1bps: -150dBm,
38,400 bps: -106dBm
1bps: -152dBm,

## Slide 14: Transceiver sensitivity
AT86RF212
BPSK, 20,000 bps: -110dBm
1bps: -153dBm,
40,00 bps: -108dBm
1bps: -154dBm,
Approx. necessary for successful reception, independent from data rate.

## Slide 15: Results (1)
868 (915) MHz
2.4 GHz

## Slide 16: Results (2)
868 (915) MHz
2.4 GHz

## Slide 17: Results (3)
868 (915) MHz
2.4 GHz
Worst case scenario:

## Slide 18: Summary
For maximum efficiency higher transmission powers and data rates are favorable, within limits of hardware capabilities, maximum current consumption and available spectrum
The maximum datarate is limited by the desired range, TX-Power, frequency and RF environment

## Slide 19: Conclusion
Define the desired range, frequency band and application scenarios
THEN define the best datarate for this

## Slide 20: Outlook
FEC might be a favorable option for some application scenarios
Examine other techniques, e.g. hopping
More detailed channel models for the application scenarios necessary