## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ NICT PHY Proposal, Part A ]
Date Submitted: [ July 6th, 2013 ]
Source: [ Marco Hernandez, Huan-Bang Li, Igor Dotlić, Ryu Miura ]
Company: [ NICT ]
Address: [ 3-4 Hikarino-oka, Yokosuka, 239-0847, Japan ]
Voice:[+81 46-847-5439] Fax: [+81 46-847-5431] E-Mail:[]
Re: [In response to call for technical proposals to TG8]
Abstract: [ ]
Purpose: [Material for discussion in 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline
General PHY description (Part A)
Physical Channels
Data Formatting
Modulation Parameters
Multiple Antenna Procedures
PHY Layer Procedures (Part B)
  discovery, random access
Optional FSK modulation

## Slide 3: Common mode PHY Description

## Slide 4: Physical Channels
Frequency bands of operation are:
  Sub-GHz, 2.4 GHz and 5.7 GHz bands.
Those are selected because they do not require operation license. Hence, implementers only comply with local regulations. Moreover, those bands cover all PAC applications in terms of mobility and operational distance.

## Slide 5: Proposed frequency band allocations
Channelization of 5.7 GHz band
  Such frequency band ranges from 5.725 GHz to 5.875 GHz, which is divided into 14 channels of 10 MHz. By regulation, the maximum transmit power at the input antenna is 1 W. The central frequencies are given by
  fc = 5735 MHz + 10n for n = 0, 1, ..., 13
Channelization of 2.4 GHz band
  Such frequency band ranges from 2.4 GHz to 2.5 GHz, which is divided into 9 channels of 10 MHz. By regulation, the maximum transmit power at the input antenna is 1 W. The central frequencies are given by
  fc = 2410 MHz + 10n for n = 0, 1, ..., 8

## Slide 6: Physical Channels
Channelization of 920 MHz band (Japan)
  Such frequency band ranges from 915.9 MHz to 929.7 MHz. However, this frequency band is divided according to the maximum power at the input antenna and maximum bandwidth allowed by regulations.
  Option 1: frequency band ranges from 915.9 MHz to 928.1 MHz and divided into 61 basic channels of 200 kHz. The bandwidth rule tolerance: 200 n kHz, where n=1,2,3,4,5. Therefore, the maximum bandwidth is 1 MHz.
  Option 2: The frequency band ranges from 928.1 MHz to 929.7 MHz and divided by 16 basic channels of 100 kHz. The bandwidth tolerance: 100 n kHz, where n=1,2,3,4,5. Therefore, the maximum bandwidth is 500 kHz.

## Slide 7: Physical Channels
The basic channelization by regulations in Japan is summarized in the following table:
  1bandwidth rule tolerance: 200 n kHz, where n=1,2,3,4,5.
  2bandwidth rule tolerance: 100 n kHz, where n=1,2,3,4,5.

## Slide 8: Physical Channels
Proposed channelization

## Slide 9: Data Formatting
The physical layer protocol data unit (PPDU) is formed by concatenating synchronization header (SHR), Discovery header (DIS), physical layer header (PHR) and physical layer service data unit (PSDU)
Reference signals for demodulation/equalization are embedded in the PSDU

## Slide 10: PSDU construction
The MAC protocol data unit (MPDU) is passed to the PHY
Such data is encoded by QC-LDPC codes.
QC-LDPC codes allows performance close to turbo codes, besides that encoder/decoder enable high throughput and low implementation complexity (efficient implementation in parallel architectures).
Quasi-cyclic LDPC codes are systematic, linear codes satisfying

## Slide 11: FEC
Codeword , k information bits, n-k parity bits.
Parity check matrix
QC-LDPC codes are defined by a prototype matrix
H is constructed from Hp by replacing each entry [Hp]i,j with either a cyclic shift matrix Pc, identity or null matrices of size ZxZ (final size of H is MpZxNpZ).
If [Hp]i,j=0 , replace it by IZxZ=P0
If [Hp]i,j=“-”, replace it by 0ZxZ
If [Hp]i,j=c , replace it by Pc

## Slide 12: FEC
The cyclic-permutation matrix Pc is obtained by cyclically shifting the columns of P0=IZxZ to the right c times.
Example:

## Slide 13: FEC
QC-LDPC parameters
k= number of information bits, n=number of coded bits,
n-k=number of parity bits.

## Slide 14: FEC
Hp for n=648, Z=27, R=1/2.
0 | - | - | - | 0 | 0 | - | - | 0 | - | - | 0 | 1 | 0 | - | - | - | - | - | - | - | - | - | -
22 | 0 | - | - | 17 | - | 0 | 0 | 12 | - | - | - | - | 0 | 0 | - | - | - | - | - | - | - | - | -
6 | - | 0 | - | 10 | - | - | - | 24 | - | 0 | - | - | - | 0 | 0 | - | - | - | - | - | - | - | -
2 | - | - | 0 | 20 | - | - | - | 25 | 0 | - | - | - | - | - | 0 | 0 | - | - | - | - | - | - | -
23 | - | - | - | 3 | - | - | - | 0 | - | 9 | 11 | - | - | - | - | 0 | 0 | - | - | - | - | - | -
24 | - | 23 | 1 | 17 | - | 3 | - | 10 | - | - | - | - | - | - | - | - | 0 | 0 | - | - | - | - | -
25 | - | - | - | 8 | - | - | - | 7 | 18 | - | - | 0 | - | - | - | - | - | 0 | 0 | - | - | - | -
13 | 24 | - | - | 0 | - | 8 | - | 6 | - | - | - | - | - | - | - | - | - | - | 0 | 0 | - | - | -
7 | 20 | - | 16 | 22 | 10 | - | - | 23 | - | - | - | - | - | - | - | - | - | - | - | 0 | 0 | - | -
11 | - | - | - | 19 | - | - | - | 13 | - | 3 | 17 | - | - | - | - | - | - | - | - | - | 0 | 0 | -
25 | - | 8 | - | 23 | 18 | - | 14 | 9 | - | - | - | - | - | - | - | - | - | - | - | - | - | 0 | 0
3 | - | - | - | 16 | - | - | 2 | 25 | 5 | - | - | 1 | - | - | - | - | - | - | - | - | - | - | 0

## Slide 15: FEC
Hp for n=648, Z=27, R=2/3
25 | 26 | 14 | - | 20 | - | 2 | - | 4 | - | - | 8 | - | 16 | - | 18 | 1 | 0 | - | - | - | - | - | -
10 | 9 | 15 | 11 | - | 0 | - | 1 | - | - | 18 | - | 8 | - | 10 | - | - | 0 | 0 | - | - | - | - | -
16 | 2 | 20 | 26 | 21 | - | 6 | - | 1 | 26 | - | 7 | - | - | - | - | - | - | 0 | 0 | - | - | - | -
10 | 13 | 5 | 0 | - | 3 | - | 7 | - | - | 26 | - | - | 13 | - | 16 | - | - | - | 0 | 0 | - | - | -
23 | 14 | 24 | - | 12 | - | 19 | - | 17 | - | - | - | 20 | - | 21 | - | 0 | - | - | - | 0 | 0 | - | -
6 | 22 | 9 | 20 | - | 25 | - | 17 | - | 8 | - | 14 | - | 18 | - | - | - | - | - | - | - | 0 | 0 | -
14 | 23 | 21 | 11 | 20 | - | 24 | - | 18 | - | 19 | - | - | - | - | 22 | - | - | - | - | - | - | 0 | 0
17 | 11 | 11 | 20 | - | 21 | - | 26 | - | 3 | - | - | 18 | - | 26 | - | 1 | - | - | - | - | - | - | 0

## Slide 16: FEC
Hp for n=648, Z=27, R=3/4
16 | 17 | 22 | 24 | 9 | 3 | 14 | - | 4 | 2 | 7 | - | 26 | - | 2 | - | 21 | - | 1 | 0 | - | - | - | -
25 | 12 | 12 | 3 | 3 | 26 | 6 | 21 | - | 15 | 22 | - | 15 | - | 4 | - | - | 16 | - | 0 | 0 | - | - | -
25 | 18 | 26 | 16 | 22 | 23 | 9 | - | 0 | - | 4 | - | 4 | - | 8 | 23 | 11 | - | - | - | 0 | 0 | - | -
9 | 7 | 0 | 1 | 17 | - | - | 7 | 3 | - | 3 | 23 | - | 16 | - | - | 21 | - | 0 | - | - | 0 | 0 | -
24 | 5 | 26 | 7 | 1 | - | - | 15 | 24 | 15 | - | 8 | - | 13 | - | 13 | - | 11 | - | - | - | - | 0 | 0
2 | 2 | 19 | 14 | 24 | 1 | 15 | 19 | - | 21 | - | 2 | - | 24 | - | 3 | - | 2 | 1 | - | - | - | - | 0

## Slide 17: FEC
Hp for n=648, Z=27, R=5/6
17 | 13 | 8 | 21 | 9 | 3 | 18 | 12 | 10 | 0 | 4 | 15 | 19 | 2 | 5 | 10 | 26 | 19 | 13 | 13 | 1 | 0 | - | -
3 | 12 | 11 | 14 | 11 | 25 | 5 | 18 | 0 | 9 | 2 | 26 | 26 | 10 | 24 | 7 | 14 | 20 | 4 | 2 | - | 0 | 0 | -
22 | 16 | 4 | 3 | 10 | 21 | 12 | 5 | 21 | 14 | 19 | 5 | - | 8 | 5 | 18 | 11 | 5 | 5 | 15 | 0 | - | 0 | 0
7 | 7 | 14 | 14 | 4 | 16 | 16 | 24 | 24 | 10 | 1 | 7 | 15 | 6 | 10 | 26 | 8 | 18 | 21 | 14 | 1 | - | - | 0

## Slide 18: FEC
Hp for n=1944, Z=81, R=1/2
57 | - | - | - | 50 | - | 11 | - | 50 | - | 79 | - | 1 | 0 | - | - | - | - | - | - | - | - | - | -
3 | - | 28 | - | 0 | - | - | - | 55 | 7 | - | - | - | 0 | 0 | - | - | - | - | - | - | - | - | -
30 | - | - | - | 24 | 37 | - | - | 56 | 14 | - | - | - | - | 0 | 0 | - | - | - | - | - | - | - | -
62 | 53 | - | - | 53 | - | - | 3 | 35 | - | - | - | - | - | - | 0 | 0 | - | - | - | - | - | - | -
40 | - | - | 20 | 66 | - | - | 22 | 28 | - | - | - | - | - | - | - | 0 | 0 | - | - | - | - | - | -
0 | - | - | - | 8 | - | 42 | - | 50 | - | - | 8 | - | - | - | - | - | 0 | 0 | - | - | - | - | -
69 | 79 | 79 | - | - | - | 56 | - | 52 | - | - | - | 0 | - | - | - | - | - | 0 | 0 | - | - | - | -
65 | - | - | - | 38 | 57 | - | - | 72 | - | 27 | - | - | - | - | - | - | - | - | 0 | 0 | - | - | -
64 | - | - | - | 14 | 52 | - | - | 30 | - | - | 32 | - | - | - | - | - | - | - | - | 0 | 0 | - | -
- | 45 | - | 70 | 0 | - | - | - | 77 | 9 | - | - | - | - | - | - | - | - | - | - | - | 0 | 0 | -
2 | 56 | - | 57 | 35 | - | - | - | - | - | 12 | - | - | - | - | - | - | - | - | - | - | - | 0 | 0
24 | - | 61 | - | 60 | - | - | 27 | 51 | - | - | 16 | 1 | - | - | - | - | - | - | - | - | - | - | 0

## Slide 19: FEC
Hp for n=1944, Z=81, R=2/3
61 | 75 | 4 | 63 | 56 | - | - | - | - | - | - | 8 | - | 2 | 17 | 25 | 1 | 0 | - | - | - | - | - | -
56 | 74 | 77 | 20 | - | - | - | 64 | 24 | 4 | 67 | - | 7 | - | - | - | - | 0 | 0 | - | - | - | - | -
28 | 21 | 68 | 10 | 7 | 14 | 65 | - | - | - | 23 | - | - | - | 75 | - | - | - | 0 | 0 | - | - | - | -
48 | 38 | 43 | 78 | 76 | - | - | - | - | 5 | 36 | - | 15 | 72 | - | - | - | - | - | 0 | 0 | - | - | -
40 | 2 | 53 | 25 | - | 52 | 62 | - | 20 | - | - | 44 | - | - | - | - | 0 | - | - | - | 0 | 0 | - | -
69 | 23 | 64 | 10 | 22 | - | 21 | - | - | - | - | - | 68 | 23 | 29 | - | - | - | - | - | - | 0 | 0 | -
12 | 0 | 68 | 20 | 55 | 61 | - | 40 | - | - | - | 52 | - | - | - | 44 | - | - | - | - | - | - | 0 | 0
58 | 8 | 34 | 64 | 78 | - | - | 11 | 78 | 24 | - | - | - | - | - | 58 | 1 | - | - | - | - | - | - | 0

## Slide 20: FEC
Hp for n=1944, Z=81, R=3/4
48 | 29 | 28 | 39 | 9 | 61 | - | - | - | 63 | 45 | 80 | - | - | - | 37 | 32 | 22 | 1 | 0 | - | - | - | -
4 | 49 | 42 | 48 | 11 | 30 | - | - | - | 49 | 17 | 41 | 37 | 15 | - | 54 | - | - | - | 0 | 0 | - | - | -
35 | 76 | 78 | 51 | 37 | 35 | 21 | - | 17 | 64 | - | - | - | 59 | 7 | - | - | 32 | - | - | 0 | 0 | - | -
9 | 65 | 44 | 9 | 54 | 56 | 73 | 34 | 42 | - | - | - | 35 | - | - | - | 46 | 39 | 0 | - | - | 0 | 0 | -
3 | 62 | 7 | 80 | 68 | 26 | - | 80 | 55 | - | 36 | - | 26 | - | 9 | - | 72 | - | - | - | - | - | 0 | 0
26 | 75 | 33 | 21 | 69 | 59 | 3 | 38 | - | - | - | 35 | - | 62 | 36 | 26 | - | - | 1 | - | - | - | - | 0

## Slide 21: FEC
Hp for for n=1944, Z=81, R=5/6
13 | 48 | 80 | 66 | 4 | 74 | 7 | 30 | 76 | 52 | 37 | 60 | - | 49 | 73 | 31 | 74 | 73 | 23 | - | 1 | 0 | - | -
69 | 63 | 74 | 56 | 64 | 77 | 57 | 65 | 6 | 16 | 51 | - | 64 | - | 68 | 9 | 48 | 62 | 54 | 27 | - | 0 | 0 | -
51 | 15 | 0 | 80 | 24 | 25 | 42 | 54 | 44 | 71 | 71 | 9 | 67 | 35 | - | 58 | - | 29 | - | 53 | 0 | - | 0 | 0
16 | 29 | 36 | 41 | 44 | 56 | 59 | 37 | 50 | 24 | - | 65 | 4 | 65 | 52 | - | 4 | - | 73 | 52 | 1 | - | - | 0

## Slide 22: FEC
There are several techniques for decoding of QC-LDPC codes.
LDPC decoding is represented as a message passing (MP) algorithm in a factor graph with NpZ variable nodes and MpZ check nodes.
  Variable nodes are associated to information bits. The mth parity check node is connected to the nth variable node if [H]m,n=1

## Slide 23: FEC
  For lack of space and not being part of the standard, details of receivers are omitted. We present core ideas and results.
  An efficient decoding implementation is based on Layered LDPC decoding with offset min-sum (OMS) algorithm.
  Efficient and low complex implementation in VLSI architectures.
  Details can be found in the literature.

## Slide 24: Interleaver
In order to minimize latency and integration on parallel architectures within the encoder/decoder implementation, an algebraic interleaver is proposed.
Maximum contention-free quadratic permutation interleaver is defined as
where i=0,1,…,NI-1. NI is interleaver’s length.
If NI is even, f1 is odd and relative prime to NI and all prime factors of NI are also factors of f2.

## Slide 25: Interleaver
Elements of codewords of length n (ci for i=0,1,…,n-1) are interleaved in blocks of NI bits as c∏(j) for j=0,1,…,NI-1
Short length interleaver
Long length interleaver
If (NTc is the total number of coded bits in a packet), in the last codeword, insert Nrem bits stuffing.

## Slide 26: Scrambler
An scrambler is used to shape the data spectrum and to randomize data across users in order to reduce interference.
Gold code generator of length 63 is proposed as scrambler
  PN sequence with period 263 (truly random for long packets)
  Different initialization seeds, enables a different Gold code per user with low correlation respect to other user using a different seed.
63 shift register initialization
  User ID and group ID (already known during discovery phase)
  Fast forward 100 times to reduce PAPR (OFDM)

## Slide 27: Scrambler
The Gold code generator (with polynomials x6+x+1 and x6+x5+x2+x+1) outputs si for i=0,1,…,263-1, which is used to scramble the interleaved codeword bits ci for i=0,1,…,n-1 prior to modulation as
  It may include several codewords in a packet (k=0,1,…NCW-1)
63 shift registers initialization at start of a packet
  User ID (1st register) and group ID (2nd register)
  Fast forward both registers 100 times to reduce PAPR

## Slide 28: Modulation mapper
The scrambled coded bits for i=0,1,…,n-1 are modulated with either BSPK, QPSK or 16QAM modulations, resulting in the a block of complex modulation symbols di for i=0,1,…,Nsym-1, where di=I+jQ
BPSK mapping QPSK mapping
bi | I | Q
0 | 1/√2 | 1/√2
1 | -1/√2 | -1/√2
bi,bi+1 | I | Q
00 | 1/√2 | 1/√2
01 | 1/√2 | -1/√2
10 | -1/√2 | 1/√2
11 | -1/√2 | -1/√2

## Slide 29: Modulation mapper
16 QAM mapping
bi,bi+1,bi+2,bi+3 | I | Q
0000 | 1/√10 | 1/√10
0001 | 1/√10 | 3/√10
0010 | 3/√10 | 1/√10
0011 | 3/√10 | 3/√10
0100 | 1/√10 | -1/√10
0101 | 1/√10 | -3/√10
0110 | 3/√10 | -1/√10
0111 | 3/√10 | -3/√10
1000 | -1/√10 | 1/√10
1001 | -1/√10 | 3/√10
1010 | -3/√10 | 1/√10
1011 | -3/√10 | 3/√10
1100 | -1/√10 | -1/√10
1101 | -1/√10 | -3/√10
1110 | -3/√10 | -1/√10
1111 | -3/√10 | -3/√10

## Slide 30: Layer mapping
Two MIMO technologies are supported: open loop spatial multiplexing and transmit diversity (SFBC) for 2 and 4 antennas.
The [complex] modulation symbols per codeword di for i=0,1,…,Nsym-1 are mapped into several layers
  Layer=independent stream of symbols in a MIMO configuration.
  Rank=number of layers transmitted.
As for
  where is the number of layers and is the number of symbols per layer for the qth codeword.

## Slide 31: Layer mapping
Open loop spatial multiplexing (parallel data streams)
  Here , where P is the number of antennas.
No layers | No codewords | Mapping | Parameter
1 | 1 |  | 
2 | 1 |  | 
2 | 2 |  | 
4 | 1 |  | 
4 | 2 |  | 
No layers | No codewords | Mapping | Parameter
1 | 1 |  | 
2 | 1 |  | 
2 | 2 |  | 
4 | 1 |  | 
4 | 2 |  | 

## Slide 32: Layer mapping
Transmit diversity (same information is Tx from multiple antennas)
  m null symbols at the end such that Nsym+m Mod4=0
No layers | No codewords | Mapping | Parameter
2 | 1 |  | 
4 | 1 |  | 
No layers | No codewords | Mapping | Parameter
2 | 1 |  | 
4 | 1 |  | 

## Slide 33: Precoding
Precoding allows to increase system performance and robustness by feeding back to the transmitter CSI.
Schematic diagram of MIMO support with precoding

## Slide 34: Precoding (Open loop spatial multiplexing )
Open loop spatial multiplexing increases robustness by feeding back the channel’s rank (RI=rank indicator)
  Transmitter chooses a pre-fixed codeword according to RI
  for and
  where is the number of symbols transmitted per antenna.
Single antenna mapping
  where , and

## Slide 35: Precoding (open loop spatial multiplexing )
Multiple antennas mapping
  for and
Transmitter chooses a codeword according to reported ν
Codebook for 2 antennas
index |  | 
0 |  | 
1 |  | 
2 |  | 
3 |  | 
index |  | 
0 |  | 
1 |  | 
2 |  | 
3 |  | 

## Slide 36: Precoding (open loop spatial multiplexing )
Codebook for 4 antennas is based on the Householder theorem:
  If x and y are vectors with the same norm, then exists an orthogonal symmetric matrix W such that y=Wx, where
  W=I-2uuT and ||u||=1.
  Since W is orthogonal and symmetric, then W=W-1 simplifying receiver’s complexity considerably.

## Slide 37: Precoding (open loop spatial multiplexing )
Codebook for 4 antennas
n | un |  |  |  | 
0 |  |  |  |  | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
n | un |  |  |  | 
0 |  |  |  |  | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 

## Slide 38: Precoding (open loop spatial multiplexing )
W is conformed from the codebook for 4 antennas table, where denotes the matrix formed by the columns {c1…cm} of the matrix

## Slide 39: Precoding (transmit diversity)
Support for 2 or 4 antenna configurations and one data stream. Transmit diversity is aimed to increase robustness in scenarios with low SNR, low delay tolerance or no feedback to the transmitter is available or reliable.
Case of 2 antennas
  STBC (Alamouti scheme) for DTF-Spread OFDM
  SFBC (equivalent of STBC) for OFDM

## Slide 40: Precoding (transmit diversity)
SFBC for 2 antennas
  for and

## Slide 41: Precoding (transmit diversity)
In case of 4 antennas a combination of SFBC (2 antennas) with frequency switch transmission diversity is employed.
  for and

## Slide 42: DFT-S OFDM or OFDM
Parameters
is constant and equal to 15 KHz.
Maximum FFT size M=1024
Sampling time
Timing based on a common clock at

## Slide 43: [DFT-S] OFDM
Frame structure (FDD)
One slot contains 7 [DTF-S] OFDM symbols.
Tslot=7680Ts=0.5 msec

## Slide 44: Frame structure (TDD)
S-L1=synchronization for L1
RS-L1=reference signals for L1
RA=random access or channel sounding for MIMO or beamforming.
L1=PD1 transmits and PD2 receives
L2=PD2 transmits and PD1 receives
GP=guard period

## Slide 45: Frame structure (TDD)
GP=(73+1024)Ts=71.42 µsec
Tp=1 Km/3x108m/s=3.3 µsec (worst case).
Last symbol of PD1 arrives to PD2 after Tp, the symbol is detected, PD2 switches from Rx to Tx. Then, the first transmitted symbol of PD2 arrives to PD1 after Tp.
Tp+Tdec+Tsw+Tcomp+Tp=GP
  Tdec=time to detect the last symbol
  Tsw=time to switch from Rx to Tx or vice-versa
  Tcomp=compensation time to align to GP

## Slide 46: [DFT-S] OFDM
Cyclic prefix
73Ts=4.75 usec

## Slide 47: Resource Block
RB is a set of time-frequency slots enabling multiple access

## Slide 48: Resource Block
BW is obtained by concatenating RBs
(2 upper and lower subcarriers are empty)
DFT-S OFDM symbols

## Slide 49: Resource Block
Proposed bandwidths

## Slide 50: Reference signals
Considering a maximum speed of v=100 Km/h (27.78 m/s)
Doppler spread: fd=fc v/c
Min. sampling time to reconstruct the channel: Tc=1/2fd
Slot time Tslot=0.5 msec. Then, one reference symbol per slot is needed in the time domain to estimate the channel correctly.

## Slide 51: Reference signals
Considering 90%, 50% coherence bandwidth:
  where is the RMS delay spread.
Outdoor RMS delay spread is estimated as:
If then freq. selective fading and FDE is needed.
  We propose that the spacing between 2 reference symbols in frequency in a RB is 30 KHz to resolve frequency variations.
d=500m

## Slide 52: Aid for Coherent Detection, FDE, Synchronization, Random Access and Scheduling
Preambles or beacons and reference signals (RSs) are formed with Zadoff-Chu (ZC) sequences of length N.
  Constant-amplitude zero-correlation (CAZAC) sequences
where WN is a primitive nth root of unity, r is a relative prime to N, sequence index k = 0, 1, ...,N-1and q is any integer.

## Slide 53: ZC sequences
ZC sequences have constant amplitude and so its N-point DFT.
  This limits the PAPR and simplifies implementation as only phases have to be generated and stored, besides of bypassing the FFT at transmitter for DFT-S OFDM.
ZC sequences have ideal cyclic autocorrelation, i.e., the correlation with its shifted version is a delta function
  Thus, a [large] set of orthogonal preambles or reference signals is possible to generate.

## Slide 54: Receiver
Optimum detection of coded MIMO systems is given in terms of joint detection and decoding.
  However, implementation complexity is very high.
There are plenty of proposed suboptimum techniques like MMSE-SIC detection

## Slide 55: Receiver
However, iterative MIMO decoding is the most promising approach for low complexity and close optimum performance.
  Core idea: independent MIMO detection and channel decoding.
We present 2 promising systems for spatial multiplexing
  SISO MMSE PIC and sphere decoding

## Slide 56: Receiver
For lack of space and not being part of standard, we do not give details of receivers, only the core ideas and results.
Iterative MIMO decoding
  Reliability information of coded bits (LLRs) is iteratively exchange between SISO MIMO detector and SISO decoder to improve error-rate.

## Slide 57: Receiver
SISO MMSE PIC is a suboptimum algorithm to compute LLRs
  Compute soft-symbols: . PIC: . MMSE filtering: . Intrinsic LLR: LD(zi). Extrinsic LLR: LE=LD=LA.
SISO sphere decoding allows near-optimum performance with low complexity
  Computes intrinsic LLR:
  Extrinsic LLR: LE=L-LA
  Use max-log approximation in L
  LLR is reformulated as a weighted tree search problem that is solved efficiently by the SD algorithm

## Slide 58: Receiver
  PER performance, ½ rate CC, OFDM (1 MHz) with 16QAM symbols in the form of spatial multiplexing for 4x4 antennas with ITU MIMO channel, low correlation and pedestrian.

## Slide 59: Receiver
  PER performance, ½ rate CC, OFDM (1 MHz) with 16QAM symbols in the form of spatial multiplexing for 4x4 antennas with ETSI MIMO channel, low correlation and model A.

## Slide 60: Receiver
Regarding transmit diversity, it is accepted that a wireless system with transmit diversity performs better compared to the same system without transmit diversity.

## Slide 61: Receiver
  PER performance, QC-LDPC(324,648), R=1/2, OFDM (1 MHz) with BPSK symbols for 1x1 antennas with ITU channel pedestrian. SPA=sum-product algorithm. MPA=message passing algorithm. OMS=offset min-sum algorithm.

## Slide 62: End
Thanks for your attention