## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: ETRI Technical PHY proposal for IEEE 802.15 TG8 PAC Standard
Date Submitted: July xx, 2013
Source: Kapseok Chang (ETRI), Byung-Jae Kwak (ETRI), Moon-Sik Lee (ETRI), and Sunggeun Jin
(Daegu University)
Company: ETRI and Daegu University
Address: 218 Gajeong-ro, Yuseong-gu, Daejeon, 305-700, Korea
Voice: +82 42 860 1639 Fax: E-Mail: {kschang, bjkwak, moonsiklee}@etri.re.kr, sgjin@daegu.ac.kr
Re: TG8 Call for Proposal (CFP: IEEE P802.15-13-0069-05-0008)
Abstract: This document presents technical proposals for IEEE 802.15. TG8 PAC standard.
Purpose: Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline
PHY Frame Formats
Preamble Design
  Requirements
  Basic STF Sequence Design
  Proposed Preamble Structure

## Slide 3: PHY Frame Format (1/4)
The transmitted RF signal is generated by modulating the baseband signal.
The baseband signal is composed of multifarious fields. The fields and the timing boundaries between them, that is, general PHY frame format, are composed of the following:
  Preamble field consists of short training field (STF) and long training field (LTF). It is used for automatic gain control (AGC), packet detection, timing/frequency synchronization, channel estimation, and collision detection.
  Header field is used for describing the content of the packet data as well as the protocol used to transfer it.
  Data field is used for the information to intend to transfer.
  Beam Jitter filed is used for SSF (Self Spatial Filtering)

## Slide 4: PHY Frame Format (2/4)
Management frame
  Preamble field includes STF and LTF.
  Header field includes the information related with management.
  For instance
    RTS/CTS
    ACK
    And so on

## Slide 5: PHY Frame Format (3/4)
Discovery in visible range (1/2)
  Based on Self Spatial Filtering (SSF) [8], [10]
  SSF request frame
    A broadcast or multi-cast frame
    Preamble field consists of the STF and LTF.
    Header field includes an indication of SSF request.
    Data field includes the threshold of the correlation level. The threshold is used by other PDs to decide whether they shall send a response message or not.
    Beam Jitter field includes a pre-defined beam-jittered sequence. The beam-jittered sequence is used to calculate the correlation level, which is used in Self Spatial Filtering [1], [8], [10].

## Slide 6: PHY Frame Format (4/4)
Discovery in visible range (2/2)
  SSF response frame
    A unicast frame
    Preamble field consists of the STF and LTF.
    Header field includes the indication of SSF response.
    A SSF Response frame is transmitted by a PD which received a SSF Request frame. Upon receiving a SSF Request frame, a PD calculates the correlation level and transmits SSF Response if the correlation level exceeds the threshold.
    Data field includes the estimated correlation level, the MAC address, and so on.

## Slide 7: Preamble Design (1/12) : Requirements
R1: Robustness against Frequency offset (FO)
  Symbol timing synchronization (STS) shall be acquired in case of start up, discovery, or communication in the absence of knowledge about initial carrier FO in the received signal.
  The STS performance is very sensitive to FO.
R2: Good autocorrelation property
  It is pivotal to minimize timing error.
R3: Lower complexity of preamble detector
R4: Low peak to average power ratio (PAPR)
R5: Implicit indication on which transmission mode among SC and OFDM is employed to support multi-mode coexistence

## Slide 8: Preamble Design (2/12) : Basic STF Sequence Design
Focus on design
  In terms of R1 and R2
    They should be fully satisfied.
  In terms of R3
    It is at least identical to the detector complexity of the base Zadoff-Chu (ZC) sequence specified for STS and FO compensation.
  In terms of R4
    It is at least comparable to the PAPR of the general ZC sequence.
Key ideas
  K1: Combination of base ZC sequence and its modified sequence in frequency domain
  K2: Combination of FO-immune sequence and excellent correlation sequence in time domain

## Slide 9: Preamble Design (3/12) : Basic STF Sequence Design
K1-based first modified ZC (MZC1) sequence (1/2)
  Base ZC sequence br,q,P[]
    Length-P ZC sequence that has the zero autocorrelation property [2]
      where r is a relative prime to P, sequence element index m = 0, 1, ..., P-1, and q is any integer.
    It is set that P is odd and q=0.
      However, since P can be even, the exact number of P is FFS.

## Slide 10: Preamble Design (4/12) : Basic STF Sequence Design
K1-based MZC1 sequence (2/2)
  A distribution of the based ZC sequence and its minus [3]
  At odd m, Length-N MZC1 sequence Sr,q,N[m]
  At even m, Sr,q,N[m]

## Slide 11: Preamble Design (5/12) : Basic STF Sequence Design
K1-based second MZC (MZC2) sequence
  A concatenation of the base ZC sequence [2] and its conjugated sequence [4]
  Length-N MZC2 sequence Sr,q,N[m]

## Slide 12: Preamble Design (6/12) : Basic STF Sequence Design
K2-based Gold Sine Wave (GSW) sequence (1/2)
  So as to achieve robustness against FO
    Half sine wave sequence sin(m/N) is introduced.
  So as to achieve good autocorrelation
    Gold sequence W(m) is introduced.
    For low-complexity detector, binary sequence is preferable.
    It is noted that a length-P pseudo-noise sequence can be used as W(n). Thus, exact sequence is FFS.
  GSW sequence is a multiplication of half sine wave by gold sequence [5].

## Slide 13: Preamble Design (7/12) : Basic STF Sequence Design
K2-based GSW sequence (2/2)
  Length-N GSW sequence sw,N[m]
    G1 and G2 are binary pseudo-noise sequences corresponding to the generator polynomials x5+1 and x5+x4+x+1, respectively.
    [z]N returns the modulo-N value of the integer z.
    2(N-2)/N is applied to maintain the same average-power as MZCs.

## Slide 14: Preamble Design (8/12) : Basic STF Sequence Design
PAPR comparison
  In case of N=64 with P=31 (MZC1, MZC2, GSW) or P=63 (Base ZC)
  GSW outperforms the other sequences.
  Base ZC provides the highest variance of PAPR, and its max PAPR is much more higher than that of random data field, which indicates that the careful selection of sequence index is required.
  On the other hand, MZCs are acceptable since their max PAPR is lower over the random data field.
PAPR | Base ZC | MZC1 | MZC2 | GSW
Average [dB] | 5.8011 | 5.9403 | 6.6069 | 3
Min [dB] | 1.8080 | 5.0235 | 4.3880 | 3
Max [dB] | 13.2950 | 7.0014 | 9.3670 | 3
Variance [dB] | 5.9027 | 0.4969 | 1.7983 | 0

## Slide 15: Preamble Design (9/12) : Basic STF Sequence Design
Detector complexity comparison
  The time-domain MZC1 is complex sequences, so that the computational complexity of MZC1 is identical to that of base ZC.
  The time-domain MZC2 and GSW are not complex but real sequences, so that their computational complexities can be reduced by a factor of ½ over that of base ZC if cross-correlation based detectors [3]-[5] are employed.
  If auto-correlation based detector [6] is employed, there is no complexity difference.

## Slide 16: Preamble Design (10/12) : Basic STF Sequence Design
Evaluation parameter and condition
  Parameter
    Carrier frequency of 2 GHz, system bandwidth of 1.25 MHz (i.e. N=64, P=31 or 63), subcarrier spacing of 15 kHz, FFT/IFFT size of 64, CP duration of 10, a pair of source and destination stations, no transmit diversity, two branch equal gain combining received diversity, and channel model of TU-6 [7] with mobile velocity of 3 km/h.
  Condition
    When evaluating the detection error rate (DER) of STS, a correct detection is declared if the detected sample timing is within half the CP duration.
    The transmitted power for the STF signal is the same as that of the data signals.
    The detection scheme for STS is based on cross-correlation for full-length correlation (FLC) and half-length correlation (HLC) [3]-[5].

## Slide 17: Preamble Design (11/12) : Basic STF Sequence Design
Comparison on robustness against FO
  Effective mean correlation output vs. FO with static TU6 channel [7] and no noise
     is the FO normalized to a subcarrier spacing of the effective OFDM symbol.
      For example, =1 means that one subcarrier spacing is shifted.
To appear in revision

## Slide 18: Preamble Design (12/12) : Basic STF Sequence Design
DER performance
  DER vs. SNR per received antenna with =0 and =2/3 in the TU-6 channel with 3 km/h
To appear in revision

## Slide 19: Preamble Design (1/4) : Proposed Preamble Structure
Time-domain structure (1/3)
  The first symbol of the STF is mainly used for automatic gain control (AGC).
  The second symbol of the STF is used for packet detection, 1st time/frequency synchronization, and implicit transmission-mode indication by positive/negative number of the real-part correlator output.
    Specifically, the real value is positive, it indicates OFDM. Otherwise, it indicates SC.

## Slide 20: Preamble Design (2/4) : Proposed Preamble Structure
Time-domain structure (2/3)
  The first symbol of the LTF is used for 2nd time/frequency synchronization and channel estimation.

## Slide 21: Preamble Design (3/4) : Proposed Preamble Structure
Time-domain structure (3/3)
  The second symbol of the LTE is used for collision detection (CD) [9].
  CD algorithm description
    A PD who wants to transmit data using Random Access selects a random sub-carrier.
    The PD transmits a busy tone in the selected sub-carrier of the second symbol of LTF.

## Slide 22: Preamble Design (4/4) : Proposed Preamble Structure
Frequency-domain structure
  STF
    Either MZCs or frequency-domain GSW will be employed.
    Specific description is TBD.
  LTF
    A binary sequence will be employed for 2nd time/frequency synchronization and channel estimation.
    Specific description is TBD.
Efficiency of the proposed preamble in terms of each requirement
  Regarding R1, R2, and R3
    Time-domain MZC and GSW sequences are robust to FO and correlation, as well as they can reduce the detector complexity because the property of periodic signals can be used.
  Regarding R4
    GSW can be used due to its PAPR efficiency, but MZCs are acceptable because the PAPR of data field is still higher.
  Regarding R5
    The real value of the detector’s peak output implicitly allows us to indicate OFDM or SC transmission mode.
Further study for more verifying these efficiencies will be made at the next meeting.

## Slide 23: References
ETRI, “Technical pre-proposal for IEEE 802.15 TG8 PAC standard,” IEEE 802.15-13-0271-01-0008, May 2013.
NICT, “Preliminary NICT PHY proposal (Part A),” IEEE 802.15-13-0272-00-0008, May 2013.
K. Chang and Y. Han, “Robust replica correlation-based symbol synchronisation in OFDM systems,” Electronics Letters, vol. 44, no. 17, pp. 1024-1025, Aug. 2008.
K. Chang, P. Ho, and Y. Choi, “Signal design for reduced complexity and accurate cell search/synchronization in OFDM-based cellular systems,” IEEE Transactions on Vehicular Technology, vol. 61, no. 9, pp. 4170-4175, Nov. 2012.
K. Chang, S.C. Bang, and H. Kim, “Replica correlation-based synchronization with low complexity and frequency-offset immunity,” ETRI Journal, Oct. 2013, to be appeared.
T.M. Schmidle and D.C. Cox, “Robust frequency and timing synchronization for OFDM,” IEEE Transactions on Communications, vol. 45, no. 12, pp. 1613-1621, Dec. 1997.
3GPP TR25.943 v8.0.0, Technical Specification Group Radio Access Networks: Deployment Aspects, Dec. 2008.
ETRI, “Response to the Call for Applications: Look-and-Link Communication,” IEEE 802-12-0227-01-0008, May 2012.
ETRI, “A Feasible and Efficient Channel Access Scheme for PAC Networks,” IEEE 802.15-13-0374-0x-0008, July 2013.
ETRI, “Self Spatial Filtering Scheme for PAC,” IEEE 802.15-13-0375-0x-0008, July 2013.