## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Low Energy Service Discovery PHY for PAC WPAN]
Date Submitted: [July 2013]
Source: [Tae-Joon Park*, Keun Hyung Lee*, Wun-Cheol Jeong*, Chang-Sub Shin*, Hoyong Kang*, Jewon Lee**, Jae-Min Ahn** ]
Company: [*ETRI, **Chungnam National Univ.]
E-Mail:[*tjpark@etri.re.kr, **jmahn@cnu.ac.kr]
Re: []
Abstract:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Low Energy Service Discovery PHY for PAC WPAN
Tae-Joon Park*, Keun Hyung Lee*, Wun-Cheol Jeong*, Chang-Sub Shin*, Hoyong Kang*, Jewon Lee**, Jae-Min Ahn**
*ETRI, **Chungnam National Univ

## Slide 3: Discovery
Peer discovery & group discovery.
  Discovery is defined as uni-directional.
  Mutual discovery is two uni-directional discoveries
Properties
  Expedited discovery
  Energy-efficient discovery (e.g. low duty cycle)
  Support high PD density and high discovery traffic
  Efficient spectrum utilization
  Prioritized access to discovery
Source : 15-12-0568-05-0008-tg8-technical-guidance-document.docx

## Slide 4: Common discovery mode for PAC
Low Energy Service Discovery(LESD)
  Discovery
    Channel discovery : common discovery mode channel
    Device discovery : communication channel
  Channel discovery
    Find communication channel information(physical channel)
      Frequency band & channel information
        Application type ID/group ID
        Request | Response | Notification
    Move to communication channel
        Start normal communication process : con. setup, data exchange…
  Avoid to Excessive discovery delay and power consumption
    Overhearing, duty cycling, …
    15-13-0378-00-0008-low-energy-service-discovery-mac-protocol-for-pac-wpan.ppt

## Slide 5: LESD mode for PAC
Separate discovery and management function from communication function
Support interoperability between PAC devices
Separated out of band control channel
Potential applications
  Synchronization, Emergency communication, SMS, . . .

## Slide 6: Common discovery mode PHY
Mainly for discovery function(not communication mode)
  Optimized to discovery mode requirements
  Independent to communication mode technologies
Should not be a big burden : additional PHY
  Lower rate / lower power / smaller (gate) size / easier to implement / …
Coverage
  Longer than communication modes
Source : 15-13-0182-01-0008-common-discovery-mode-for-pac.ppt

## Slide 7: Common discovery mode PHY
Band(MHz) | Modulation | Modulation index | Channel spacing(kHz) | Data rate (kb/s)
Sub-GHz | Filtered 2FSK | 1 | 200 | 50
Low HW implementation complexity
Simple PHY
  IPR free to reduce the debate
   requires well known and simple PHY
  Single mode (modulation type, rate, etc.)

## Slide 8: Example of transmitter structure

## Slide 9: Basic Frame structure
SHR(Preamble + SFD) : 64 bits(48+16)
PHY Header : 1 byte
  Message type (1 bit)
    Request, response, Notification, Preamble(No PSDU field)
  PSDU Length / BRB count (7 bits) : 0 ~ 127
Max PSDU length : 127 bytes
Preamble(48bits)
PHY Header(8bits)
PHY Payload(0~127bits)
SFD(16bits)
SHR
PHR
PSDU
Octets
1
Variable

## Slide 10: Basic Frame structure
SHR(Preamble + SFD) : 64 bits(48+16)
Message type | SFD value for uncoded (PHR+PSDU) | SFD value for coded (PHR+PSDU)
Request | 0110 0011 1011 0001 | 1001 1100 1011 0001
Response | 0110 0011 0100 1110 | 1001 1100 0100 1110
Notification | 0110 0011 0110 0011 | 1001 1100 0110 0011

## Slide 11: Basic Frame structure
PHR
Bit string index | 0 | 1–7
Bit mapping | T0 | L6–L0
Field name | FrameType | Frame Length / BRB count
T0 | Frame Type
0 | LESD PSDU
1 | No PSDU

## Slide 12
Symbol duration : 20us
CCA(ED) time : 8 symbol periods
Interframe spacing (IFS)
  macLIFSPeriod : 40 symbol periods
  macSIFSPeriod : 12 symbol periods
Forward error correction (FEC)
  FEC is optional.
  If the SFD indicates that FEC is used, then the FEC is applied to the PHR and PSDU as a single block of data.

## Slide 13: Appendix. Selected simulation results.
Ref. : 15-13-0378-00-0008-low-energy-service-discovery-mac-protocol-for-pac-wpan.ppt

## Slide 14: Simulation Parameter
Scenarios & parameters for discovery phase
  IEEE P802.15-12-0568-05-0008 Tg8 TGD
    Uniform random drop in 500×500 m2 area
    100, 500, 1000, 5000, 10000 PDs
  IEEE P802.15-12-0459-0008 Channel models for TG8
  15-13-0378-00-0008-low-energy-service-discovery-mac-protocol-for-pac-wpan.ppt
Time Parameter
Parameter | Value
Channel Space | 200 [kHz]
Data Rate | 50 [kbps]
Frame Length | 3.6 [msec]
Request Time | 720 [msec]
Response Time | 4 [msec]
Processing Time | 5 [msec]
Random Backoff unit Time | 100[usec]

## Slide 15: Performance metric for discovery
Average number of discovered PDs over the simulation time.
CDF of the discovery latency according to the number of PDs
Average power consumption for discovery[mW/s]
Source : 15-12-0568-05-0008-tg8-technical-guidance-document.docx

## Slide 16: Simulation results for 100 PDs (1)
Average number of discovered PDs for the 5 path loss models

## Slide 17: Simulation results for 100 PDs (2)
CDF of the discovery latency for the 5 path loss models

## Slide 18: Simulation results for 100 PDs (3)
Average power consumption for the 5 path loss models

## Slide 19: Simulation results for 10000 PDs (1)
Average number of discovered PDs for the 5 path loss models

## Slide 20: Simulation results for 10000 PDs (2)
CDF of the discovery latency for the 5 path loss models

## Slide 21: Simulation results for 10000 PDs (3)
Average power consumption for the 5 path loss models

## Slide 22
Thank you.
Q & A