## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Technical Proposal for IEEE 802.15.8]
Date Submitted: [May 6th, 2013]
Source: [Jeongseok Yu, Woongsoo Na, Hyoungchul Bae, Taejin Kim, Yunseong Lee, Juho Lee, Zeynep Vatandas, Sungrae Cho, and Junbeom Hur]
Company [Chung-Ang University, Korea]
E-Mail:[jsyu@uclab.re.kr, wsna@uclab.re.kr, hcbae@uclab.re.kr, tjkim@uclab.re.kr, yslee@uclab.re.kr, jhlee@uclab.re.kr, zvatandas@uclab.re.kr, srcho@cau.ac.kr, jbhur@cau.ac.kr]
Re: [This is the original document]
Abstract: [Technical Proposal for IEEE 802.15.8]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Technical Proposal for IEEE 802.15.8
Jeongseok Yu, Woongsoo Na, Hyoungchul Bae, Taejin Kim, Yunseong Lee, Juho Lee, Zeynep Vatandas, Sungrae Cho, and Junbeom Hur
Chung-Ang University

## Slide 3: Contents (1/2)
Multicast Group Management
  Finding/Joining Multicast Group
  Device Group ID Creation
  Multicast Group Notification Frame (MGNF)
    How to reduce MGNF traffic
    Redundant MGNF Transmission
    UMA-based MGNF Transmission
  Creation and Management of Routing Table
  Leaving Multicast Group
  Mobility Support for Multicast
  Merging Multicast Groups
Multicast/Unicast Routing
  Multicast/Unicast Data Transmission
    Prevention Loopback Problem

## Slide 4: Contents (2/2)
Reliability
  Reliability Support
  Reliable Multicast
Multicast Protocol using Directional Antenna
Energy-Efficient and Fair Peer Discovery
Security Mechanism
  Security Modes
  Security Parameters
  Flow Chart for Authentication
  Infrastructureless Architecture
  Key Derivation
  Authentication
  Authorization
  One-Way Authentication

## Slide 5: Terminologies
Full-Function PD
  A PD which supports whole spec. including routing table.
  Always relay-enabled
Reduced-Function PD
  Relay-enabled: A reduced-function PD which supports routing table for specific multicast group.
  Relay-disabled: A reduced-function PD which does not support routing table.

## Slide 6: Why Multi-hop Multicast?
Group Owner (AP) and Client (Terminal) make
a group
Multiple clients is associated per one group
owner (1:N).
1-to-1 data communication (Group owner and
client)
The data communication between clients is
impossible.
Communication Range is limited 100m
It does not support Multi-hop
GPS or Basestation is not necessary for synchronization
It supports Multi-hop
1-to-1 Data Communication
Low Data Service Rate
Communication Range is limited 10m
It does not support Multi-hop
Compare with FlashLinQ, Bluetooth, and Wi-Fi Direct, PAC has a several merits including multi-hop support.
Bluetooth
Wi-Fi
Direct
PAC
1:1, 1:N, N:N Communication is available.
High Data Service Rate
Communication Range is limited 1km
It supports Multi-hop
Fully Distributed (There is no role for AP or terminal)
Data communication among clients is available
Communication Range is limited 1km
Low energy consumption
It supports Multi-hop
GPS or Basestation is necessary for synchronization
It does not support Multi-hop
FlashLinQ

## Slide 7: Finding/Joining Multicast Group (1/12)
A multicast group consists of two or more PDs with the same application type ID, application specific ID, application specific group ID, and device group ID.
A multicast group can be formed only if two or more PDs can recognize themselves.
Before a PD joins a multicast group, it has to find the multicast group within K-hop coverage.
  If the PD cannot find the group, then it finds the group periodically.
  In order to find a multicast group, a PD broadcasts an Advertisement Command Frame (ACF) after random timer Tj where the maximum TTL is set to K. Range of Tj is [0, Tjmax ].

## Slide 8: Finding/Joining Multicast Group (2/12)
If a PD receive the ACF,
  It stores the ACF in order to forward it to other PDs,
  It saves backward path in the routing table during expiration timer where is calculated by one-hop RTTand K if it is relay-enabled.
    Backward path: originator of the ACF, one-hop PD sending the ACF, Device Group ID & Application type ID & Application-specific ID & Application-specific group ID.
  It compares the receiving frame’s Device Group ID & Application type ID & Application-specific ID & Application-specific group ID with its own.
    If they all are same, it replies an ARCF (Advertisement Reply Command Frame) to the PD sending the ACF (Reply of the ARCF depends upon the MGNF explained in the following slide).
    If any of them is not same, it decrements the TTL of the ACF and forwards the ACF.

## Slide 9: Finding/Joining Multicast Group (3/12)
In order to limit the duplicate ARCF, PDs replying the ARCF multicast a Multicast Group Notification Frame (MGNF) after random time. (MGNF is explained detail in later section)
Then, the PD multicasting the MGNF replies source PD with an ARCF by using backward path.
A PD receiving both ACF and MGNF does not reply an ARCF.
A PD receiving the ARCF whose destination is not itself saves the route information of
      ID of the source PD sending the ARCF, ID of the one-hop PD sending the ARCF, Device Group ID, Application type ID, Application-specific ID, Application-specific group ID.
      Then, this PD is referred to as “FORWARDING PD.”
A PD receiving the ARCF whose destination is itself saves the route information same as FORWARDING PD.
  Then, this PD is referred to as “JOINED MULTICAST GROUP MEMBER.”

## Slide 10: Finding/Joining Multicast Group (4/12)
Assume the following topology.
  There is a multicast group consisting PDs B, D, F, and G.
A
C
E
1-hop
1-hop
1-hop
1-hop
D
F
1-hop
B
1-hop
G
: Candidate PD
: Non-member PD
: Member PD

## Slide 11: Finding/Joining Multicast Group (5/12)
If PD A want to join the multicast group, it broadcasts an ACF (assume K=4 hops).
: Adv Command Frame
A
C
E
D
F
B
G
: Candidate PD
: Non-member PD
: Member PD

## Slide 12: Finding/Joining Multicast Group (6/12)
PD C is not in the multicast group. Therefore, it saves the route information and forwards to the others (e.g., F and E).
PD D already received the ACF and PD F now receives the ACF.
Then, there will be a duplicate ARCF from both of D and F to A.
In order to limit the duplicate ARCF, PD D multicasts a MGNF notifying that D will send an ARCF instead of F.
C
E
: Adv Command Frame
: Candidate PD
: Non-member PD
: Member PD
A
C
E
D
F
: Multicast Group Notification Frame
B
G

## Slide 13: Finding/Joining Multicast Group (7/12)
E forwards the ACF to B and G.
D replies with ARCF to A.
D may send KEKs(key encryption keys) to A after authentication for secure multicast if needed.
D may send rekeying messages to update an existing group key for backward secrecy.
F does not transmit an ARCF to A.
B
A
C
E
: Adv Command Frame
: Adv Reply Command Frame
: Candidate PD
: Non-member PD
: Member PD
D
F
G

## Slide 14: Finding/Joining Multicast Group (8/12)
When PD A receives the ARCF, A joins D’s multicast group.
Also, PD B receives the ACF from PD E.
Then, B multicasts a MGNF to limit a duplicate ARCF from G.
B
A
C
E
: Adv Command Frame
: Adv Reply Command Frame
: Non-member PD
: Member PD
D
F
: Multicast Group Notification Frame
G

## Slide 15: Finding/Joining Multicast Group (9/12)
PD B replies with an ARCF to A through E.
B may send KEKs(key encryption keys) to A after authentication for secure multicast if needed.
B may send rekeying messages to update an existing group key for backward secrecy.
G does not transmit an ARCF to A since the PD G already received the MGNF from B.
A
C
E
D
: Adv Command Frame
: Adv Reply Command Frame
: Non-member PD
: Member PD
F
B
G

## Slide 16: Finding/Joining Multicast Group (10/12)
E forwards the ARCF to PD C.
A
C
E
: Adv Command Frame
: Adv Reply Command Frame
D
F
B
G
: Non-member PD
: Member PD

## Slide 17: Finding/Joining Multicast Group (11/12)
C forwards the ARCF to PD A.
C
E
: Adv Command Frame
: Adv Reply Command Frame
A
D
F
B
G
: Non-member PD
: Member PD

## Slide 18: Finding/Joining Multicast Group (12/12)
PD A is aware of route between PD A and PD B.
Now, PD A joins PD B’s multicast group.
Although group of B and G are not aware of group of D and F currently, multicasting service still works by simply forwarding multicast data frames.
B
C
E
: Adv Command Frame
: Adv Reply Command Frame
A
D
F
G
: Non-member PD
: Member PD

## Slide 19: Device Group ID Creation (1/5)
A multicast group is determined by application type ID, application specific ID, and application specific group ID.
Therefore, it is inefficient if transmitting all IDs in a frame and managing routing table.

## Slide 20: Device Group ID Creation (2/5)
Therefore, we propose a device group ID creation scheme.
  Device group ID should be unique and distributed by a PD sending the first ARCF in the group.
  The PD manages/updates group keys for secure and dynamic multicast group communications after authentication procedures described in security section.
  The PD generates device group ID based on its unicast ID.
  Since a PD’s unicast ID is unique, prefix concatenated by PD’s unicast ID is also unique.
Prefix | Unicast ID

## Slide 21: Device Group ID Creation (3/5)
When two or more multicast groups are merged, the device group ID should be same.
A
D
E
: Merger PD
: Member PD
B
C
: Multicast Group Notification Frame
A recognizes that
two device
group IDs exist
in networks
Group ID: 5
Group ID: 8

## Slide 22: Device Group ID Creation (4/5)
The PD recognizing the existence of two or more multicast groups randomly determines the device group ID for those groups.
A
D
E
: Merger PD
: Member PD
B
C
: Multicast Group Notification Frame
A determines that
device group
ID is 8
Group ID: 5
Group ID: 8

## Slide 23: Device Group ID Creation (5/5)
Then, the PD sends MGNF (notification type = 3 and TTL = ) to the group that does not have the selected group ID to update multicast group ID.
A may send rekeying messages to update an existing group key for backward secrecy.
A
D
E
: Merger PD
: Member PD
B
C
: Multicast Group Notification Frame
A sends
MGNF to D and E
to change
device group ID
Group ID: 5 8
Group ID: 8

## Slide 24: Multicast Group Notification Frame (MGNF) (1/6)
The purposes of MGNF are
  Limiting duplicate ARCF,
  Management of routing table,
  Notifying leaving multicast group,
  Device group ID creation,
  Request for unicast routing,
  Reply for unicast routing,
  Mobility support, and
  Local repair,
  Notification of removed routing entry.
  for relay-enabled PDs.
The MGNF has following eight notification types for above purposes.
0  Limiting duplicate ARCF
1  Management of routing table
2  Notifying leaving multicast
3  Device group ID creation
4  Request for unicast routing
5  Reply for unicast routing
  6  Mobility support
  7  Local repair
  8  Notification of removed routing entry
Notification Type

## Slide 25: Multicast Group Notification Frame (2/6)
Limiting duplicate ARCF (Notification Type=0)
  a PD receiving an ACF multicasts MGNF with notification type set to 0 with random timer Tj. Range of Tj is [0, Tjmax ]
  Although missing MGNF can increase duplicate ARCF, MGNFs are not retransmitted to avoid flooding.
  In this case, payload of MGNF contains source of the ACF.

## Slide 26: Multicast Group Notification Frame (3/6)
Management of routing table (Notification Type=1)
  Assumption: In order to reduce routing entries in the table, each PD maintains entries only for PDs that has exchanged ACFs and ARCFs in its routing table.
  Each PD in multicast group multicasts MGNFs periodically (with notification type set to 1. Range of random timer Tjis [0, Tjmax]
  Upon receiving a MGNF, a forwarding PD updates the entries of the originator of the MGNF and one-hop PD sending the MGNF in its routing table, and forward the MGNF.
  Upon receiving a MGNF, a non-forwarding PD updates the entries of the originator of the MGNF and one-hop PD sending the MGNF in its routing table, but does not forward the MGNF.

## Slide 27: Multicast Group Notification Frame (4/6)
Dst | …
A | …
D | …
E | …
G | …
I | …
Dst | …
A | …
D | …
G | …
I | …
Dst | …
A | …
D | …
E | …
G | …
Dst | …
A | …
D | …
E | …
G | …
I | …
Dst | …
A | …
D | …
E | …
I | …
Dst | …
A | …
D | …
E | …
G | …
I | …
Dst | …
A | …
D | …
E | …
G | …
I | …
Dst | …
A | …
E | …
G | …
I | …
Dst | …
D | …
E | …
G | …
I | …
E
A
B
C
F
G
D
H
I
<If every PD has member
destinations in the table>
Dst | …
A | …
Dst | …
D | …
Dst | …
E | …
Dst | …
G | …
I | …
Dst | …
A | …
D | …
Dst | …
E | …
G | …
Dst | …
E | …
G | …
E
A
B
C
F
G
D
Dst | …
E | …
Dst | …
E | …
I | …
H
I
<Proposed technique can reduce the routing table size>
We assume PDs A, D, E, G, and I are same multicast group.
A  D, E  G, G  I
40
16

## Slide 28: Multicast Group Notification Frame (5/6)
Detection and Routing Table Update for link breakage
  Suppose the link between A and B is broken.
  E does not receive MGNF from A.
  E is aware that the link is broken because A’s MGNF does not arrive before E’s routing table Expiration timer is expired.
  E then removes entry of A from E’s routing table.
E does not
forward MGNF
since E is not a
forwarding PD
Although I does not
update its routing
table for A, I’s multicast
data frame can be
transmitted to group members
E
A
B
C
F
G
D
H
I

## Slide 29: Multicast Group Notification Frame (6/6)
  Device group ID creation
    Explained in the previous section
Notifying leaving multicast group
  Will be explained in later section
Request for unicast routing
  Will be explained in later section
Reply for unicast routing
  Will be explained in later section
Mobility support
  Will be explained in later section
Local repair
  Will be explained in later section
  Notification of removed routing entry
  Will be explained in later section

## Slide 30: Reliable MGNF Transmission
For reliable MGNF transmission, we classify the level of reliable transmission.
  ACK-based MGNF transmission: Notification type = 2, 3, 4, 5, 8 (A source node which transmits a MGNF has to receive ACK frame)
  No ACK-based MGNF transmission: Notification type = 0, 1, 6, 7 (ACK frame is not required Since type 0, 1, 6, 7 MGNF’s role restricts the duplicated procedures, it still work well)

## Slide 31: How to reduce MGNF traffic
When a PD belongs to multiple multicast groups, it multicasts MGNF multiple times.
In order to resolve the above problem, a PD may set Destination Address field of MGNF as United Multicast Address (UMA).
The UMA unifies multiple different groups into a single one.
The UMA can reduce the MGNF traffic as the following slides.

## Slide 32: Redundant MGNF Transmission (1/3)
Suppose A, B, C, and D are in group 2 while B, C, and E are in group 1.
B and C are in both groups 1 and 2 simultaneously.
B starts to multicast its MGNF for Group 1 to C and D (forwarding to E).
After C and D verify device group ID field in PD B’s MGNF, PDs C and D recognize that the MGNF belongs to group 1.
: Multicast Group Notification Frame
Destination Address | Src Address | Originator Address | Notification Type | ……
Group 1 | B | B | 1 | ……
<PD B’s Group 1 MGNF>
: Group1 Member PD
: Group2 Member PD
: Group1 and 2 Member PD
B
D
A
E
C

## Slide 33: Redundant MGNF Transmission (2/3)
Then, D forwards the MGNF from B to E.
After PD E verifies device group ID in B’s MGNF, E recognizes that the MGNF belongs to group 1.
B
D
A
E
: Multicast Group Notification Frame
<PD B’s Group 1 MGNF>
: Group1 Member PD
: Group2 Member PD
: Group1 and 2 Member PD
C
Destination Address | Src Address | Originator Address | Notification Type | ……
Group 1 | D | B | 1 | ……

## Slide 34: Redundant MGNF Transmission (3/3)
B starts to transmit its MGNF for Group 2 to PD A, C, and D.
Then A, C, and D verify their device group ID in PD B’s MGNF, they recognize that the MGNF belongs to group 2.
Total 3 transmissions for MGNF (B transmitted MGNF twice).
: Multicast Group Notification Frame
<PD B’s Group 2 MGNF>
: Group1 Member PD
: Group2 Member PD
: Group1 and 2 Member PD
B
D
A
E
C
Destination Address | Src Address | Originator Address | Notification Type | ……
Group 2 | B | B | 1 | ……

## Slide 35: UMA-based MGNF Transmission (1/3)
B starts to transmit its MGNF whose destination address field set to UMA for Groups 1 and 2 to A, C, and D.
Then A, C, and D verify the device group ID field in PD B’s MGNF, they recognize that the MGNF belongs to UMA.
: Group1 Member PD
: Group2 Member PD
: Group1 and 2 Member PD
B
D
A
E
C
<B’s MGNF>
Destination Address | Src Address | Originator Address | Notification Type | ……
UMA | B | B | 1 | ……
Destination address | … | Device Group ID | …
B | … | 1 | …
B | … | 2 | …
<C’s Routing Table>
<A’s Routing Table>
Destination address | … | Device Group ID | …
B | … | 2 | …
<D’s Routing Table>
Destination address | … | Device Group ID | …
B | … | 2 | …
B | … | 1 | …
E | … | 1 | …

## Slide 36: UMA-based MGNF Transmission (2/3)
If a PD finds
  Received MGNF’s destination address is equal to UMA,
  Two or more device group IDs that have the same value (forwarding PD for that group ID), and
  Those device group ID have the same destination address with the originator of the received MGNF,
  Then, the PD forwards the received MGNF.
: Group1 Member PD
: Group2 Member PD
: Group1 and 2 Member PD
B
D
A
E
C
<B’s MGNF>
Destination Address | Src Address | Originator Address | Notification Type | ……
UMA | B | B | 1 | ……
Destination address | … | Device Group ID | …
B | … | 1 | …
B | … | 2 | …
<C’s Routing Table>
<A’s Routing Table>
Destination address | … | Device Group ID | …
B | … | 2 | …
<D’s Routing Table>
Destination address | … | Device Group ID | …
B | … | 2 | …
B | … | 1 | …
E | … | 1 | …

## Slide 37: UMA-based MGNF Transmission (3/3)
E receives the MGNF from D.
E does not forward the MGNF.
Total 2 transmissions for MGNF (B transmitted MGNF just once).
Although reduction seems to be not much, this can really reduce the MGNF traffic if you have bigger network size.
B
D
A
E
C
<PD B’s MGNF>
Destination Address | Src Address | Originator Address | Notification Type | ……
UMA | B | B | 1 | ……
: Group1 Member PD
: Group2 Member PD
: Group1 and 2 Member PD
<E’s Routing Table>
Destination address | … | Device Group ID | …
B | … | 1 | …

## Slide 38: Creation and Management of Routing Table (1/15)
Whenever a relay-enabled PD receives ACF or ARCF, a routing entry is created in the routing table.
Also, the routing table is updated by receiving MGNF.
A routing table contains
  Destination address
  Next-hop address
  Expiration timer
  Number of hops
  Current_SN
  Device Group ID
  Last ACF reception time()

## Slide 39: Creation and Management of Routing Table (2/15)
B
A
C
E
D
If A wants to join a multicast group, it broadcasts an ACF (assume K=4 hop).
The initial routing table for A is as the following table (Note that originator of ACF has to save the ACF Tx time).
When C receives the ACF, it creates the routing entry of A in its routing table.
PD A’s Routing Table
Device Group ID
Application type ID
...
: Adv Command Frame
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
- | - | - | - | ACF Tx Time | …

## Slide 40: Creation and Management of Routing Table (3/15)
B
A
C
E
D
Since C is not in the multicast group, C forwards the ACF to the others (e.g., D and E).
When D and E receive the ACF, they create the routing entry of A in their routing table.
...
...
PD A’s Routing Table
Device Group ID
Application type ID
Device Group ID
Application type ID
: Adv Command Frame
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
- | - | - | - | ACF Tx Time | …

## Slide 41: Creation and Management of Routing Table (4/15)
B
A
C
E
D
Since D is in the multicast group, D replies A with ARCF by using routing table.
C creates the routing entry of D in its routing table.
Suppose C forwarded an ACF at T0
Suppose C receives an ARCF from D at T1.
Expiration timer of route entry to D in C’s routing table is updated to
At the same time, since E is not in the multicast group, it creates the routing entry of Ain its routing table and forwards to the others (e.g., B).
When B receives the ACF, it creates the routing entry of A in its routing table.
PD A’s Routing Table
: Adv Command Frame
: Adv Reply Command Frame
Destination address : A
Hops : 1
...
Next-hop address : C
...
Device Group ID
Application type ID
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
- | - | - | - | ACF Tx Time | …

## Slide 42: Creation and Management of Routing Table (5/15)
B
A
C
E
D
Since B is in the multicast group, B replies A through E with ARCF.
E creates the routing entry of B in its routing table.
C forwards ARCF from D to A.
A updates a routing entry with expiration timer .
PD A’s Routing Table
Destination address : A
Hops : 2
...
Next-hop address : A
Destination address : A
Hops : 1
...
Next-hop address : E
: Adv Reply Command Frame
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …

## Slide 43: Creation and Management of Routing Table (6/15)
B
A
C
E
D
E forwards the ARCF received from B to C.
C creates the routing entry of B in its routing table.
PD A’s Routing Table
: Adv Reply Command Frame
Destination address : A
Hops : 2
...
Next-hop address : C
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …

## Slide 44: Creation and Management of Routing Table (7/15)
B
A
C
E
D
PD C forwards the ARCF received from E to A.
A creates a routing entry with expiration timer .
PD A’s Routing Table
: Adv Reply Command Frame
Destination address : A
Hops : 3
...
Next-hop address : A
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …
B | C |  | 3 | ACF Tx Time | …
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …
B | C |  | 3 | ACF Tx Time | …

## Slide 45: Creation and Management of Routing Table (8/15)
Finally, A is aware of route to B and D.
PD A’s Routing Table
B
A
C
E
D
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …
B | C |  | 3 | ACF Tx Time | …
Destination address | Next-hop address | Expiration timer | Number of hops | T0 | …
D | C |  | 2 | ACF Tx Time | …
B | C |  | 3 | ACF Tx Time | …

## Slide 46: Creation and Management of Routing Table (9/15)
When a node full of routing table, it chooses a node from its routing table with shortest distance (hop-based) firstly.
It sends a MGNF (Notification type : 8) to the chosen node and sets timer.
When the node receives the MGNF (Notification type : 8), it breaks the link between the node and itself, and sends an ACF.
The node which has timer ignores the ACF and another node which receives ACF, sends ARCF to it and creates a new link between the node which sends ACF and itself.

## Slide 47: Creation and Management of Routing Table (10/15)
When S wants to break the link between B and itself. S transmits MGNF (Notification type : 8) to B and sets a timer.
Destination address | …
A | …
B | 
C | 
D | 
: MGNF (Type 8)
S
C
A
D
B
: ACF
: ARCF
S’s Routing Table
Destination address | …
S | …
A’s Routing Table
Destination address | …
S | …
B’s Routing Table

## Slide 48: Creation and Management of Routing Table (11/15)
When B receives the MGNF (Notification type : 8), it breaks the link between S and B.
C
A
D
B
S
: MGNF (Type 8)
: ACF
: ARCF
Destination address | …
A | …
B | 
C | 
D | 
S’s Routing Table
Destination address | …
S | …
A’s Routing Table
Destination address | …
S | …
B’s Routing Table

## Slide 49: Creation and Management of Routing Table (12/15)
B sends ACF.
S ignores B’s ACF because of PD S’s timer is not expired.
B
: MGNF (Type 8)
: ACF
: ARCF
C
A
D
S
Destination address | …
A | …
C | 
D | 
S’s Routing Table
Destination address | …
S | …
A’s Routing Table
Destination address | …
B’s Routing Table

## Slide 50: Creation and Management of Routing Table (13/15)
A receives the ACF and sends MGNF (type 0) and ARCF to B.
B
: MGNF (Type 8)
: ACF
: ARCF
C
A
D
S
Destination address | …
A | …
C | 
D | 
S’s Routing Table
Destination address | …
S | …
A’s Routing Table
Destination address | …
B’s Routing Table

## Slide 51: Creation and Management of Routing Table (14/15)
Then A and B creates a new link between A and B.
: MGNF (Type 8)
: ACF
: ARCF
D
S
C
Destination address | …
A | …
C | 
D | 
S’s Routing Table
Destination address | …
S | …
B | 
A’s Routing Table
Destination address | …
A | …
B’s Routing Table
A
B

## Slide 52: Creation and Management of Routing Table (15/15)
If MGNF is transmitted periodically, the MGNF (notification type: 1) implosion problem can occurs.
In order to restrict the MGNF implosion problem, we proposed adaptive MGNF transmission technique based on distance.
If the distance between nodes become longer (e.g., a node moves away from the networks), the MGNF transmission period get smaller since the link can be break.
The distance can be measured from received signal strength indicator (RSSI).
  Equations……

## Slide 53: Leaving Multicast Group (1/5)
There are several reasons for a PD to leave from the network: (1) by its intention, (2) by mobility, (3) by limited resources.
If a PD wants to leave from a multicast group, it multicasts (within K-hop) a MGNF with notification type set to 2. A recipient of MGNF may send rekeying messages to valid group members for forward secrecy.
  Upon receiving the MGNF, a forwarding PD deletes the entry of the originator of the MGNF, and forward the MGNF.
  Upon receiving the MGNF, a non-forwarding PD deletes the entry of the originator of the MGNF, but does not forward the MGNF.

## Slide 54: Leaving Multicast Group (2/5)
If PD C wants to leave from a multicast group, it multicasts a MGNF with notification type set to 2.
<PD C’s Routing Table>
Destination Address | ……
D | ……
A
B
C
D
: Multicast Group Notification Frame
<PD A’s Routing Table>
Destination Address | ……
D | ……
<PD D’s Routing Table>
<PD B’s Routing Table>
Destination Address | ……
A | ……
C | ……
Destination Address | ……
A | ……
C | ……
D | ……

## Slide 55: Leaving Multicast Group (3/5)
  B receives the MGNF from C and deletes the entry of the originator of the MGNF, and forward the MGNF.
<PD C’s Routing Table>
Destination Address | ……
D | ……
A
B
C
D
<PD A’s Routing Table>
Destination Address | ……
D | ……
<PD D’s Routing Table>
<PD B’s Routing Table>
Destination Address | ……
A | ……
C | ……
Destination Address | ……
A | ……
C | ……
D | ……
: Multicast Group Notification Frame

## Slide 56: Leaving Multicast Group (4/5)
PD D receives the MGNF and it deletes the entry of the originator of the MGNF.
<PD C’s Routing Table>
Destination Address | ……
D | ……
A
B
C
D
<PD A’s Routing Table>
Destination Address | ……
D | ……
<PD D’s Routing Table>
<PD B’s Routing Table>
Destination Address | ……
A | ……
C | ……
Destination Address | ……
A | ……
D | ……
: Multicast Group Notification Frame

## Slide 57: Leaving Multicast Group (5/5)
Finally, PD C leaves the multicast group.
A
B
C
D
<PD A’s Routing Table>
Destination Address | ……
D | ……
<PD D’s Routing Table>
<PD B’s Routing Table>
Destination Address | ……
A | ……
Destination Address | ……
A | ……
D | ……
: Multicast Group Notification Frame

## Slide 58: Mobility Support for Multicast (1/4)
Previously, B was 2-hop away from A.
If B moves within the one-hop coverage of A, both of A and B are aware of each other within the one-hop by MGNF’s TTL and update their routing table.
Then, A or B sends a MGNF (notification type = 6) to C.
When C receives that MGNF, C is aware that A and B become closer.
  If C is a multicast group member, it does not do anything.
  If C is a forwarding PD, it deletes routing entries whose destination field is A and B.
B
A
A
C
B
Multicast Group Notification Frame
Move

## Slide 59: Mobility Support for Multicast (2/4)
Since expiration timer is proportional to the number of hops from the impaired PD, the closest multicast group member detects link breakage.
A PD starts local repair if it detects link breakage between multicast group members (due to expiration timer).
Then, the PD multicasts MGNF (notification type = 7) .
If PDs receiving the MGNF create routing entry of originator of the MGNF during Tw .
Then the PD performing local repair broadcasts an ACF within K-hop coverage.
Link
Break
PD
Disappear
Link
Break
Local
Repair
Start
Local
Repair
Start
Advertisement Command Frame

## Slide 60: Mobility Support for Multicast (3/4)
If a PD receiving the ACF then It compares the receiving frame’s Device Group ID & Application type ID & Application-specific ID & Application-specific group ID with its own.
  If they all are same, it finds entry the originator of the ACF in its routing table. And it found the entry then check the expiration timer.
  If the expiration timer is less than Tm then replies an ARCF to the PD sending the ACF. (Tm is threshold time to decide reply)
  In other case, the PD receiving the ACF does not reply.
  If any of them is not same, it decrements the TTL of the ACF and forwards the ACF.
Local repair &
merging groups.

## Slide 61: Mobility Support for Multicast (4/4)
Find/join procedure by using ACFs and ARCFs can help merging disjoint groups.
  If a PD in a group receives a ACF from different disjoint group with the same Device Group ID & Application type ID & Application-specific ID & Application-specific group ID, it can initiate merging process.
  The PD then replies to the ACF originator with ARCF.
  Then, these two disjoint groups are merged by Device ID Creation Scheme.
Local repair by using ACFs and ARCFs also can help merging disjoint groups.
  Each group member performs local repair periodically during TL (long duty cycle) in order to merge disjoint groups.

## Slide 62: Multicast Data Transmission(1/6)
If a PD receives a multicast data frame, it has to decide forwarding the frame or not.
The PD receiving the multicast data frame compares the source address of the data frame and next-hop address entries of its routing table.
PD checks the next hop addresses in its routing table. If it finds
  one or more next-hop entries which not overlapped with the source address of the received frame and
  those next-hop entries have same device group ID with the received frame.
  Then, the PD forwards the incoming data frame to other PDs.
Otherwise, the PD do not forward the incoming frame.

## Slide 63: Multicast Data Transmission(2/6)
For the multicast data transmission, we have to know the following information from multicast data frame:
  Destination address
  Source address
  Originator address
  Sequence number
  Time To Live(TTL)
This information should be included in all multicast data frames.
Therefore, the header in multicast data frames should contain the followings.
Destination address | Source address | Originator address | Sequence number | Time To Live(TTL) | Payload

## Slide 64: Multicast Data Transmission(3/6)
We assume that :
  A, B, F, and G are in a same group ID of 1.
  A, D and H are in a same group ID of 2.
  A has routing information of B, D, and G.
  B has routing information of A and F.
  D has routing information of A and H.
B
C
E
D
F
G
Destination address | Next-hop address | … | Device Group ID | Application type ID | Application-specific ID | Application-specific group ID
B | C | … | 1 | 3 | 2 | 5
D | C | … | 5 | 2 | 7 | 5
G | G | … | 1 | 3 | 2 | 5
PD A’s Routing Table
H
A

## Slide 65: Multicast Data Transmission(4/6)
A multicasts data frame to group 1.(Device Group ID: 1, Application type ID: 3, Application-specific ID: 2, Application-specific group ID: 5).
C receiving the data frame compares the source address of the data frame and next-hop address entries in its routing table which has same group IDs from the received data frame.
C finds any routing entry matching with the source address of the received frame and it searches another routing entry that has same multicast group with different next-hop address fields. Since C found, it will forward the data.
B
C
E
Multicast Data Frame
F
G
PD C’s Routing Table
Destination address | Next-hop address | … | Device Group ID | Application type ID | Application-specific ID | Application-specific group ID
A | A | … | 1 | 3 | 2 | 5
B | E | … | 1 | 3 | 2 | 5
D
H
Destination
Address :
Source Address : C
...
C receiving
a data frame
from A
Searching same
multicast group with
different next-hop
address
Originator Address : A
A

## Slide 66: Multicast Data Transmission(5/6)
C forwards the data.
E receiving the data frame checks the condition weather forward or not.
E will forward data frame.
B
C
E
F
G
PD E’s Routing Table
Destination address | Next-hop address | … | Device Group ID | Application type ID | Application-specific ID | Application-specific group ID
A | C | … | 1 | 3 | 2 | 5
B | B | … | 1 | 3 | 2 | 5
F | F | … | 1 | 3 | 2 | 5
D
H
Destination
Address
Source Address : E
...
Originator Address : A
A
E receiving
a data frame
from C
Searching same
multicast group with
different next-hop
address
Searching same
multicast group with
different next-hop
address
Multicast Data Frame

## Slide 67: Multicast Data Transmission(6/6)
E forwards the data.
B and F do not forward the multicast data frame because B and F don’t have next-hop address in their routing table except E.
B
C
E
F
G
D
H
Destination
Address
Source Address : E
...
Destination
Address
Source Address : E
...
Originator Address : A
Originator Address : A
A
PD B’s Routing Table
Destination address | Next-hop address | … | Device Group ID | Application type ID | Application-specific ID | Application-specific group ID
A | E | … | 1 | 3 | 2 | 5
F | E | … | 1 | 3 | 2 | 5
B receiving
a data frame
from C but has not to
forward
Multicast Data Frame

## Slide 68: Unicast Data Transmission(1/5)
When a PD wants to unicast data frame, the PD finds routing entry of destination address in its routing table.
If the PD finds routing entry of destination address, the PD starts to unicast immediately.
If the PD does not find routing entry of destination address, the PD multicasts a MGNF (Notification type : 4) to group.
When the other PD receives the MGNF,
  It saves a backward route information in routing table during Tw
  It starts to find a routing entry of destination address in its routing table
If a PD receiving MGNG finds routing entry of destination address , the PD unicasts a MGNF (Notification type : 5) to the PD which wants to unicast.

## Slide 69: Unicast Data Transmission(2/5)
A wants to unicast to F within same multicast group ID of 1, but A does not have routing information of F in A’s routing table.
Then, A multicasts a MGNF (Notification type : 4) to group 1.
When C receives the MGNF,
  It saves a backward route information in routing table during Tw
  It starts to find a routing entry of F in its routing table.
B
C
E
D
F
G
Destination address | Next-hop address | … | Device Group ID | Application type ID | Application-specific ID | Application-specific group ID
B | C | … | 1 | 3 | 2 | 5
D | C | … | 5 | 2 | 7 | 5
G | G | … | 1 | 3 | 2 | 5
PD A’s Routing Table
H
A
: Multicast Group Notification Frame
A does not have
F’s routing
information
Notification type : 4
Destination Address : F
...
Notification type : 4
Destination Address : F
...

## Slide 70: Unicast Data Transmission(3/5)
Since C did not find the routing entry, C forwards the MGNF.
When E receives the MGNF,
  It saves a backward route information in a routing table during Tw
  It starts to find a routing entry of F in its routing table.
B
C
E
D
F
G
H
A
: Multicast Group Notification Frame
PD E’s Routing Table
Destination address | Next-hop address | … | Device Group ID | Application type ID | Application-specific ID | Application-specific group ID
F | E | … | 1 | 3 | 2 | 5
E has a routing
information
Notification type : 4
Destination Address : F
...

## Slide 71: Unicast Data Transmission(4/5)
: Multicast Group Notification Frame
PD C’s Routing Table
Destination address | Next-hop address | … | Device Group ID | Application type ID | Application-specific ID | Application-specific group ID
F | E | … | 1 | 3 | 2 | 5
Since E finds routing information of F, E unicasts a MGNF (notification type=5) to A.
C creates routing entry of F in its routing table.
B
C
E
D
F
G
H
A
C saves a routing
Information of F
Notification type : 5
Destination Address : A
...

## Slide 72: Unicast Data Transmission(5/5)
C forwards the MGNF to A.
When A receives the MGNF, it creates a routing entry of F in its routing table.
Now, A can unicast data to F.
B
C
E
D
F
H
A
: Multicast Group Notification Frame
Destination address | Next-hop address | … | Device Group ID | Application type ID | Application-specific ID | Application-specific group ID
F | E | … | 1 | 3 | 2 | 5
PD A’s Routing Table
A creates a
routing Information
of F
G
Notification type : 5
Destination Address : A
...

## Slide 73: Prevention Loopback Problem (1/3)
PD prevents multicast/broadcast loopback problem by using SN (Sequence Number) of data frames.
A
C
B
A starts multicast/
broadcast with
K=4 and SN=1
E

## Slide 74: Prevention Loopback Problem (2/3)
When a PD forwards data with SN = n, the PD sets current_SN field in its routing table to n.
A
C
E
B
B sets current _SN=1,
decreases K, and
forwards frame.

## Slide 75: Prevention Loopback Problem (3/3)
If the receiving frame’s SN is not greater than the current_SN , the PD discards the frame.
A
C
B
E
C also sets
current_SN=1,
decreases K, and
forwards frame.
B receives data
with SN = 1 from C,
it discards frame and
does not forward.

## Slide 76: Reliability Support (1/2)
For 1-hop reliable multicast, the role of a transmitting PD is to complete successful transmission of its multicast data frame to its 1-hop multicast members in its routing table.
For multi-hop reliable multicast, the role of a transmitting PD is to complete successful transmission of its multicast data frame to its multicast members in its routing table within K-hop coverage.

## Slide 77: Reliability Support (2/2)
Timeout Mechanism
  To avoid ACK implosion, transmitters send the ACK at random time.
  Randomized timer for ACK transmission to substantially reduce the possibility of contentions.
  If an ACK does not arrive within retransmission timeout, the transmitter retransmits the multicast data frame until R (a maximum retransmit limit) times.
For reliable unicast, the role of a transmitting PD is to complete successful transmission of its unicast data frame to its destination.
Every receiving PD along the route from the source to destination shall send ACK to the transmitter in the unicast routing.
The reliable unicast shall using immediate ACK or n-block ACK mechanism.

## Slide 78: Reliable Multicast (1/11)
We proposed a Block ACK technique for reliable multicast to know whether the nodes receive Multicast Data Frame fully or not.
When sender PD sends Multicast Data Frame, it chooses the groups in the multicast group by depending on the order of the information of the nodes in its routing table.
If the sender wants to have ‘n’ groups, it reached it by dividing the numbers of all nodes in the multicast group to n.
Then, the sender transmits Multicast Data Frame including the information of the group which sends the block ACK.
When the nodes in the group receive all multicast data frames successfully, they transmit Block ACK to the sender by notifying that they received all frames from it.
If they did not receive any data frame or they did not receive it fully, they do not transmit Block ACK to the sender.

## Slide 79: Reliable Multicast (2/11)
Sender PD S chooses the groups with dynamically.
In this example, the number of nodes in a group is 3.
A,B,C are in group1, D,E,F are in group2 and G,H,I are in group3.
PD S transmit multicast data frame F1 included group1’s information.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK

## Slide 80: Reliable Multicast (3/11)
PD A, B, and C transmit Block ACK to S for F1 because these nodes are in group 1.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK

## Slide 81: Reliable Multicast (4/11)
PD S transmit multicast data frame F2 included group2’s information.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK

## Slide 82: Reliable Multicast (5/11)
PD D, E, and F transmit Block ACK for F1, F2 (Frame1, Frame2) to S.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK

## Slide 83: Reliable Multicast (6/11)
PD S transmit multicast data frame F3 included group3’s information.
And PD S requests Block ACK from PD G, H, and I.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK

## Slide 84: Reliable Multicast (7/11)
PD G, H, and I transmit Block ACK for F1, F2, F3 (Frame1, Frame2, Frame3) to S.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK

## Slide 85: Reliable Multicast (8/11)
If PD S does not have any multicast data frame, it sets a timer.
If the timer is expired, it sends Request ACK to the groups.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK
: Request Block ACK

## Slide 86: Reliable Multicast (9/11)
If PD A, B, and C receive the frame F2 and F3, they transmit the ACK to S.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK
: Request Block ACK

## Slide 87: Reliable Multicast (10/11)
Similarly sender PD S transmit the Request Block ACK to PD F, E, and D.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK
: Request Block ACK

## Slide 88: Reliable Multicast (11/11)
If PD D, E, and F receive the frame F3, they transmit the ACK to S.
I
A
S
F
E
D
B
H
C
G
: Multicast Data Frame
: Timer Based Block ACK
: Request Block ACK

## Slide 89: Directional Antenna Support (1/8)
If a PD can support directional antenna, it has to additional routing table field which is describes its beam number forwarding to destination in order to transmit frame.
That routing table contains
  Destination address
  Next-hop address
  Expiration timer
  Number of hops
  Current_SN
  Device Group ID
  Last ACF reception time()
  Beam Number

## Slide 90: Directional Antenna Support (2/8)
If each PD wants to join a multicast group, it performs find/join procedure by using all of beams.
During finding/joining procedure, PDs receiving a ACF check the SNR per beams and saves the specific beam with the highest SNR measured in order to find communication beam.
  If non-multicast group member receives the ACF forwards the ACF by using all of beams.
  If multicast group member receives the ACF, it replies ARCF by using saved specific beam with the highest SNR measured to the originator of the ACF.
When PDs receiving ARCF, it saves the specific beam with the highest SNR measured into its routing table and forwards the ARCF by using backward path.
After updated routing table, all of frames except to broadcast frame can be transmitted directionally.

## Slide 91: Directional Antenna Support (3/8)
1
2
4
This example shows finding/joining multicast group when we employ directional antenna.
If PD A wants to join a multicast group, it broadcasts ACF by using all of beams.
Slide 91
B
A
C
E
: Adv Command Frame
: Candidate PD
: Non-member PD
F
3
D

## Slide 92: Directional Antenna Support (4/8)
1
2
4
3
1
2
3
4
Then PDs D and C receive the ACF.
Since D is a multicast group member, it replies ARCF by using beam 3. Then, A finds the beam with the highest SNR measured and updates its routing table.
C is a non multicast group member then forwards ACF by using all of beams.
Slide 92
B
A
C
E
D
: Candidate PD
: Non-member PD
F
1
2
3
4
: Adv Reply Command Frame
: Adv Command Frame
<PD A’s Routing Table>
Destination Address | Beam Number | ……
D | 1 | ……

## Slide 93: Directional Antenna Support (5/8)
1
2
3
4
1
2
3
4
Since F is a multicast group member, it replies ARCF by using beam 4. Then, C receives ARCF and updates its routing table.
Also, E forwards its ACF by using all of beams.
Slide 93
B
A
C
E
D
: Candidate PD
: Non-member PD
F
1
2
3
4
: Adv Reply Command Frame
: Adv Command Frame

## Slide 94: Directional Antenna Support (6/8)
1
2
3
1
2
3
4
1
2
3
4
When A receives ARCF from C, it updates its routing table.
Also, B replies ARCF by using beam 1. Then, E receives ARCF and updates its routing table.
Slide 94
B
A
C
E
D
: Candidate PD
: Non-member PD
F
1
2
3
4
: Adv Reply Command Frame
: Adv Command Frame
<PD A’s Routing Table>
Destination Address | Beam Number | ……
D | 1 | ……
F | 3 | ……
4

## Slide 95: Directional Antenna Support (7/8)
1
2
3
1
2
3
4
Also, E forwards ARCF by using beam 1. Then, C receives ARCF and updates its routing table.
Slide 95
B
A
C
E
D
: Candidate PD
: Non-member PD
F
1
2
3
4
: Adv Reply Command Frame
: Adv Command Frame
4

## Slide 96: Directional Antenna Support (8/8)
1
2
3
C forwards ARCF by using beam 1.
Then, A receives ARCF and updates its routing table.
Slide 96
B
A
C
E
D
: Candidate PD
: Non-member PD
F
1
2
3
4
: Adv Reply Command Frame
: Adv Command Frame
4
<PD A’s Routing Table>
Destination Address | Beam Number | ……
D | 1 | ……
F | 3 | ……
C | 3 | ……

## Slide 97: MAC Parameters Used in Simulations
Parameter | Value
ACF Frame Size | 32.75 bytes
Application Data Size | 512 bytes
MGNF Size | 48.5 bytes
Data Type | Multicast
Number of Groups | 1
Topology Size | 500m x 500m
PHY | BPSK (1/2)
Simulation Time | 100 seconds
Number of Channels | 1
Tx Power | DCN-0568
Communication Range | 100m
# of Nodes | 500
Data arrival Rate | Full Buffer

## Slide 98: MAC Parameters Used in Simulations
Parameter | Value
Topology | 500m x 500m
Mobility | Static Mobility
Drop | 2-stage Drop
Data Rate | 10Mbps
Multi-hop | Supported
RTS/CTS | Disable
NAV | Disable
ACK/NACK | Enable
CSMA/CA | Exponential increase of CW
Carrier Sensing | Enable
CWmin | 24
CWmax | 210
Retry Limit | 7

## Slide 99: Simulation Results
Goodput (bps/km2): Total number of packets received by all PDs during 1 second, expressed as bits per second per square-meter.
Fairness: Jain’s index for number of packets received by PDs.

## Slide 100: Authentication
Process of verifying ‘who’ is at the other end of the link
Performed for devices (PAC_ADDR)
Achieved by authentication procedure based on the stored authentication key (AUTH_KEY) or by peering (entering a PIN)
Slide 100

## Slide 101: Authorization
Process of deciding if device X is allowed to have access to service Y
Trusted devices (authenticated) are allowed to services
Untrusted or unknown devices may require authorization based on interaction before access to services is granted
Authorization always includes authentication
Technically, key would be derived or given (established) to the authorized user
Slide 101

## Slide 102: Authorization
Device trust levels
Trusted device | The device has been previously authenticated, An AUTH_KEY is stored The device is marked as “trusted” in the device DB
Untrusted device | The device has been previously authenticated An AUTH_KEY is stored But the device is not marked as “trusted” in the device DB
Unknown device | No security information is available for this device This is also an untrusted device
Slide 102

## Slide 103: Security Modes
Security mode 1 (non-secure)
  When a PAC device is in security mode 1, it shall never initiate any security procedure
Slide 103

## Slide 104: Security Modes
Security mode 2 (service level enforced security)
  When a PAC device is in security mode 2, it shall not initiate any security procedure before a channel establishment request has been received or a channel establishment procedure has been initiated by itself
  Whether a security procedure is initiated or not depends on the security requirements of the requested channel or service
  Security mode 1 can be considered as a special case of security mode 2 where no service has registered any security requirements
Slide 104

## Slide 105: Security Modes
Security mode 2 (cont.)
  A PAC device in security mode 2 should classify the security requirements of its services using the following attributes
Authentication required | - Before connecting to the application, the remote device must be authenticated
Authorization required | - Access is only granted automatically to trusted PAC devices, or untrusted devices after an authorization procedure - Always requires authentication to verify that the device is the right one
Encryption required | - The link must be changed to encrypted mode, before access to the service is possible

## Slide 106: Security Modes
Security mode 3 (link level enforced security)
  When a PAC device is in security mode 3, it shall initiate security procedures before the channel is established

## Slide 107: Security Parameters
PAC_ADDR: PAC device address (unique for each device)
AUTH_KEY: used for authentication purposes
ENC_KEY: encryption key (for secure unicast)
GENC_KEY: group encryption key
RAND: frequently changing random or pseudo-random number made by the PAC device itself
Entity | Size
PAC_ADDR | xxx bits
AUTH_KEY | 160 bits
ENC_KEY | 128 bits
GENC_KEY | 128 bits
RAND | 128 bits
Entity | Size
PAC_ADDR | xxx bits
AUTH_KEY | 
ENC_KEY | 
GENC_KEY | 
RAND | 

## Slide 108: Flow Chart for Authentication
Authentication start
Already authenticated
Peering allowed
Peering
Authentication OK
Authentication fail
Link key (AUTH_KEY) available
no
no
no
fail
yes
yes
ok
yes

## Slide 109: Flow Chart for Authorization
Authorization start
Trusted
Create trust
Authorization OK
Authorization fail
Link key (AUTH_KEY) available
no
no
no
fail
yes
yes
yes
Creation of trust allowed?
yes
Authentication succeed?
Slide 109

## Slide 110: Infrastructureless Architecture
No coordinator or AAA (authentication, authorization, accountability) server
Using PIN (symmetric), or certificate (asymmetric) issued by the trusted third party
  Cf) Bluetooth pairing
Slide 110

## Slide 111: Key Derivation
PRF
PRF
PRF
PRF
PIN
PIN
AUTH_KEYAB
AUTH_KEYAB
ENC_KEY
ENC_KEY
Authentication
Encryption
Device A
Device B
During
peering
Slide 111

## Slide 112: Infrastructure Architecture
AAA (authentication, authorization, accountability) server
(Dynamic) Coordinator
  Intermittent connection to the AAA server
Using master key (symmetric) issued by the AAA server, or certificate issued by the AAA server
  Cf) IEEE 802.1x, Kerberos protocol
2G/3G/LTE
AAA server
Server for some services (e.g., advertising)
Authentication &
communication
flow
Communication
flow
coordinator
Slide 112

## Slide 113
PD A
Coordinator B
AS
(Re)association
Association
EAP authentication
EAP Start(Msg Header)
ENC_KEY
Group key delivery
Group key delivery delay
EAP Transfer(EAP Payload)
EAP Transfer(EAP Success)
Access Accept(PMK)
MSK
PMK
AUTH_KEY
SA-ENC-Challenge
SA-ENC-Request
SA-ENC-Response
3-way handshake
MSK, PMK
Key Request
Key Reply(ENC_KEY)
ENC_KEY delivery
AUTH_KEY
ENC_KEY
PMK

## Slide 114: EAP Authentication
Extensible Authentication Protocol (EAP)
  De facto authentication protocol for infrastructure architecture (interact with AAA server)
    IEEE 802.16, 802.11, …
  Fulfill the criteria: mutual authentication, protection against the man-in-the-middle attack
  EAP-PSK, EAP-AKA, EAP-PEAP, …
  Yields the512-bit master secret key (MSK)
    Then the other key encryption keys (KEK) and HMAC/CMAC keys are derived from the MSK
Slide 114

## Slide 115: Authentication Key Generation
PD A and AS derive MSK, and then PMK
PD A and coordinator B derive AUTH_KEY from PMK
Then, PD A and coordinator B derive
  A shared KEK
  HMAC/CMAC key from the AUTH_KEY

## Slide 116: SA-ENC 3-Way Handshake
Provides the following security guarantees:
  Full mutual authentication
  PD A is alive and that A possesses the AUTH_KEY
  Coordinator B is alive
  The coordinator B is guaranteed that SA-ENC-Update is sent by the PD A and is fresh
Slide 116

## Slide 117: ENC_KEY Distribution
After a successful authorization, the PD A dynamically requests parameters for SA(security association) including ENC_KEY
  KEY_Request
  KEY_Reply
Slide 117

## Slide 118: Group Key Distribution
In a network environment where the secure multicast and broadcast service (MBS) is supported, additional group key (GENC_KEY) generation and delivery process is performed optionally after ENC_KEY distribution procedure
Update on every membership change
  Backward security
  Forward security
Slide 118

## Slide 119: Thank you