## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Technical proposal of PAC procedure
Date Submitted: July 7th, 2013
Source: Jinyoung Chun, Suhwook Kim, Han Gyu Cho (LG Electronics)
Address: Seocho R&D Campus, 19, Yangjae-daero 11gil, Seocho-gu, Seoul , Korea
E-Mail: jiny.chun@lge.com
Re: Technical Proposal for PAC Framework Document
Abstract: Technical proposal for PAC Framework Document
Purpose: Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline
Basic conditions
Overview of PAC structure
PAC procedures
  Discovery procedure
  Peering procedure
  Communication procedure
  Operation example
MAC/PHY Design
  Frame structure, etc
Conclusion

## Slide 3: Basic Conditions
IDs for PAC discovery
  Device ID [e.g. 48bits]
    Unique device address (e.g. MAC address)
  Service type ID [e.g. 8bits]
    Discovery according to service type is useful because a PD can discover other PDs with a capability to support the service, not all neighbor PDs.
    e.g. real-time streaming, display, talking, two-way gaming, etc
[Note] ‘Application type’ is useless for discovery because there are lots of service types in it (e.g. data transfer, talking, gaming in SNS). And ‘application specific ID’ may be useful but there are too many IDs now and it will increase in the future. Moreover periodic updates of the IDs are not possible without center control tower/server.
Operation band
  PAC uses unlicensed bands with multiple channels.
    e.g. PAC can use all or parts of channels among 3 channels in 2.4GHz and 8 channels in 5GHz (UNII-1, UNII-3) when bandwidth is 20MHz per channel.
  The fundamental access method of the IEEE802.15.8 PAC is CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance).

## Slide 4: Overall PAC structure
  PD transmits signals for each usage in each region, respectively. The fundamental access method for the signaling is CSMA/CA.
  Discovery region
    It is region for PD to search other neighbour PDs.
    The size is unit(s) of hopping slot. It divides multiple discovery slots.
  Peering region
    It is region for PD to fit its slot sync with discovered PDs and make peering.
    The size is flexible because slot sync can be changed.
  Communication region
    It is region for PD to communicate with peered PDs.
    The size is units of hopping slot. The operating channel is changed by hopping pattern.

## Slide 5: Overall PAC procedure
Overview of PAC procedure
  Discovery procedure
    Active discovery is mandatory.
    When a PD turns on, it starts from discovery region. During communication, discovery region is allocated when it wants to discover others.
    In discovery region, a PD can discover other PDs over all channels by moving the each channel in each discovery slot.
  Peering procedure
    After discovery, the PD goes to the channel in the discovered PDs.
    They make hopping slot timing same and exchange the peering information.
  Communication procedure
    After peering, the PD starts communication with the same hopping slot timing with connected PDs.

## Slide 6: Discovery
What is discovery procedure?
  The procedure that PDs know transmits discovery request and receives discovery response. finds other PD’s device ID.
Discovery region format
  Discovery region
    The size is one or more times of hopping slots.
    It divides multiple discovery slots(e.g. number of channels)
  Discovery slot
    PD moves to the corresponding channel during each discovery slot, and discovers the neighbour PDs in the channel.

## Slide 7: Discovery (Cont’d)
Discovery procedure
  Discovering PD transmits ‘discovery request message’ and waits ‘discovery response message’ in each discovery slot at each channel.
  Discovered PD receiving ‘discovery request message’ transmits ‘discovery response message’ within the discovery slot.
  Discovering PD transmits ACK message right after the response message. (it’s omitted in figure)
  Others
    If discovering PD already has communication links, Discovery region is pre-announced to the already communicated PDs.
    Several PDs can be discovered over several channels. They can make a peering in next peering region or after the region. But they are waiting without re-discovery because they all received ACK messages.

## Slide 8: Discovery (Cont’d)
Information of discovery messages
  Discovery request message
    device ID, service type(s), (offset of the next discovery region1)), etc
  Discovery response message
    Device ID, service type(s)2), slot timing info3), hopping pattern4), etc
offset of the next discovery region: indicate next discovery region for the PDs which receives the request message but can’t transmit the response message within the discovery slot due to e.g. contention
If service type(s) of the responder is same with the requester, the field can be omitted.
slot timing info: time offset to transmit this message(e.g. x in the below figure) when the start timing of a hopping slot is zero, and the index of the current hopping slot(e.g. 0 in the below figure), etc
hopping pattern: the channel information of hopping slots in communication region. The detail is in slide 13.

## Slide 9: Peering
What is peering procedure?
  Make slot-sync & Peering
    PDs make the same hopping slot timing each other.
    PDs exchange their peering information such as hopping pattern, authenticate each other.
Peering region
  The size of the region is flexible because the region includes the time for slot-sync of discovering PD to fit discovered PDs.
  PDs transmits and receives the messages to match hopping slot timing and make a peering.

## Slide 10: Peering (Cont’d)
Peering procedure
  Wait for timing1
    Discovering PD moves to the channel of discovered PD. When the remaining duration of the hopping slot of discovered PD is less than time of 3 messages exchange, discovering PD waits and do peering in the next hopping slot.
  Slot-sync & peering
    Discovering PD transmits ‘Peering request message’ with device ID of discovered PD, which is ‘I want to do peering to you and follow your slot timing’.
    Discovered PD receives the message and check its device ID, and transmits ‘Peering response message’, which is ‘OK’ and peering information.
    Discovering PD transmits ‘Peering confirmation’ message, which is peering information.
  [Note] There is no physical timing procedure. The slot sync is rough timing (e.g. units of milliseconds) by message exchange.
  Wait for timing2
    Discovering PD waits the newly revised slot timing before communication region is started.

## Slide 11: Peering (Cont’d)
Peering message information
  Peering request message
    Sync negotiation: I’ll follow you.
  Peering response message
    Sync negotiation: Ok.
    Peering information: available channels1), status2), authentication information, etc
  Peering confirmation message
    If the sync negotiation is failed, the message isn’t transmitted.
    Peering information: Hopping pattern, slot timing, available channels1), status2), authentication information, etc
  Available channels: channels that the PD can be operated in e.g. when the usage of the channels are divided
  Status: sleep timing, availability check information about the remaining capability for new connection, e.g. the number and channel of already communicated PDs, etc

## Slide 12: Communication
What is communication procedure
  Peered PDs communicates each other when they meet in same channel.
Communication region
  Peered PDs have the same hopping slot timing and moves the channel according to the hopping pattern. When they meet in the same channel, they can communicate each other.
  In the region, hopping pattern is applied repeatedly unless PD transmits the signal to change it or to allocate discovery region.
  During the region, they also can listen discovery request message from other PDs.

## Slide 13: Channel hopping pattern
What is (channel) hopping pattern?
  Channel information of hopping slots in communication region
Why channel hopping is needed?
  PDs have to be operated in whole channels in the well-distributed manner.
  PDs have to support the concurrent communication mode, which a PD has multiple communication links in multiple channels.
The basic rule to make channel hopping pattern
  When a PD turns on or make the first communication link,
    ‘Discovering PD’ follows the hopping pattern of ‘Discovered PD’.
  When a PD make more than a communication link,
    ‘Discovering PD’ changes parts of its hoping pattern to meet ‘Discovered PD’.

## Slide 14: Channel hopping pattern (Cont’d)
Parameters and signaling for hopping pattern
  Pre-determined parameters
    Number of total channels
    Maximum number of channels that a PD communicates concurrently
    The length of hopping pattern
  Signaling information for hopping pattern
    Channel indexes of hopping slots
  Signaling of hopping pattern
    PD can change the hopping pattern when it is in communication region, e.g. channel status is changed. The amount of data communication in each channel is increased/decreased or become zero.
    Then the PD has to announce the changes to already communicated PDs.

## Slide 15: The PAC operation example
PDing transmits ‘Discovery request message’ (Device ID, service type) @ channel 1.
PDed transmits ‘Discovery response message’ (Device ID, service type, slot timing, hopping pattern) and receives ‘ACK message’ @ channel 1.
PDing moves to channel 2 and transmits ‘Peering request message’. (I’ll follow your slot timing).
PDed transmits ‘Peering response message’ (OK, authentication info).
PDing transmits ‘Peering confirmation message’ (hopping pattern, authentication info).
PDing and PDed does the contention-based communication in the hopping slot they meet.

## Slide 16: PAC Frame Structure
  PPDU structure
    Preamble: sequence(s) for time/freq offset, channel estimation, etc
    Physical header: physical information such as bandwidth, PPDU length, etc.
    PSDU
  MPDU structure
    MAC header: data type, MPDU length, MCS, etc
    Frame body: data such as request/response messages
    FCS: 32-bit CRC

## Slide 17: Conclusion
In this slide, we introduce the technical view for PFD.
The specific proposed text is in IEEE 15-13-0395.doc.