## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Processing the work on the new measurement parameters for radio resource management]
Date Submitted: [14 May, 2013]
Source: [Takashi Yamamoto] Company [Sumitomo Electric Industries, Ltd]
Address [1-1-3, Shimaya, Konohana-ku, Osaka, 554-0024 Japan]
Voice:[+81-06-6466-5695], FAX: [+81-06-6462-4586], E-Mail:[yamamoto-takashi@sei.co.jp]
Re: [In response to call for pre-proposals for potential SRU Study Group]
Abstract: [The proceedings to identify new radio resource measurement and management strategies are proposed.]
Purpose: [For the future SG work]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Processing the work on the new measurement parameters for radio resource management
Authors:
Name | Affiliations | Address | Phone | email
Takashi Yamamoto | Sumitomo Electric Industries, Ltd. | 1-1-3, Shimaya, Konohana-ku, Osaka, 554-0024 Japan | +81-06-6466-5695 | yamamoto-takashi@sei.co.jp
Yoshizo Tanaka |  |  |  | yoshizo-tanaka@sei.co.jp
Kenichi Murakami |  |  |  | kenichi-murakami@sei.co.jp
Hirotsugu Yamamoto |  |  |  | hirotsugu-yamamoto@sei.co.jp
Yoji Okada |  |  |  | yoji-okada@sei.co.jp

## Slide 3: Introduction
The LQI (Link Quality Indicator) is one of the measurement parameters specified in IEEE802.15.4, but its definition is vague and imprecise.
Since manufacturers may implement different computation method of the LQI, it is difficult to use for radio resource management system.
  A specific device may obtain more radio resources than other devices.

## Slide 4: Current Definition of the LQI
IEEE802.15.4-2011 8.2.6 Link quality indicator (LQI)
  The LQI measurement is a characterization of the strength and/or quality of a received packet. The measurement may be implemented using receiver ED, a signal-to-noise ratio estimation, or a combination of these methods. The use of the LQI result by the network or application layers is not specified in this standard.
  The LQI measurement shall be performed for each received packet. The minimum and maximum LQI values (0x00 and 0xff) should be associated with the lowest and highest quality compliant signals detectable by the receiver, and LQI values in between should be uniformly distributed between these two limits. At least eight unique values of LQI shall be used.

## Slide 5: How do we proceed?
Identify and evaluate new radio resource management strategies in the following steps.
  Step1: Establish evaluation methodology (e.g. network simulation and experiment).
  Step2: Evaluate radio resource management performance under legacy IEEE802.15.4 measurement features including LQI and ED.
  Step3: Collect proposals for new measurement features and evaluate their performance.
  Step4: Define new measurement procedures that can help improve user experience quantitatively.