## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Enhancing and missing simulation result for PAC operating in synchronous mode(MAC)]
Date Submitted: [ August 25th, 2013 ]
Source: [Soojung Jung ,Seungkwon Cho, Hyungjin Kim, Seokki Kim and Sungcheol Chang]
Company: [ETRI]
Address: [218 Gajeong-ro, Yuseong-gu, 305-700, Republic of Korea]
Fax: [+82-42-861-1966] E-Mail:[sjjung@etri.re.kr]
Re: [In response to the solicitation of submission of “Enhancing and missing simulations” announced in the previous PAC meeting in July.]
Abstract: [This document includes enhancing and missing simulation result for PAC operating in synchronous mode(MAC)]
Purpose: [To provide materials for discussion in 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Contents
Performance of discovery procedure
Performance of data communication
References
  This documents presents simulation results for PAC operating in synchronous mode (DCN:15-13-390-01-008[2])

## Slide 3: Performance of discovery procedure
Terms and concepts
  Status of a PD
    Tx status: a PD is transmitting own discovery signals using a selected discovery Resource Unit(RU)
    Rx status: a PD is receiving other PD’s discovery signal through discovery RUs except own (/selected) discovery RU
    At a specific time (/on a discovery RU), a active PD is either Tx status or Rx status

## Slide 4: Performance of discovery procedure
Terms and concepts(cont.)
  average number of discovered PDs
    Average value of numbers of PDs which is discovered by a PD
  “to discover” latency
    Interval between the time that a PD(in the Rx status )is turned on(/activated) and the time that a PD(in the Rx status) discovers successfully other PD (in the Tx status )

## Slide 5: Performance of discovery procedure
PD deployment
  Number of Total RUs=1024
    Uniform random drop in 500m*500m
      Number of PDs =[100,1000,2000]
  Number of Total RUs=64
    Uniform random drop in 125m*125m
      Number of PDs=[100, 200, 300,400,500]
  All PDs are sequentially activated from time 0. after activated, a PD start to select a discovery RU for transmission of own discovery signal and listen other PD’s signals

## Slide 6: Performance of discovery procedure
Simulation configuration
Parameter | Value
Frame length | UltraFrame (UF)=3.2s, SuferFrame (SF)=200ms, Frame=20ms
Simulation time | 20 UF(64s)
Num. of Total RU | 1024(/64) per UF
Bandwidth | 20MHz
Data rate | 2.67M bps
General parameters | Refer to TGD[1]

## Slide 7: Performance of discovery procedure
Performance Metrics
  Average number of discovered PDs
  Ratio of discovered PDs
    The ratio between the number of successfully discovered PDs and total PDs
  CDF of “ to discovery” latency

## Slide 8: Performance of discovery procedure
Average number of discovered PDs
3 UFs
7 UFs

## Slide 9: Performance of discovery procedure
Ratio of discovered PDs
Over 90%

## Slide 10: Performance of discovery procedure
CDF of latency
3~7 UFs

## Slide 11: References
[1] 15-12-0568-07-0008 , “IEEE 802.15.8 Technical Guide Document(TGD)”
[2] 15-13-0390-01-0008, “A MAC proposal for PAC operating in synchronous mode”