## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposal of Gaussian filter definition for CMB GFSK PHY
Date Submitted: May , 2013
Source:
Kenichi Mori (mori.ken1@jp.panasonic.com), Panasonic; Shinsuke Hara (shinsukehara0122@gmail.com ), QoL-SN; Masahiro Kuroda (marsh@nict.go.jp), QoL-SN&NICT;
Abstract: PSD calculation result of GFSK PHY for 15.4n
Purpose: Clarification of PSD of GFSK Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Abstract
Proposal of the correlation factor of Gaussian Filter used for CMB GFSK PHY - Integration range - Correlation factor

## Slide 3: Background
In the last face-to-face meeting at Geneva, explanation of Gaussian filter definition was added into Draft 0.01.
But integration range parameter (TBD2) and correlation factor(TBD1) are not fixed.
In order for CMB GFSK PHY transmitter to be compliant with this standard, the transmitted pulse p(t) shall have a magnitude of the cross-correlation function | f (t)| whose main lobe is greater than or equal to TBD1, when integrated over a period of at least 2xTBD2 time.
Current document

## Slide 4: Calculation condition
Gaussian filter parameter | Value
BT | 0.7
Filter length (symbol duration) | 100
Over sampling number | 200
Reference Gaussian filter
Evaluation Gaussian filter (Digital filter)
Gaussian filter parameter | Value
BT | 0.7
Filter length (symbol duration) | variable
Over sampling number per symbol | variable
Bit width of tap coefficients | variable
Under the above calculation condition, preferable integration and correlation factor are estimated using the next equation.

## Slide 5: Calculation result 1
Around 99.99% energy of Gaussian wave form is concentrated into -0.5 – 0.5 range in time domain. Note: time is normalized by symbol duration
Integration range -0.5 – 0.5 should be enough to determine Gaussian filter accuracy.
Proposal TBD2 value = 0.5

## Slide 6: Calculation result 2
As one of the worst cases, the following parameter set was calculated
Gaussian filter parameter | Value
BT | 0.7
Filter length (symbol duration) | 1
Over sampling number per symbol | 4
Bit width of tap coefficients | 4
Although this condition is not so accurate, the correlation factor with the reference Gaussian filter is more than 0.96.
Hence proposal TBD1 value (correlation factor) is 0.96.
Example of evaluation Gaussian filter

## Slide 7: Summary
In order for CMB GFSK PHY transmitter to be compliant with this standard, the transmitted pulse p(t) shall have a magnitude of the cross-correlation function | f (τ)| whose main lobe is greater than or equal to TBD1, when integrated over a period of at least 2xTBD2 time.
Current document
Proposal TBD1 and 2 values
TBD1: 0.96
TBD2: 0.5