## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Consideration on multi-channel operation
Date Submitted: September, 10th, 2013
Source: Jinyoung Chun, Suhwook Kim, Han Gyu Cho (LG Electronics)
Address: LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea
Voice: +82-31-450-1901, FAX: +82-31-450-4049, E-Mail: jiny.chun@lge.com
Re:
Abstract:
Purpose: Proposal for discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Contents
Channelization in unlicensed band.
  Channelization of Bluetooth
  Channelization of Wi-Fi
  Suggestion for PAC
Multi-channel operation of PAC

## Slide 3: Channelization of unlicensed band
Bluetooth
  It operates in the 2.4GHz ISM band.
  Operating frequency bands are as below.
  Guard bands are as below.
  Channel hopping without carrier sensing in unit of 625us.
Regulatory range | RF channels
2.400-2.4835 GHz | F=2402 + k MHz, k=0,..,78
Lower guard band | Upper guard band
1.5 MHz | 3 MHz

## Slide 4: Channelization of unlicensed band
  Wi-Fi in 2.4GHz
  IEEE 11b/g/n operates in 2.4GHz ISM band. The operation range is from 2.400 to 2.4835 GHz. It can be a little different by country.
  Operating frequency bands are 20/40MHz.
  Channelization of 20MHz OFDM is as below.

## Slide 5: Channelization of unlicensed band
  Wi-Fi in 5GHz
  IEEE802.11n/ac operates in 5GHz unlicensed band. The operation range is from 5.15 to 5.35GHz and from 5.47 to 5.850GHz. It can be a little different by country.
  Operating frequency bands are 20/40/80/160MHz.
  Channelization is as below.
    UNII-1 (5150 - 5250MHz): Indoor use only.
    UNII-2 (5250 - 5350MHz, 5470-5725MHz): Indoor and outdoor use permitted. DFS/TPC required.
    UNII-3 (5725 - 5825MHz): Fixed Service operations only. DFS/TPC required.
  D2D system can use only UNII-1 band by the current regulation.
Available channels for 11n
New available channels for 11ac

## Slide 6: Channelization of unlicensed band
Suggestion for PAC
  Add the detail channelization for PAC in PFD as below.
  Proposal
    PAC devices operate in 2.4GHz and 5GHz unlicensed band. The operation range is from 2.4 to 2.4835 GHz and from 5.15 to 5.25GHz.
    Operating frequency band is 20MHz bandwidth(TBD).
    PAC follows the channelization as IEEE802.11 as below because of maintaining the coexistence and minimizing inter-channel interference with 802.11devices.
Regulatory range | RF channels
2.400-2.4835 GHz | F=2412 + k*25 MHz, k=0,1,2
5.15-5.25 GHz | F= 5180 + k*20 MHz, k=0,1,2,3

## Slide 7: Multi-channel operation
Operation range of PAC
  There are over 80MHz operation range in 2.4GHz and 5GHz unlicensed band, respectively. If PAC operates with 20MHz bandwidth, PAC has over 8 channels.
  Therefore PAC shall use the multi channels efficiently. And PDs shall communicate with PDs in other channels. We call it ‘multi-channel operation.’
Multi-channel operation
  A PD shall be able to communicate with PDs which is communicating in multi channels concurrently.
    E.g. PD ‘A’ in channel 1 shall discover PD ‘B’ in channel 2, while PD ‘A’ and ‘B’ are communicating in each channel, respectively.
  In AP mode, APs can handle multi-channel operation . But in D2D mode, there is no efficient operation scheme yet. PAC must solve the problem.

## Slide 8: Multi-channel operation
Suggestion for PAC
  All proposals should include multi-channel operation how to operate in multi channels and how to make connection with other PDs in other channels, etc.
  LG’s case: channel hopping [1], [2]
< A simple example of channel hopping for multi-channel operation >

## Slide 9: Conclusion
Proposal for the progress of PFD
  Add the detail channelization for PAC in PFD
  All proposals should include multi-channel operation how to operate in multi channels and how to make connection with other PDs in other channel, etc

## Slide 10: Reference
[1] 15-13-0280-00-0008, Technical proposal for PAC
[2] 15-13-0394-00-0008, Technical proposal for PFD