## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Summary of E-mail discussion on PAC technical issues
Date Submitted: Sept 15, 2013
Source: 802.15.8 Technical Editors: Byung-Jae Kwak (ETRI), Seung-Hoon Park (Samsung)
Company:
Address:
Voice: Fax: E-Mail: bjkwak@etri.re.kr, shannon.park@samsung.com
Re:
Abstract: This document summarizes the e-mail discussion on PAC technical issues.
Purpose: Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: E-mail Threads
“[Discussion] Key Technical Issues relevant to PAC Framework Document”
“Suggestion on key issues regarding discovery”
“Suggested Key Technical Issues relevant to PHY design”

## Slide 3: Thread I (1/4)
Subject: “[Discussion] Key Technical Issues relevant to PAC Framework Document”
Aug. 19 ~ Sept. 12, 11 e-mails
Seung-Hoon triggered a discussion to address missing issues in the proposal compared to the framework document (0328)
Basically,
  proposed a template for discussion of technical issues and comments;
  started a discussion of synchronization

## Slide 4: Thread I (2/4)
Summary of discussion
  Seung-Hoon categorized proposals into three groups:
    Centralized: NICT, ETRI (SS Joo), InterDigital
    Distributed: Samsung, ETRI (SC Chang)
    No network synchronization: LG
  Suhwook’s categorization
    Pre-sync system (sync before discovery/peering): Samsung, ETRI (SC Chang)
    Post-sync system: NICT, ETRI (SS Joo, BJ Kwak, WC Jeong), LG

## Slide 5: Thread I (3/4)
Summary of discussion (continued)
  Jinyoung’s categorization
    Synchronization before discovery
      Centralized synchronization (group 1): InterDigital, NICT
      Distributed synchronization (group 2): Samsung, ETRI (SC Chang)
    Discovery without synchronization: LG, ETRI (SS Joo, BJ Kwak, WC Jeong)
  Marco’s comment on NICT proposal
    “NICT’s proposal is a combination of contention and contention-free access, but it does not require a global synchronization mechanism.”
    “NICT proposal is not centralized and timing reference does not depend on one PD.”  Jinyoung: “I think your proposal is centralized sync because PDs in a group share a procedure timing […] by receiving the Beacon from initiator.”

## Slide 6: Thread I (4/4)
Summary of discussion (continued)
  Seung-Hoon’s clarification of the definition of “synchronization”
    Link-level synchronization
      Time (or frequency) synchronization between two devices
      Related to preamble or pilot design
    System-level synchronization
      Time (or frequency) synchronization among multiple devices in a system
      For example, related to beacon operation to indicated system timing
      Can be global or local

## Slide 7: Definition of Network Synchronization (Monday PM1)
Definition of Network Synchronization
  Time synchronization among multiple PDs in PAC network
    To have same reference timing to align slot boundary
Centralized Network Synchronization
  MasterSlaves
  Time reference is decided based on the single PD
  Master role can be changed to satisfy distributed coordination feature of PAC
Distributed Network Synchronization
  PeersPeers
  Time reference is decided based on the multiple PDs

## Slide 8: Discussion on Network Synchronization (Monday PM1)
Definition
  Time synchronization among multiple PDs in PAC network
    To have same reference timing to align slot boundary
Synchronization before discovery
  Centralized synchronization (group 1): Qing(InterDigital), SS Joo(ETRI))
  Distributed synchronization (group 2): Samsung, ETRI (SC Chang), Qing(InterDigital), BJ Kwak(ETRI, can tolerate lack of sync)
  Hybrid : Qing(InterDigital), H.B. (NICT), SS Joo(ETRI)
Discovery without synchronization: WC Jeong(ETRI)
  Synchronization for communication : LG
  No synchronization for communication
Adaptive Synchronization
  BJ Kwak(ETRI) : discovery without synch. in coarse situation, synchronization before discovery in dense situation.

## Slide 9
Application-specific network management (Qing, SS Joo(ETRI))
  Synchronization
    Intra app-group synchronization
    Inter app-group synchronization

## Slide 10: Thread II (1/4)
  Subject: “Suggestion on key issues regarding discovery”
  Sept. 12 ~ Sept. 13, 2 e-mails
  A discussion on “discovery” initiated by Seungkwon Cho
Seungkwon Cho’s discussion
  Where does the discovery occur?
    In-band discovery: discovery and data use the same time-frequency resource
    Out-of-band discovery: discovery uses dedicated time-frequency resource

## Slide 11: Thread II (2/4)
Seungkwon Cho’s discussion (continued)
  How does the discovery information flow?
    Unidirectional discovery:
        Discoverer listens to discovery information transmitted by discoveree
        When the discovery procedure is over only the discoverer has discovery information of the discoveree.
        Ex: passive scan by non-AP station in Wi-Fi
    Mutual discovery:
        Two unidirectional discoveries. No interactive communication.
        When the discovery procedure is over, the PD that is trying to establish a link as well as the other PD may have discovery information of each other.
    Interactive discovery
        There are exchanges of discovery information between discoverer and discoveree.
        Ex: active scan by non-AP station in Wi-Fi

## Slide 12: Thread II (3/4)
Seungkwon Cho’s discussion (continued)
  How to use IDs defined in TGD in order to build discovery message?
    Lower priority than the above two issues
    TGD states “it is up to the proposers,” and should be addressed

## Slide 13: Thread II (4/4)
Marco’s comment
  “[T]he proposals for discovery have resources for communication and discovery separate. Thus, the case of in-band discovery does not occur.” (Editor: What about LG’s proposal?)
Editor’s comment
  Alternative approach: broadcast based discovery vs. query based discovery

## Slide 14: Thread III (1/3)
Subject: “Suggested Key Technical Issues relevant to PHY design”
Sept. 12 ~ Sept. 13, 2 e-mails
Initiated by Seung-Hoon Park, various PHY issues
PHY Issues
  Duplex
    Candidates: TDD
    Discussion: FDD is logically impossible
  Multiplex
    Wide-band system: OFDM, DFT-spread FDM (SC-FDM)
    Narrow-band system: TDM (for single carrier)

## Slide 15: Thread III (2/3)
PHY Issues (continued)
  Multiple access: TDMA, FDMA
  Channelization
    LG submitted a slides to be presented Nanjing meeting
    Discussion: there is a tradeoff between the number of channels and discovery performance (discovery latency, power consumption, etc)

## Slide 16: Thread III (3/3)
Marco’s comment
  “Multiplex and multiple access are the same thing”
  “The proposals so far are OFDMA and SC-FDMA for wideband and narrowband systems. There is not multiple access for FSK based PHYs so far.”
  “NICT PHY proposal has a comprehensive channelization for unlicensed bands.”