## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Comment resolution for CID 133
Date Submitted: September, 2013
Source: Youngae Jeon, Sangjae Lee, Jaehwan Kim, and Sangsung Choi (ETRI), Soo-Young Chang (SYCA)
Contact: yajeon@etri.re.kr
Voice: +82 42 860 6497, E-Mail: yajeon@etri.re.kr
Re: [802.15 TG4m]
Abstract: This document provides proposed resolution for CID 133 of Sponsor Ballot
Purpose: To provides proposed resolutions for CID 133
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Page | Sub- clause | Line # | Comment | Proposed Change
17 | 5.1.14.1 | 44 | There is not the deallocation procedure about the DBS and the dedicated channel in 5.1.14.1. | Add the deallocation procedure about the DBS and the dedicated channel in 5.1.14.1.

## Slide 3
Change the 10th paragraph of 5.1.14.1 on page 14, line 34.
  In Step B, the SPC transmits an enhanced beacon containing a TMCTP Extended Superframe Specification IE as described in 5.2.4.35. Upon successful reception of the beacon from the SPC, the TMCTP-child PAN coordinator may request a DBS allocation or a DBS deallocation by sending a DBS request frame, as described in 5.3.14, to the SPC. Upon receiving the DBS request frame, the SPC will allocate or deallocate a DBS slot and channel, and generate a DBS response frame, as described in 5.3.15, to report the slot and channel allocated or deallocated. The SPC can generate the DBS response frame for the deallocation without the request of the TMCTP-child PAN coordinator.
CID | Category | Page | Sub-clause | Line # | Comment State
133 | T | 17 | 5.1.14.1 | 44 | A

## Slide 4
Change the 3th paragraph of 5.1.14.1 on page 15, line 53.
  In Step B, the TMCTP-parent PAN coordinator sends an enhanced beacon containing a TMCTP Specification IE, as in 5.2.4.35. Upon successful reception of the beacon from the TMCTP-parent PAN coordinator, the TMCTP-child PAN coordinator requests a channel and a slot by using the DBS request sent to the TMCTP-parent PAN coordinator. Upon receiving the DBS request, the TMCTP-parent PAN coordinator directly generates the DBS response frame reporting the slot and channel allocated or deallocated, or it sends the DBS request command frame to the SPC and then receives the DBS response command frame from the SPC. The TMCTP-parent PAN coordinator can generate the DBS response frame for the deallocation without a request of the TMCTP-child PAN coordinator.
CID | Category | Page | Sub-clause | Line # | Comment State
133 | T | 17 | 5.1.14.1 | 44 | A

## Slide 5
Change the 4th paragraph of 5.3.15.2 on page 36, line 10.
  The Allocated DBS Length field shall contain the length of the allocated DBS. If the Allocated DBS Length field is equal to zero, it indicates that the DBS slot and the dedicated channel are deallocated.
CID | Category | Page | Sub-clause | Line # | Comment State
133 | T | 17 | 5.1.14.1 | 44 | A