## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed OFDM PHY comment resolutions for TG4m Sponsor Ballot
Date Submitted: September 16, 2013
Source: Soo-Young Chang (SYCA), Cheolho Shin (ETRI), Byounghak Kim (ETRI), Sangsung Choi (ETRI)
Contact: sychang@ecs.csus.edu
Voice: +1-530-574-2741 E-Mail: sychang@ecs.csus.edu
Re: [802.15 TG4m]
Abstract: This document provides proposed OFDM resolutions for TG4m Sponsor Ballot.
Purpose: To provides proposed resolutions for OFDM PHY related comments from TG4m sponsor ballot.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comments regarding OFDM PHY
CID 297
CID 298
CID 299
CID 300
CID 301
CID 303
CID 307
CID 313
CID 317
CID 388

## Slide 3: Proposed resolution of CID 297 (1)
Related subclause
  Subclause 20.2 page 67 line 1
Comment
  Previous versions and amendments of the 802.15.4 standard include already well defined OFDM modes. Why is there a need for a different OFDM mode definition? It will make more difficult the adoption of the standard having different implementations, where a common implementation would have been possible.
Proposed change from commenter
  The Working Group must explain in the text the technical reasons for a different OFDM scheme to be selected for this amendment.

## Slide 4: Proposed resolution of CID 297 (2)
Proposed resolution
  Accept in principle.
  For TVWS OFDM PHY, considering better radiation propagation characteristics of TVWS signals, transmitter specifications can be simplified to have an appropriate structure which fits better for command and control applications by reducing the number of OFDM symbols for the better packet structure.
  Add a paragraph at the beginning of Clause, 20 on Page 69,
  “One of key considerations for a new setting of parameters for TVWS PHYs is how to optimize the parameters to allow 802.15.4 wireless networks to take advantage of the TV white space spectrum for use in large scale device command and control applications. The parameters for three PHYs are identified for TVWS services in this standard, considering this optimization.”

## Slide 5: Proposed resolution of CID 298 (1)
Related subclause
  Subclause 20.2.1.1.2 page 69 line 11
Comment
  Definition for STF_freq is missing.
Proposed change from commenter
  State that STF_freq is given in Table 203.

## Slide 6: Proposed resolution of CID 298 (2)
Proposed resolution
  Accepted.
  Add a statement, “where STF_freq is given in Table 203.” in Line 12 of Page 69.

## Slide 7: Proposed resolution of CID 299 (1)
Related subclause
  Subclause 20.2.1.1.2 page 69 line 54
Comment
  Definition for LTF_freq is missing.
Proposed change from commenter
  State that LTF_freq is given in Table 204.

## Slide 8: Proposed resolution of CID 299 (2)
Proposed resolution
  Accepted.
  Add a statement, “where LTF_freq is given in Table 204.” below Line 54 of Page 69.

## Slide 9: Proposed resolution of CID 300 (1)
Related subclause
  Subclause 20.2.1.3 page 72 line 6
Comment
  Need to clarify the procedure of the HCS calculation by adding some steps of the procedure.
Proposed change from commenter
  Refer to the document to be submitted (15-14-0505-00).

## Slide 10: Proposed resolution of CID 300 (2)
Proposed resolution
  Accepted
  Add a paragraph to Page 72 as explained in doc. 15-13-0505-00.

## Slide 11: Proposed resolution of CID 301 (1)
Related subclause
  Subclause 20.2.3.3 page 75 line 29
Comment
  Order of coded bits in a coded symbol is unspecified.
Proposed change from commenter
  State that the first coded bit is Output Data A and the second coded bit is Output Data B.

## Slide 12: Proposed resolution of CID 301 (2)
Proposed resolution
  Accepted
  Add a sentence, “The first coded bit is Output Data A and the second coded bit is Output Data B.” at the end of Subclause 20.2.3.3. on Page 75.

## Slide 13: Proposed resolution of CID 303 (1)
Related subclause
  Subclause 20.2.3.4 page 75 line 43
Comment
  The structure of the interleaver is not clear, the process of interleaving should be illustrated.
Proposed change from commenter
  Insert a figure to show the corresponding process of interleaving.

## Slide 14: Proposed resolution of CID 303 (2)
Proposed resolution
  Accepted
  Add a figure on Page 75 as explained in doc 15-13-0515-00.

## Slide 15: Proposed resolution of CID 307 (1)
Related subclause
  Subclause 20.2.3.5 page 76 line 50
Comment
  Manner in which data symbols are mapped to data carriers is left unspecified..
Proposed change from commentor
  State that the first output symbol is mapped to the most negative data carrier index, etc.

## Slide 16: Proposed resolution of CID 307 (2)
Proposed resolution
  Accepted.
  Add a sentence, “The first output symbol is mapped to the most negative data carrier index in data tones and the second output symbol is mapped to the second most negative data carrier index in data tones and so on.” before the sentence in Line 49 of Page 76.

## Slide 17: Proposed resolution of CID 313 (1)
Related subclause
  Subclause 20.2.3.9 page 77 line 53
Comment
  Need to correct the figure number referenced.
Proposed change from commenter
  Change "PHR, as shown in Figure 102" to "PHR, as shown in Figure 176".

## Slide 18: Proposed resolution of CID 313 (2)
Proposed resolution
  Accepted.
  Change as suggested by commenter.

## Slide 19: Proposed resolution of CID 317 (1)
Related subclause
  Subclause 20.2.4.7 page 79 line 51
Comment
  The subscript f of Nf is lower case in the formula, where as in the description it is in upper case.
Proposed change from commenter
  It can be made to NF in the formula, F in the subscript

## Slide 20: Proposed resolution of CID 317 (2)
Proposed resolution
  Accepted.
  Change two “Nf”s to “NF” in the formula in Line 38 of Page 79 as suggested by the commenter and additionally one “Nf” to “NF” in Line 6 of Page 80.

## Slide 21: Proposed resolution of CID 388 (1)
Related subclause
  Annex U page 119 line 1
Comment
  Show the example encoding a packet for the TVWS-OFDM PHY to avoid ambiguity.
Proposed change from commenter
  Insert the Annex U for the example encoding a packet for the TVWS-OFDM PHY.

## Slide 22: Proposed resolution of CID 388 (2)
Proposed resolution
  Accepted.
  Add an annex U as suggested by the commenter. (Refer to doc. 15-13-0287-00.)