## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposal of Eye Diagram for CMB GFSK PHY
Date Submitted: May , 2013
Source:
Kenichi Mori (mori.ken1@jp.panasonic.com), Panasonic; Shinsuke Hara (shinsukehara0122@gmail.com ), QoL-SN; Masahiro Kuroda (marsh@nict.go.jp), QoL-SN&NICT;
Abstract: PSD calculation result of GFSK PHY for 15.4n
Purpose: Clarification of PSD of GFSK Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Abstract
Proposal of Eye diagram for CMB GFSK PHY - Frequency deviation tolerance - Zero crossing tolerance
TBD1%
TBD2%
TBD3% Ts
-TBD3% Ts
TBD2%
TBD1%

## Slide 3: Background
The latest specification draft has TBD values for frequency deviation tolerance and zero crossing tolerance as shown the next. 21.2.2.5 Frequency deviation tolerance Modulation frequency tolerance is measured as a percentage of the frequency deviation, fdev, dictated by the modulation index. In the case of filtered 2FSK, the measured frequency deviation, f, at Ts / 2 shall be constrained to the range TBD% fdev < |f| < TBD% fdev, as shown in Figure 21.24, where Ts is the symbol time. 21.2.2.6 Zero crossing tolerance In the case of filtered 2FSK, the excursions for the zero crossings for all trajectories of the eye diagram shall be constrained to within ±TBD% of the symbol time Ts, as shown in Figure 21.24. => Need to fix these values

## Slide 4: Parameters Influence Eye Diagram
Example parameters influence eye diagram are
PLL Synthesizer
VCO Phase noise
Charge pump noise
Delta-Sigma circuit noise (in case of fractional synthesizer)
PLL loop filter characteristics
etc.
Others
Parts to parts variation
Voltage variation
Temperature variation
etc.
These parameters are determined considering target data rate, usage environment and so on.
Target data rate, up to 200kbps, is similar to 15.4g.
How about temperature?

## Slide 5: Usage condition of CMB devices
One of the main applications of IEEE802.15.4g is a smart meter which may be used outdoor condition. Hence -45 - +85 operation temperature range is considered in devices compliant with IEEE802.15.4g.
Target applications of CMB are as below. (see DCN 15-12-539r0)
Hospital and Clinics
  Medical Instruments continuous monitoring
  Medical instrument management in hospital
  (See next slide for examples, etc)
  Therapy management
Home
  Medical Data collection and download
  Exercising and sport equipment data
  Senior movement detection and location tracking
Some data collector devices may be placed in outdoor as the worst case. Hence, it is better to reuse the eye diagram adopted by IEEE802.15.4g to support those possible worst condition.

## Slide 6: Eye diagram proposal
・same as the IEEE802.15.4g eye diagram

## Slide 7: Conclusion
21.2.2.5 Frequency deviation tolerance Modulation frequency tolerance is measured as a percentage of the frequency deviation, fdev, dictated by the modulation index. In the case of filtered 2FSK, the measured frequency deviation, f, at Ts / 2 shall be constrained to the range 70% fdev < |f| < 130% fdev, as shown in Figure 21.24, where Ts is the symbol time. 21.2.2.6 Zero crossing tolerance In the case of filtered 2FSK, the excursions for the zero crossings for all trajectories of the eye diagram shall be constrained to within ±12.5% of the symbol time Ts, as shown in Figure 21.24.