## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks(WPANs)
Submission Title: Proposed comment resolutions for CIDs 21, 153 and 155
Date Submitted: Nov. 2013
Source: Soo-Young Chang (SYCA) and Cheol-ho Shin (ETRI)
Contact: sychang@ecs.csus.edu
Voice: +1 530 574 2741, E-Mail: sychang@ecs.csus.edu
Re:
Abstract: This document provides proposed resolution for CIDs 21, 153 and 155 of TG4m SB Recirculation Ballot 1
Purpose: Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: CID 21
Related Subclause
  5.1.1.3, Page 12 Line 9
Comment
  The updated Figure 10 shows an incorrect IFS following the ACK of a Short frame. Instead of LIFS, it should be max(SIFS, aTurnaroundTime).
Proposed Change
  Fix as suggested.
Proposed Resolution
  Accept
  Modify the figure as suggested in the comment.

## Slide 3: CID 153
Related Subclause
  20.2.3.9, Page 80 Line 46
Comment
  Need to clarify the scrambling procedure by adding a sentence.
Proposed Change
  Add two sentences, "The PN9 generator is clocked using the seed as the starting point and enabled after the first clock cycle. The PN9 generator shall be reinitialized to the seed after each packet (either transmit or receive)." at the end of the paragraph.
Proposed Resolution
  Accept
  Modify the clause as suggested in the proposed change.

## Slide 4: CID 155
Related Subclause
  20.2.4.7, Page 82 Line 32
Comment
  Equation is in error, appears to be cut-and-paste of corresponding equation for NB-OFDM. The "384" is incorrect for this PHY, it should be the number of data tones, which is 100 for this PHY. Also need editorial fix in the equation so the top line of the "square root" sign shows up properly.
Proposed Change
  Fix as suggested.
Proposed Resolution
  Accept
  Modify the clause as suggested in the comment.