## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks(WPANs)
Submission Title: Proposed comment resolutions for CIDs 150, 152, 154 and 166
Date Submitted: Nov. 2013
Source: Soo-Young Chang (SYCA), Cristina Seibert (Silver Spring Networks) and Cheol-ho Shin (ETRI)
Contact: sychang@ecs.csus.edu
Voice: +1 530 574 2741, E-Mail: sychang@ecs.csus.edu
Re:
Abstract: This document provides proposed resolution for CIDs 150, 152, 154 and 166 of TG4m SB Recirculation Ballot 1
Purpose: Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: CID 150
Related Subclause
  20.2.1, Page 68 Line 17
Comment
  In Figure 173, a variable number (1-4) of STF symbols is not acceptable, because the receiver synchronization must have prior knowledge of the preamble length to adjust its synchronization procedures. The minimum value of 1 symbol is NOT sufficient to settle AGC and perform timing and frequency synchronization.
Proposed Change
  Change length of STF to 4 symbols.

## Slide 3: CID 150 (cont’d)
Proposed Resolution
  Out of Scope
  The commentor does not provide any data to justify why a change to the draft would be needed. One OFDM symbol shows 10 STF correlation repetitions. It should be enough to perform synchronization. Refer to 15-12-0641-00.

## Slide 4: CID 152
Related Subclause
  20.2.2, Page 73 Line 45
Comment
  Table 205: To fulfill the target of data rates ranging up to 2 Mb/s the mandatory should be extended to MCS3, 16-QAM + rate 3/4 FEC, which allows 2343.75kb/s.
Proposed Change
  Add Mode MCS3 as 16-QAM+ rate 3/4 FEC. Shift the optional modes to MCS4, MCS5, MCS6 and MCS7 respectively (BPSK,rate1/2; QPSK,rate1/2;16-QAM,rate1/2;16QAM,rate3/4) .

## Slide 5: CID 152 (cont’d)
Proposed Resolution
  Out of Scope
  The draft already includes modes that support higher data rates as identified by the commenter. There is no need to consider a new FEC mode as suggested by the commenter. While the PAR refers to such data rates, it does not mandate they be supported. The comment is deemed out of scope for this recirculation ballot.

## Slide 6: CID 154
Related Subclause
  20.2.4.2, Page 81 Line 3
Comment
  Pulse shaping is not necessary for OFDM signals, because their spectrum is ideal bandlimited. However to address possible spurious during transition between OFDM symbols, optional windowing should be applied to meet regulatory requirements.
Proposed Change
  Either discard pulse shaping conformal to 802.15.4g or specify windowing, conformal to sub-clause 20.3.3.12.

## Slide 7: CID 154 (cont’d)
Proposed Resolution
  Out of Scope
  Basic OFDM signals have out-of-band noise which has more power than the regulatory spectral mask requirements. Refer to 15-12-0377-00. To address this spurious noise during transition between OFDM symbols and enhance performance, pulse shaping specified in the draft should be applied. Refer to 15-12-0627-02. The comment is deemed out of scope for this recirculation ballot.

## Slide 8: CID 166
Related Subclause
  T.4, Page 118 Line 9
Comment
  In time domain the STF consists of overlayed sine waves. An autocorrelation would result in a constant value during the STF period, which is NOT useful for ToA measurements. Moreover DFT of FFT based OFDM receives normally do not require autocorrelation or cross-correlations techniques in time domain, such that an a significant design overhead is introduced for a very rough location purpose.
Proposed Change
  Remove proposal to measure ToA on OFDM PHYs. Reference to TG 802.15.4r for appropriate ranging algorithms.

## Slide 9: CID 166 (cont’d)
Proposed Resolution
  Reject
  In the time domain, autocorrelation has periodic peaks during the STF period. Therefore the distinctive correlation characteristics of this STF combined with the following LTF are useful for ToA measurements. Refer to 15-13-0242-01. Most OFDM systems use correlation methods to realize synchronization at the initial stage at the receiver, which can also be used for the ranging purpose. Therefore T.4 does not need to be removed.