## Slide 1
Simulation Methodology for SRU
Authors:
Name | Affiliations | Address | Phone | email
Takashi Yamamoto | Sumitomo Electric Industries, Ltd. | 1-1-3, Shimaya, Konohana-ku, Osaka, 554-0024 Japan | +81-06-6466-5695 | yamamoto-takashi@sei.co.jp
Yoshizo Tanaka |  |  |  | tanaka-yoshizo@sei.co.jp
Kenichi Murakami |  |  |  | murakami-kenichi@sei.co.jp
Hirotsugu Yamamoto |  |  |  | yamamoto-hirotsugu@sei.co.jp
Yoji Okada |  |  |  | okada-yoji@sei.co.jp

## Slide 2
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [SRU Simulation Methodology]
Date Submitted: [16 , Sep 2013]
Source: [Takashi Yamamoto] Company [Sumitomo Electric Industries, Ltd]
Address [1-1-3, Shimaya, Konohana-ku, Osaka, 554-0024 Japan]
Voice:[+81-06-6466-5695], FAX: [+81-06-6462-4586], E-Mail:[yamamoto-takashi@sei.co.jp]
Re: [In response to call for proposals for SRU Study Group]
Abstract: [A simulation methodology for SRU is proposed.]
Purpose: [For the SG and future work]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 3: Abstraction
In this report, we propose simulation methodology to identify and evaluate gains of new RRMM strategies.
Unique requirements for focused M2M use cases shall be looked into, and so traffic model, power consumption model, evaluation metrics and measurement modeling are particularly discussed.

## Slide 4: Traffic Model
Periodic transmission of short packet should be evaluated. The simulation parameters are below.
  Payload Size:5bytes, Interval:1s-10s
Additional random backoff in application can be applied to avoid constant packet loss caused by interference.
  The efficiency of 802.15.4 CSMA/CA is unclear with many devices.
  Clock accuracy of oscillation may affect this issue.
Device A
(without random backoff)
Device B
(without random backoff)
Device C
(with random backoff)
Time
packet

## Slide 5: Power Consumption Model
Gateway
Device
Application Data
ACK
Time
Sleep Time
Sleep Time
(X[mW])
Microcomputer on
Wireless module on
Microcomputer and wireless module off
Run Application
(Y[mW])
Transmission and Reception
(Z[mW])
Battery life extension by reducing wake-up time can be one of the requirements of the RRMM mechanism.
An example of power consumption model is shown below, but more precise models and parameters should be investigated.

## Slide 6: Evaluation Metrics
Currently SRU has focus on the following use cases:
  hospital, industrial automation and infrastructure monitoring.
In the use cases, each device conveys important information for each application.
Therefore, we propose that 1% throughput from CDF should be evaluated.
CDF over multiple
random trials
throughput
100%
1%
Evaluate whether this value
is acceptable or not.

## Slide 7: Measurement Function Modeling
Measurement functions are not clarified in IEEE802.15.4, but they have impact on the performance of RRMM. The following simulation models are applied as baseline.
ED (Energy Detection)
LQI (Link Quality Indicator)
X: ED value
Xe : RSSI [dBm] of the channel at any
measurement time (128us)
Z: error (90% bound for +/-6dB)
X: LQI value
Xl : RSSI [dBm] of a received packet
Z: error

## Slide 8: Other Simulation Parameters

## Slide 9: Outdoor Industrial Automation Scenario
Area size: 2km x 2km
Channel model:
  Free space (no fading)
Gateway locations:
  Number: 25
  Placed at intervals of 400m
  5 channels at 2450MHz
Device locations:
  Number: from 500 to 6000
  Placed randomly
  Mobility: Stationary
Gateway
The colors of gateways show their channels.
[m]
[m]

## Slide 10: MAC/PHY Parameters
PHY | Frequency | 2450MHz
 | Bandwidth | 2MHz
 | Tx power | 10dBm
 | Modulation | IEEE802.15.4-2006 O-QPSK 250kbps
 | Bit error rate | IEEE802.15.4-2006 E.4.1.8
 | Radio noise figure | 25dB
 | PHY header size | 6bytes
 | Clock error | ideal
MAC | Access protocol | IEEE802.15.4-2006 unslotted CSMA-CA with default parameters
 | CCA Mode | 1: Energy above threshold ( -75dBm)
 | Max # of retries | 3
 | Max backoff window size | 255
 | MAC header size | 11bytes
 | Association (baseline) | Devices are associated with the highest LQI gateways.

## Slide 11: An Example of Simulation Result
[m]
[m]
Number of Devices:500, Transmission Interval:1s (40bps)
CDF of per-device throughput
[bps]
[%]
Deployment map
The colors of devices
show their channels.
Some devices are associated with the distant gateways because of the
measurement errors, though their QoS performances seem good enough.
Average throughput:: 39.992bps
1% throughput: 39.676bps

## Slide 12: Summary
Simulation methodology for SRU was proposed.
  Traffic model: periodic transmission of short packet
  Power consumption model: should be investigated further
  Evaluation metric: 1% throughput from cdf
  Measurement function modeling
Future work
  Advance the simulation activity and clarify the requirements of SRU through RRMM mechanism.
  Can we use this methodology to assess enhancements? If you encounter any problems to do the simulation, please contact me.