## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Technical Issues for MIMO OCC]
Date Submitted: [January, 2014]
Source: [Yeong Min Jang and Nirzhar Saha]
[Kookmin University]
Address [Kookmin University, Seoul, Korea]
Voice:[82-2-910-5068], FAX: [82-2-910-5068], E-Mail:[yjang@kookmin.ac.kr]
Re: []
Abstract: [Technical Issues for MIMO Optical Camera Communication]
Purpose: [Contribution to IEEE 802.15.SG7a OCC]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15-14-0042-00-007a
Notes: doc.: IEEE 802.15-09-0117-00-0007
<month year>

## Slide 2
Technical Issues for MIMO OCC
Several issues relating MIMO adoption in OCC System
  Combining multiplexing and diversity simultaneously
  Transmitter and receiver alignment problem
  Spatial separation of transmitters in the receivers
doc.: IEEE 802.15-14-0042-00-007a

## Slide 3
MIMO Schematic for OCC System
Each LED or group of LEDs can be used as transmitting antenna.
Either camera or image sensor (IS) can be used as receiver.
doc.: IEEE 802.15-14-0042-00-007a

## Slide 4: Challenges for MIMO OCC System
Combining multiplexing and diversity for OCC
  Objective: Capacity enhancement (for speed) and robust communication link (for reliability)
  Problem: To achieve optimum gain when both diversity and multiplexing are combined
  Remark: To introduce MIMO coding schemes (V-BLAST and STBC) into OCC
Spatial Separation of pixels (channels)
  Objective: Distinguish the multi-channel by successful pixel separation
  Problem: Pixels may overlap and result inter-symbol interference
  Remark: Efficient algorithm to distinguish pixel. Selection and combining schemes (e.g. MRC, generalized selection combining etc.) can be used in OCC to select channels (pixels) with highest SNR values
Transmitter and receiver alignment problem
  Objective: To increase the number of rank of the channel matrix
  Problem: Placing receiver in corner of the room reduce the channel rank to one, therefore it is impossible to achieve diversity as well as multiplexing
  Remark: To introduce angle diversity and tilting receiver arrangement
doc.: IEEE 802.15-14-0042-00-007a

## Slide 5: Conclusions
Need to study about multi-array LED based transmitter for MIMO OCC system in order to achieve both diversity and multiplexing simultaneously
Need to develop a selector or combiner technology for MIMO OCC system
Need to introduce transmitter and receiver arrangement issues for MIMO OCC system
doc.: IEEE 802.15-14-0042-00-007a