## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Ranging in 802.15.4m and Beyond]
Date Submitted: [20 January 2014]
Source: [Ben Rolfe] Company [BCA.] Cristina Seibert [SSN]
Address [PO Box 798 Los Gatos CA 95031]
Voice:[+1 408 395 7207], FAX: [deprecated], E-Mail:[ben.rofe @i eee.org]
Re: [Call for Applications in Study Group 4s]
Abstract: [Review Ranging applications, and the current state of ranging in 802.15.4]
Purpose: [Contribute to developing the project]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Ranging in 4m and beyond
Ranging Applications and 802.15.4

## Slide 3: 802.15.4
PHY Support for ranging
  UWB (clause 14)
  LRP UWB (clause 17)
  TVWS PHYS (clause 20)
SAP Support
  PHY PIB attributes
  Ranging enable/report in MCPS-DATA
  Calibration MLME
OTA protocol (IEs) for time exchange

## Slide 4: Summary of 4m Ranging Features
Ranging bit in the PHR of each PHY.
  RFRAMES and RMARKERS
IEs for exchanging timing information that can be used for ranging:
  TX time
  RX TX Time difference
ACK of RFRAME required to include RX TX Time difference IE
Informative annex on techniques to compute TOA
  For FSK PHY: based on phase transitions between consecutive preamble symbols
  For OFDM PHY: use autocorrelation properties of STF/LTF

## Slide 5: Possible Extensions
Generalized IE content, e.g. include information:
  Pertaining to absolute time
  Pertaining to signal phase
  Pertaining to signal power
  Pertaining to device calibration, processing chain delays, etc.
  Pertaining to one or more carrier frequencies
Communicate known geo-coordinates
  IEs defined in 4m may be reusable
Define transaction-based exchanges
  Added flexibility compared to current method
  Request particular information, e.g. phase for particular carrier frequencies, absolute time, geo-coordinates, calibration aspects per device/chain
  Ability to pair response with a particular request
  Include retransmission mechanisms?

## Slide 6: Ranging Applications

## Slide 7: Ranging and Localization
Localization: Determining location, relative to something
  Geo-location – location relative to surface of the Earth (sometimes called “absolute” position inaccurately)
  Relative to some known location
    Position of objects in a building
  Proximity to other objects
    Relative distance between objects
Ranging: Determining distance between two objects
  RF ranging via time of flight / time of arrival
  RF ranging via relative phase of arrival
  RF ranging via signal strength
  Other (optical, sonic, … not in scope of 15.4)

## Slide 8: Ranging Applications: Motion Rates
No dynamics
  Provisioning of fixed or seldom moving devices
Portable
  Move but not during operation
Slow moving
  Personal/portable at pedestrian rates
Moderate to fast moving
  On vehicles (tranes, planes, automobiles)

## Slide 9: Ranging Applications: Motion Rates
No dynamics
  Provisioning of fixed or seldom moving devices
Portable
  Move but not during operation
Slow moving
  Personal/portable at pedestrian rates
Moderate to fast moving
  On vehicles (tranes, planes, automobiles)

## Slide 10: Ranging Applications: No dynamics
Provisioning of fixed devices
  Meters, sensors , monitoring devices
  Building automation, Process Control
  Automatic localization
    Reduces provisioning cost (lower skill required)
    Reduces errors
Location of assets
  Inventory, containers, etc
  Post deployment “finding” (errors in records)

## Slide 11: Application vs Precision
Various needs
  Coarse position (TVWS)
  medium precision (Meters, sensors)
  Apps for high precision (assets, people, …)
Various technical approaches
  UWB – high precision via wide bandwidth
  Narrow band ToF – precision scales with time (trade time for precision)
  Phase – precision scales with time