## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Comments on IEEE 802.15.8 PAC Technical Guidance Document
Date Submitted: 21 January, 2014
Source: Byung-Jae Kwak, Kapseok Chang, Moon-Sik Lee
ETRI, Korea
Address: 218 Gajeong-ro, Yuseong-gu, Daejeon, 305-700, Korea
Voice: +82-42-860-6618, FAX: +82-42-860-6732, E-Mail: bjkwak@etri.re.kr
Re: TG8 Technical Guidance Document (15-12-0568-07-0008)
Abstract: Editorial and technical comments on IEEE 802.15.8 PAC Technical Guidance Document.
Purpose: Update TG8 technical guidance document
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: This Contribution Includes:
Editorial comments
  White spaces
  Font sizes (9,10,11  11)
  Units
  Other cosmetic improvements
  See the attachment for details
Technical comments
  Error in equations
  See the attachment for details
Discussion on receiver sensitivity for channel sensing

## Slide 3: Receive Sensitivity for Channel Sensing
Receiver sensitivity: -82 dBm
Thermal noise density: -174 dBm/Hz
SNR for 20 MHz channel:
  Thermal noise power:
  -174 + 10 log10(20*E6) = -101 dBm
  SNR at carrier sensing range: 19 dB

## Slide 4: Receive Sensitivity for Channel Sensing
SNR for 10 MHz channel:
  Thermal noise power:
    -174 + 10 long10 (10*E6) = -104 dBM
  SNR at carrier sensing range: 22 dB

## Slide 5: Link Performance: PER Curve
Chart: Es/N0
| -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13
BPSK(1/2) | 1 | 0.9857 | 0.85703 | 0.55969 | 0.23655 | 0.077784 | 0.019396 | 0.0051832 | 0.00086006 | 0.00013901
BPSK(3/4) | 1 | 0.978 | 0.807 | 0.446 | 0.161 | 0.0483 | 0.0118 | 0.00251 | 0.000503 | 8e-05
QPSK(1/2) | 1 | 0.9884 | 0.86343 | 0.54989 | 0.23685 | 0.071786 | 0.021196 | 0.0042777 | 0.00092071 | 0.00013998
QPSK(3/4) | 1 | 0.978 | 0.807 | 0.446 | 0.161 | 0.0483 | 0.0118 | 0.00251 | 0.000503 | 8e-05
16QAM(1/2) | 1 | 0.987 | 0.864 | 0.562 | 0.26 | 0.0898 | 0.0288 | 0.00679 | 0.00138 | 0.00025 | 4.8e-05
16QAM(3/4) | 1 | 0.998 | 0.947 | 0.725 | 0.38 | 0.154 | 0.0506 | 0.0168 | 0.00421 | 0.000945 | 0.000221 | 3.8e-05
64QAM(2/3) | 1 | 0.998 | 0.975 | 0.823 | 0.511 | 0.232 | 0.0807 | 0.0246 | 0.00741 | 0.00208 | 0.000479 | 9.2e-05
64QAM(3/4) | 1 | 0.985 | 0.873 | 0.601 | 0.316 | 0.127 | 0.0476 | 0.0169 | 0.0054 | 0.00163 | 0.000455 | 0.000103
64QAM(5/6) | 1 | 0.991 | 0.906 | 0.652 | 0.337 | 0.13 | 0.0496 | 0.0147 | 0.00507 | 0.0015 | 0.00038 | 8.7e-05

## Slide 6: Implication
PER = 0 at carrier sensing range
Carrier sensing range = communication range
Discussion:
  Carrier sensitivity -82 dBm too large?
  What is the appropriate value?

## Slide 7: Motion
Motion: “Approve the attached version of TGD as an updated version of TGD.”
Voting
  Yes:
  No:
  Abstain:
  Result: