## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Review of Evaluation methodology of other task groups in 802.15 and proposal of evaluation methodology for TG10 TGD
Date Submitted: February 10, 2014
Source: Soo-Young Chang (SYCA), Jaehwan Kim (ETRI), and Sangsung Choi (ETRI) Voice: +1 530 574 2741, E-maill: sychang@ecs.csus.edu
Re: [802.1.5 TG10 TRD]
Abstract: Evaluation methodologies of some 802.15 Task Groups are reviewed and an evaluation methodology for TG10 TRD is proposed.
Purpose: To prepare the evaluation methodology for TG10.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: INTRODUCTION
An evaluation methodology needs to be prepared for TG10 Technical Guidance Document.
To prepare this methodology, evaluation methodologies from other task groups are reviewed.
  TG4a, TG4g, TG4k, TG4m, TG4n, TG4p, TG4q, TG6, TG7, and TG8
In this document, from this review an evaluation methodology is proposed.

## Slide 3: EVALUATION METHODOLOGY FROM TG4a (1)
Related documents:
15-04-0380-02-004a-tg4a-call-proposals
15-03-0442-01-004a-sg4a-categories-cfa-responses
15-04-0198-02-004a-tg4a-technical-requirement-doc
15-04-0232-16-004a-tg4a-alt-phy-selection-criteria
15-04-0247-03-004a-tg4a-down-selection-voting-procedure
Contents related to evaluation methodology:
From CFP
This CFP solicits data that will fulfill this PAR for the creation of this amendment standard. Additionally, there are 2 other documents that are required reading:
  (1) a summary of the 19 application presentations from the Study Group 4a call for applications (document 03/442r1) and definition of the fundamental requirements implied by applications (draft document: IEEE P802.15-04/198r2 Alternate PHY Technical Requirements) and
  (2) a list of expected performance and attribute criteria (draft document: IEEE P802.15-04/232 Alternate PHY Selection Criteria – latest revision). These criteria will be used to evaluate the proposals.

## Slide 4: EVALUATION METHODOLOGY FROM TG4a (2)
Contents related to evaluation methodology:
From TRD
This document serves two purposes. It is first a summary of the application presentations from the Study Group 4a call for applications. Second it defines the fundamental requirements implied by applications and summarized in the documents
  ref. 15-03-0489-04-004a-application-requirement-analysis.xls
  ref. 15-03-0442-01-004a-Categories for CFA SG4a Response.doc
This document associated with the corresponding selection criteria document will guide proposers on how to respond to a call for proposals.
From SCD
This document defines technical criteria which the proposals should meet including general selection criteria, PHY and MAC criteria.
This group struggled to apply this document, but the group completed the baseline document before it was finalized.
Methodology for this group
Methodology for preparing the proposals is mentioned in the call for proposals (CFP) and TRD: technical requirements details.
The methodology for evaluation of proposals is mentioned in a separate document, SCD.

## Slide 5: EVALUATION METHODOLOGY FROM TG4g (1)
Related document:
15-09-0077-00-004g-call-for-proposals
15-09-0075-08-004g-phy-parameters-for-15-4g: Technical Guidance Document (TGD))
Contents related to evaluation methodology:
From CFP
The proposals should refer to the latest version IEEE 802.15-09-0075 (technical guidance) for proposal content guidance.
From TGD
Methodology
The methodology provides a consensus approach to defining a minimal set of features, characteristics, performance and constraints. This document provides
  A functional view of the PHY characteristics, in the form of specific parameters which define externally verifiable performance and interoperability characteristics;
  A dependency matrix, which considers the interdependency of tradeoffs which are made in the selection of PHY features;
  Application/performance descriptions which characterizes the types of SUN applications and the derived performance characteristics;
  Supporting background information on the source of requirements

## Slide 6: EVALUATION METHODOLOGY FROM TG4g (2)
Contents related to evaluation methodology: (cont’d)
From TGD (cont’d)
Methodology (cont’d)
The parameters table provides guidance on developing complete technical proposals. This represents a subset of parameters, and the absence of a parameter should not be seen as a constraint. The parameter column consists of two sub-columns. The first identifies the parameter, which should be addressed in the proposal; the second provides some examples of how this may be addressed in a proposal; there may be alternatives appropriate to specifying the characteristic.
The performance criteria column includes requirements and constraints, and/or explanations. The “regulatory” column is intended to identify where regional differences in regulations (present and anticipated) may affect the PHY characteristics.
Methodology for this group
Methodology for preparing the proposals is mentioned in the call for proposals (CFP).
The methodology for evaluation of proposals is mentioned in a document, TGD.
  This document also serves to guide in preparation and evaluation of proposals.

## Slide 7: EVALUATION METHODOLOGY FROM TG4k (1)
Related document:
15-11-0147-02-004k-lecim-call-for-proposals
15-11-0359-04-004k-technical-guidance-document
Contents related to evaluation methodology:
From CFP
These proposals should refer to IEEE 802.15-11-0359-04 for proposal content guidance.
From TGD
Methodology
The methodology provides a consensus approach to defining a minimal set of features, characteristics, performance and constraints to be considered. This document provides
  A functional view of the PHY characteristics, in the form of specific parameters which define externally verifiable performance and interoperability characteristics;
  Application/performance descriptions which characterizes the types of LECIM applications and the derived performance characteristics;

## Slide 8: EVALUATION METHODOLOGY FROM TG4k (2)
Contents related to evaluation methodology: (cont’d)
From TGD
Methodology (cont’d)
The parameters table provides guidance on developing complete technical proposals. This represents a subset of parameters, and the absence of a parameter should not be seen as a constraint. The parameter column consists of two sub-columns. The first identifies the parameter, which should be addressed in some way in the proposal; the second provides some examples of how this might be addressed in a proposal; there will be alternatives appropriate to specifying the characteristic depending on the specifics of the proposal. The performance criteria column includes potential requirements, constraints, and/or explanations that may help in consideration during the proposal preparation. The “regulatory” column is intended to identify where regional differences in regulations (present and anticipated) may affect the PHY characteristics.
In preparing proposals, this can be used as a framework to produce a concise summary of the characteristics of each given proposal, and will allow the group to see the similarities and differences in submitted proposals.
Methodology for this group
Methodology for preparing the proposals is mentioned in the call for proposals (CFP).
The methodology for evaluation of proposals is mentioned in a document, TGD.
    This document also serves to guide in preparation and evaluation of proposals.

## Slide 9: EVALUATION METHODOLOGY FROM TG4m (1)
Related document:
15-12-0170-02-004m-call-for-proposals
15-11-0684-12-004m-TG4m-technical-guidance-document
Contents related to evaluation methodology:
From CFP
GUIDELINES FOR PROPOSALS
These proposals should refer to the latest version IEEE 802.15-11-0684 (Technical Guidance Document, TGD) for proposal content guidance.

## Slide 10: EVALUATION METHODOLOGY FROM TG4m (2)
Contents related to evaluation methodology: (cont’d)
From TGD
Methodology
The methodology provides recommendations to defining a minimal set of features, characteristics, performance and constraints to be considered. This document provides:
  A functional view of the PHY characteristics, in the form of specific parameters which define externally verifiable performance and interoperability characteristics; and
  Application/performance descriptions that characterizes the types of WPAN-WS applications and the derived performance characteristics.
In preparing proposals, this can be used as a framework to produce a concise summary of the characteristics of each given proposal, and will allow the group to see the similarities and differences in submitted proposals.
Methodology for this group
Methodology for preparing the proposals is mentioned in the call for proposals (CFP).
The methodology for evaluation of proposals is mentioned in a document, TGD.

## Slide 11: EVALUATION METHODOLOGY FROM TG4n
Related document:
15-12-0518-01-004n-call-for-proposals
Contents related to evaluation methodology:
From CFP
Proposers are suggested to refer to the following documents:
  15-12-0471-01-004n-detail-summary-of-interference-on-chinese-medical-bands
  15-12-0105-00-004n-translation-of-chinese-miit-doc423-2005
for the regulatory requirements in China.
Methodology for this group
Methodology for preparing the proposals is mentioned in the call for proposals (CFP).
No TGD found.

## Slide 12: EVALUATION METHODOLOGY FROM TG4p
Related document:
15-12-0267-01-004p-ptc-technical-guidance-document
Contents related to evaluation methodology:
From TGD
Methodology
The methodology provides a consensus approach to defining a minimal subset of features, characteristics, performance and constraints. This document will provide
  A functional view of the PHY characteristics, in the form of specific parameters which define externally verifiable performance and interoperability characteristics;
  A dependency matrix, which considers the interdependency of tradeoffs which are made in the selection of PHY features;
  An application/performance matrix which characterizes by classes of rail control applications the priority of performance characteristics; this shall include a link budget, with at least transmitter parameters, receiver parameters, and link margin in AWGN (see Link Budget section).
The parameters table provides guidance on developing complete technical proposals. This represents a subset of parameters, and the absence of a parameter should not be seen as a constraint. The parameter column consists of two sub-columns. The first identifies the parameter, which should be addressed in the proposal; the second provides some examples of how this may be addressed in a proposal; there may be alternatives appropriate to specifying the characteristic. The performance criteria column includes constraints (derived form the PAR) or explanations. The regulator column is intended to identify where regional differences in regulations (present and anticipated) may affect the PHY characteristics.
Methodology for this group
No CFP document found
The methodology for evaluation of proposals is mentioned in a document, TGD.

## Slide 13: EVALUATION METHODOLOGY FROM TG4q (1)
Related document:
15-13-0573-01-004q-ulp-cfp
15-13-0341-03-004q-tg4q-tgd-draftt
Contents related to evaluation methodology:
From CFP
No methodology is mentioned in the call for proposals.
From TGD
Methodology
The methodology is based on a consensus approach to defining a minimal set of features, characteristics, performance and constraints to be considered when making a proposal. This document provides:
  A functional view of the PHY characteristics, in the form of specific parameters which define externally verifiable performance and interoperability considerations ;
  Performance descriptions which characterize the ULP physical layer with any required MAC changes.

## Slide 14: EVALUATION METHODOLOGY FROM TG4q (2)
Contents related to evaluation methodology: (cont’d)
From TGD (cont’d)
Methodology
The parameters discussed in this document are essential parameters for the design of physical layer and also satisfy IEEE 802.15.4q PAR. The proposal shall reference the relevant regulations. The device shall abide by regulations in the region it is operating. The parameters are as follows
  Range
  Data Rate
  Symbol/chip rate
  Modulation/coding
  Synchronization and Timing
  PHY frame structure
  Transmit Power
  Interference rejection
Proposers should clearly stipulate the mandatory and optional behaviors.
Methodology for this group
No methodology is mentioned in the call for proposals: only PAR is mentioned.
The methodology for evaluation of proposals is mentioned in a document, TGD.
  - capability
  - Chan availability
  - Sensitivity
  - Interoperability
  - Co-existence
  - Low Power capability
  - Operational bands.
  - Transmit PSD

## Slide 15: EVALUATION METHODOLOGY FROM TG6 (1)
Related document:
15-08-0829-01-0006-tg6-call-for-proposals
15-08-0080-00-0006-ieee-802-15-6-selection-criteria-document
15-08-0644-09-0006-tg6-technical-requirements-document
Contents related to evaluation methodology:
From CFP
Proposals are solicited for a standard compliant with the PAR for TG6. For additional information see the latest revision of the Application, Regulatory and Channel model documents.
Proponents should provide, the following information, using IEEE 802.15 document template:
  Proposal document describing the details of the proposal.
  Proposal overview presentation, which will be presented to TG6 members, not longer than 45 minutes, including the Q&A.
  Simulation results, if available.
The CFP does not mention about SCD and TRD.

## Slide 16: EVALUATION METHODOLOGY FROM TG6 (2)
Contents related to evaluation methodology: (cont’d)
From SCD
The SCD document will become the repository for the requirements to be used in the selection process for PHY and MAC Draft Standard for IEEE 802.15.6.
From TRD
This technical requirement document (TRD) describes the technical aspects that TG6 standard must fulfill.
This document serves two purposes. First, it summarizes the applications presented in response to BAN Study group and TG6 Call for Applications. Second, it describes and defines the fundamental requirements implied by applications but not necessarily stated explicitly.
Methodology for this group
Methodology for preparing the proposals is mentioned in the call for proposals.
The methodology for evaluation of proposals is mentioned in two separate document, TGD and SCD with detailed criteria and technical requirements.

## Slide 17: EVALUATION METHODOLOGY FROM TG7
Related document:
15-09-0564-01-0007-tg7-technical-considerations-document
Contents related to evaluation methodology:
From CFP
No CFP document found
From TCD
TG7 group used TCD (technical Considerations Document)
Difference between Considerations and Requirements (TCD vs. TRD)
The TG7 group decided to use the term “considerations” instead of “requirements” in order to adopt a less rigid and formal process with the intention to be able to develop the standard quickly. This document serves to provide guidance for development of technical contributions for the IEEE 802.15.7 standard. The contents of the document are expected to be similar to a technical requirements document.
Methodology for this group
Methodology for the proposals is mentioned in the call for proposals:
  The “proposals should refer to the latest version IEEE 802.15-09-0075 (technical guidance) for proposal content guidance”.
This TCD specifies the methodology for preparing the TGD with detailed technical requirements.

## Slide 18: EVALUATION METHODOLOGY FROM TG8 (1)
Related document:
15-13-0069-05-0008-tg8-call-for-proposals-cfp
15-12-0568-05-0008-tg8-technical-guidance-document
Contents related to evaluation methodology:
From CFP
CFP refers to the following documents:
  PAR: Doc. 15-12-0063r2
  5C: Doc. 15-12-0064r1
  Technical Guidance Document: 15-12-0568r5
  Application Matrix: 15-12-0684r0
Proposers should provide the following information using IEEE 802.15 document template:
  Proposal document describing the details of the proposal.
  Proposal presentation, which will be presented to TG8 members, not longer than 40 minutes, excluding the Q&A.
  Simulation results based on evaluation methodology in TGD, if available.

## Slide 19: EVALUATION METHODOLOGY FROM TG8 (2)
Contents related to evaluation methodology:
From TRD
4. General descriptions
  This clause provides the basic framework of PDs. The framework serves as a guideline in developing the functionalities of PDs and their interactions specified in detail in the subsequent clauses.
9. Evaluation methodology
9.1. Antenna Configuration
9.2. Channel models
9.3. Simulation scenarios and parameters
9.3.1. Link budget analysis (PHY)
9.3.2. Link-level simulation (PHY)
9.4. System-level simulation (MAC)
9.4.1. General simulation parameters
9.4.2. Scenarios & parameters for just PDs
9.4.3. Scenarios & parameters for PD links
Methodology for this group
Methodology for the proposals is mentioned in the call for proposals (CFP).
This TRD specifies the detailed methodology to evaluate the proposals in Subclause 9 as shown above.

## Slide 20: SUMMARY AND CONCLUSIONS (1)
  In this document,
    Evaluation methodologies from 10 TGs in 802.15 are reviewed.
    From this review, two methodologies in TGD can be considered:
    Methodology to prepare the TGD
    Methodology to describe technical details for providing guidance to proposers
      to assist proposers for preparation of proposals
      to evaluate proposals

## Slide 21: SUMMARY AND CONCLUSIONS (2)
  Observations from this review
    TG4a group has three documents related to evaluation methodology:
      CFP (Call for Proposals), TRD (Technical Requirements Documents), and SCD (Selection Criteria Document).
      An evaluation methodology is mentioned in SCD.
      TG6 has a similar format.
    All TG4 task groups except TG4a and TG7 show similar tendency to relieve the constraints for the proposals using TGD (Technical Guidance Document), not TRD.
      Just to guide the proposers for their preparation
      Using a minimal set of features, characteristics, performance and constraints to be considered when making a proposal to select technical details for baseline document.
    TG8 uses a unique form of TGD in the middle of these two types.
      One section for this methodology is included in TGD: Subclause 9 Evaluation Methodology.

## Slide 22: SUMMARY AND CONCLUSIONS (3)
  Conclusions
    Understanding from the Table of Contents of the TG10 TGD draft is that this group intends to follow the TG8 type methodology.
      By including a section in the TGD for evaluation methodology.
    For this format, we need to have strict metrics and related values to evaluate proposals.
      However, at this point, it is not easy to identify these metrics and their values.
    Therefore an approach used for most TG4 task groups can be used for the TG10 TGD document.
      Defining a minimal set of features, characteristics, performance and constraints to be considered when making a proposal to select technical details for baseline document.
      Not including a clause for evaluation methodology.

## Slide 23: SUMMARY AND CONCLUSIONS (4)
  Proposed text for Methodology for TG10 TGD
  which can be included in “1 Overview” of TGD.
Methodology
The methodology is based on a consensus approach to defining a minimal set of features, characteristics, performance and constraints to be considered when making a proposal.
This document provides:
  A functional view of the L2R characteristics, in the form of specific parameters which define externally verifiable performance and interoperability considerations ;
  Performance descriptions which characterize the Layer 2 routing with any required MAC information elements.
In preparing proposals, this can be used as a framework to produce a concise summary of the characteristics of each given proposal, and will allow the group to see the similarities and differences in submitted proposals.

## Slide 24: SUMMARY AND CONCLUSIONS (5)
  Proposed table of contents for evaluation methodology for TG10
    If the group decides to adopt a format which needs a clause for Evaluation Methodology.
8 Evaluation Methodology
8.1 Simulation scenarios and parameters
8.1.1 Scenarios
8.1.1 Related parameters
8.2 System level simulation (Layer 2)
8.2.1 General simulation parameters
8.2.2 Information from MAC and PHY Layer
8.2.3 Scenarios & parameters for communication links
8.2.4 Scenarios & parameters for flow control and routing
parameters | values
Data rates | 1 kbps – 27 Mbps
Type network | Mesh, linear topology , dynamically changing on the order of a minute time frame
Transmission types | One-to-many, many-to-one, multicast, broadcast, peer to peer
Max packet delay | 10 sec
Duty cycle | TBD
Sleep time | TBD
………. |