## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Fully Distributed Contention Based MAC Proposal for PAC
Date Submitted: 12 March, 2014
Source: Byung-Jae Kwak (ETRI), Kapseok Chang (ETRI), Moon-Sik Lee (ETRI),
Junhyuk Kim (KAIST), June-Koo Kevin Rhee (KAIST)
Address: ETRI, Daejeon, Korea; KAIST, Daejeon, Korea
Voice:
E-Mail: {bjkwak, kschang, moonsiklee}@etri.re.kr, kim.jh@kaist.ac.kr, rhee.jk@kaist.edu
Re: TG8 PAC Call for Contributions (CFC), 15-14-0087-00-0008, Jan 23, 2014.
Abstract: This document provides a fully distributed, synchronized, contention based MAC proposal for PAC
Purpose: To discuss the merits of the proposed scheme, which is to be harmonized with other proposals for approval
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Fully Distributed Contention Based MAC Proposal for PAC
March 2014
Byung-Jae Kwak (ETRI), Kapseok Chang (ETRI), Mook-Sik Lee (ETRI),
Junhyuk Kim (KAIST), June-Koo Kevin Rhee (KAIST)

## Slide 3: Introduction
Unlicensed band: PAC should coexist with other networks in the same band
Simple, efficient, scalable
  Simple: little book keeping
  Efficient: high performance, small overhead
  Scalable: support large # devices
Synchronous operation: power saving [1]

## Slide 4: Frame Structure
Synchronization interval [TBD]
Sync slot
  Timing reference signal
Discovery slot
  Query/reply type discovery messages
  SSF request/response messages
  Emergency messages
Data slot
  Other discovery type messages
  Peering request/response messages
  Data

## Slide 5: Synchronization
Timing reference signal
  Transmitted in the sync slot
  Transmitted using random access
  Contains timing offset information
Frame boundary
  Arrival time + timing offset
Time as well frequency synchronization
Robust in the presence of interference from other networks (e.g., WLAN)

## Slide 6: Supported Discovery Types
Query/reply
  Conventional: when the ID of peer is known
  SSF (Self Spatial Filtering) aka LnL (Loon-and-Link):
    Peer in visible range
    The ID of peer may not known
  Transmitted in the discovery slot
Advertisement
  Transmitted in the data slot
Publish/subscribe
  Transmitted in the data slot
Transmitted using random access

## Slide 7: Peering
Peering, re-peering, de-peering messages
Transmitted in the data slot using random access

## Slide 8: Data
Unicast, multicast, and broadcast messages
Transmitted in the data slot using random access

## Slide 9: MPDU Structure
MPDU Header: TBD
FCS: TBD

## Slide 10: Sleep Mode Support
PDs in sleep mode
  Stay active in the sync slot to maintain network sync
  Stay inactive in the data slot to reduce power consumption
  Listen to discovery indication sub-slot
    If carrier is sensed, listen to discovery sub-slot for discovery messages
    If no carrier is sensed, do not listen to the discovery sub-slot to further reduce power consumption
PDs with discovery message to transmit
  Transmit discovery indication signal in the discovery indication sub-slot
  Transmit discovery message in the discovery sub-slot using random access

## Slide 11: Discovery Slot Reuse
PDs with data to transmit
  Stay active in the sync slot to maintain network sync
  Listen to discovery indication sub-slot
    If carrier is sensed, this means discovery sub-slot is reserved for discovery messages
    If no carrier is sensed, this means no discovery message will be transmitted in the discovery sub-slot, and thus discovery sub-slot can also be used for data transmission.

## Slide 12: Network Convergence
In this document
  “Network” means a set of PDs, any two PDs of which can exchange data or control messages with each other either directly or through a multi-hop relay route.
  Two networks “meet” when one or more PDs in one network can communicate with one or more PDs in another network.
  Two networks meet when the networks move, or any obstacles separating the two networks are removed.
Our proposal: convergence of two networks with no interruption of services

## Slide 13: Network Convergence: Case I
PDs in Net 1
  Maintain normal behavior in the sync slot & discovery slot of Net 1
  Maintain normal behavior in the data slot of Net 1, except that they stop transmitting in the sync slot & discovery slot of Net 2 to avoid interference
(T1 < T2)

## Slide 14: Network Convergence: Case I
PDs in Net 2
  Maintain normal behavior, except that they stop transmitting during the sync slot & discovery slot of Net 1.
  Set timeout as a function of their current CW, and if the timeout expires, switch to Net 1.
  When switching to Net 1, they transmit a notification message in the discovery slot of Net 2, notifying other PDs in Net 2 of their move.
  When in sleep mode and hear move notification messages from other PDs in Net 2, wake up from sleep mode to follow the normal move procedure
(T1 < T2)

## Slide 15: Network Convergence: Case II
Net 1 and Net 2 cannot coexist without interfering with each other
Immediate convergence of the two networks is desirable
PDs in Net 1 maintain normal behavior
PDs in Net 2:
  Switch to Net 1 as soon as they discover Net 1.
  When switching to Net 1, they transmit a notification message in the discovery slot of Net 2, notifying other PDs in Net 2 of their move.
  When in sleep mode and hear either timing reference signal of Net 1 or move notification from other PDs in Net 2, wake up and follow the normal move procedure
(sync slot + discovery slot) of Net 1 overlaps with (sync slot + discovery slot) of Net 2

## Slide 16: Proposed Random Access
Typical Random Access (CSMA/CA)
  A random number is selected between 0 and CW-1 (CW: contention window)
  The chosen number is decreased every idle slot time
  A frame is transmitted when the number reaches 0
  If the transmitter does not receive an ACK (interpreted as a collision), the CW is increased by factor 2 (BEB: Binary Exponential Backoff)
  If the transmission succeeds, the CW is reduced to the minimum CW

## Slide 17: Proposed Random Access
Improvements to Typical Random Access
  CW should reflect the # of PDs
    Each device should estimate the # of PDs in the network
    Collision is a good indicator of the # of PDs
  Improved backoff algorithm
    BEB is not scalable
    Use EIED backoff algorithm [2]
  Slotted CAMA/CA
    Channel access is tried in units of slot time
    Eases the design of network management

## Slide 18: Proposed Random Access
Tone based collision detection
  Requires timing- and frequency synchronization
  See [3] for details
Tx
Tx
Rx

## Slide 19: Proposed Random Access
Proposed CSMA/CA Mechanism
  Each PD overhears frames in the air
  Each PD increases its CW if it detects a collision
  Each PD decreases its CW when it does not detect a collision for a given time period (T)
  A PD transmits a frame and does not receive an ACK, the PD assumes its frame was involved in a collision and increases its CW
  The increase and decrease of CW follows EIED backoff alg.
  ※ See also [4].

## Slide 20: Proposed Random Access
Features of the Proposed CSMA/CA
  Adaptive: The CW of each PD is adjusted dynamically, reflecting the channel condition in a distributed manner
  No “lucky” or “unlucky” PDs (Fairness): The CW is updated based on network events, rather than on each PD’s own experience
  Efficient: The EIED backoff algorithm guarantees efficient medium access [2]

## Slide 21: References
[1] Jung-Hyun Kim, Jihyung Kim, Kwangjae Lim, Dong Seung Kwon, “Distributed Frequency Synchronization for Global Synchronization in Wireless Mesh Networks,” World Academy of Science and Technology, vol. 70, 2012, pp. 1080-1084.
[2] Nah-Oak Song, Byung-Jae Kwak, Jabin Song, L. E. Miller, “Enhancement of IEEE 802.11 Distributed Coordination Function with Exponential Increase Exponential Decrease Backoff Algorithm,” Proceedings of IEEE 57th Vehicular Technology Conference (VTC 2003-Spring), vol. 4, pp. 2775−2778, Jeju, Korea, April 22−25, 2003.
[3] IEEE 802.15-14-0132-00-0008, “Collision Detection based PHY Proposal for PAC,” March 2014.
[4] IEEE 802.15-13-0650-00-0008, “Collision Detection Based Random Access Scheme for IEEE 802.15 TG8 PAC,” Nov. 2013.