## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Collision Detection based PHY Proposal for PAC
Date Submitted: March 16, 2014
Source: Kapseok Chang, Byung-Jae Kwak, and Moon-Sik Lee and Byung-Jae Kwak (ETRI)
Company: ETRI
Address: 218 Gajeong-ro, Yuseong-gu, Daejeon, 305-700, Korea
Voice: +82 42 860 1639 Fax: E-Mail: {kschang, bjkwak, moonsiklee}@etri.re.kr , bjkwak, moonsiklee}@etri.re.kr,
Re: TG8 PAC Call for Contributions (CFC: IEEE P802.15-14-0087-00-0008)
Abstract: This document presents technical proposals for IEEE 802.15. TG8 PAC standard.
Purpose: Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline
Proposal Overview
Channelization
PHY Overview
MCS Characteristics
MCS Table
PHY Parameters
PPDU Format
Preamble Format
Modulation and Mapping
Header
Payload
PHY Security
Conclusions

## Slide 3: Proposal Overview
This presentation is related to collision detection based PHY proposal that:
  Supports data transmission rates up to 54 Mbps
  Supports more precise synchronization compared to IEEE 802.11
  Enables collision detection in receiving mode
  Supports discovery with spatial filtering
  Supports coexistence with other 2.4GHz and 5GHz

## Slide 4: Channelization
Channel ID | Center Freq. (GHz) | Channel width (MHz) | Sampling Rate (MHz)
1 | 2.4 | 20 | 20
2 | 5 | 20 | 20

## Slide 5: PHY Overview
Transmission mode
  Orthogonal Frequency Division Multiplexing (OFDM)
OFDM MCSs for high performance on frequency selective channels up to 64QAM
More precise synchronization compared to IEEE 802.11 [1]
Enables collision detection in receiving mode
  Realized by tone-based collision detection
Supporting discovery with spatial filtering
  Different presentation (IEEE 802.15-14-0133-00-0008)

## Slide 6: MCS Characteristics
Supports data rates up to ~ 54 Mbps
  Modulation formats: SBPSK, SQPSK, QPSK, 16-QAM, and 64-QAM
  Convolutional Coding: rates 1/2, 3/4, 5/8
Designed to operate in NLOS environments
  Fixed Cyclic Prefix (CP) duration of 0.8 us
  Modulation tolerant to significant frequency selectivity
Designed to achieve frequency diversity
  Spreading and phase-rotation: SBPSK/SQPSK

## Slide 7: MCS Table
MCS index | Modulation | Code Rate | NBPSC | NCBPS | NIBPS | Data Rate (Mbps)
1 | SBPSK | 1/2 | 0.5 | 24 | 12 | 3
2 | SQPSK | 1/2 | 1 | 48 | 24 | 6
3 | SQPSK | 3/4 | 1 | 48 | 36 | 9
4 | QPSK | 1/2 | 2 | 96 | 48 | 12
5 | QPSK | 3/4 | 2 | 96 | 70 | 17.5
6 | 16-QAM | 1/2 | 4 | 192 | 96 | 24
7 | 16-QAM | 3/4 | 4 | 192 | 144 | 36
8 | 64-QAM | 5/8 | 6 | 288 | 180 | 45
9 | 64-QAM | 3/4 | 6 | 288 | 216 | 54
Info bits per OFDM symbol
coded bits per OFDM symbol
coded bits per subcarrier
* The above MCS sets are changeable according to ensuing evaluation result

## Slide 8: Parameters
Parameter | Notation | Value
FFT Size | NFFT | 64
Number of data subcarriers | NDS | 48 (excluding dc)
Number of preamble subcarriers | NPS | 52 (excluding dc)
Number of pilot subcarriers | NSP | 4
OFDM sampling time | ts | 0.5 ns
Subcarrier frequency spacing | ΔF | 312.5 kHz
Cyclic Prefix | TCP | 16ts = 0.8us
OFDM symbol duration | Ts | 4 ns

## Slide 9: PPDU Format
Preamble
  consists of short training field (STF), long training field (LTF), and collision detection field (CDF)
  Preamble is used for carrier sensing, automatic gain control (AGC), packet detection, time/frequency synchronization, channel estimation, and collision detection.
Header
  used for describing the content of the packet data as well as the protocol used to transfer it
Data Field
  used for the information intended for the receiver
Beam Jitter (BJ) Field
  used for Look and Link (LnL)
  see the different presentation (IEEE 802.15-14-0133-00-0008)

## Slide 10: Preamble Format (1)
STF
  It is used for carrier sensing, AGC, packet detection, coarse time/frequency synchronization, and partial fine time/frequency synchronization.
  It consists of a set of 5 repetition signals (Ds).
LTF
  It is used for final fine time/frequency synchronization and channel estimation.
CDF
  It is used for collision detection.

## Slide 11: Preamble Format (2)
STF [2]-[4]
Base sequence
  Modified sequence
  The time-domain signal is inherently immune to carrier frequency offset [4].

## Slide 12: Preamble Format (3)
STF
  What is transmitted is signaled using the STF pattern as shown below
    Set (D,D,D,D,D) is configured in the beginning of the Preamble for each of synchronization slot, request to send (RTS), clear to send (CTS), and acknowledgement (Ack).
    Set (D,D,D,D,-D) is configured in the beginning of the Preamble for data packet.
  Specifically, the discovery indication subslot comprises the STF pattern (D,D,D,D,D) alone.

## Slide 13: Preamble Format (4)
Slide 13
LTF [2]-[4]
Base sequence
  Modified sequence
  The time-domain signal of an effective OFDM symbol (E) is real or imaginary, which make the complexity of a detector for fine synchronization low by a factor of 2 [4].
  The time-domain signal is inherently immune to carrier frequency offset [4].

## Slide 14: Preamble Format (5)
CDF [4]
  A PD who wants to transmit data using Random Access selects two random sub-carriers, one from the upper half and another from the lower half of the sub-carriers.
  The PD transmits a busy tone in the selected sub-carriers of the second symbol of LTF.
  When a receiver sees more than one tone in either of the two sub-carrier blocks.

## Slide 15: Modulation and Mapping (1)
SBPSK/SQPSK
  Concatenated spreading (i.e. diversity gain):
  Phase rotation to suppress peak-to-average-power ratio increasing:

## Slide 16: Modulation and Mapping (2)
QPSK/16QAM/64QAM
  Grouping N bits
  Concatenated frequency mapping so as to reduce burst error

## Slide 17: Header
Header shall be heavily protected.
Bit-level scrambling
  Shall be specified.
  Specific method is TBD.
Channel encoding
  Convolutional encoder shall be specified.
  The specification of channel encoder is TBD.
Modulation schemes applied
  SBPSK/SQPSK: FFS

## Slide 18: Payload
Bit-level scrambling
  TBD
Channel encoding
  Convolutional encoder shall be specified.
  The specification of channel encoder is TBD.
Modulation schemes applied
  SBPSK
  SQPSK
  QPSK
  16-QAM
  64-QAM

## Slide 19: PHY Security
“A system is as strong as the weakest link”
In centralized systems, the infrastructure determines the security policy
Distributed D2D: Devices (users) are on their own
Cannot trust users: “end user carelessness constitute the biggest security threat”
PHY security is especially appealing technology to D2D communications
PHY security protects the radio links between PDs, and provide the 1st layer of security in the layered security model
PHY security can protect MAC header as well as payload

## Slide 20: Conclusions
OFDM MCS’s have been proposed.
  Optimized for NLOS – tolerant to high degree of multipath
  Up to 54 Mbps
Preamble has been proposed.
  The time-/frequency-domain structure of STF
  The frequency-domain structure of LTF
  The frequency-domain structure of CDF for tone-based collision detection
  Optimized for high performance
    To be verified at the next meeting.

## Slide 21: References
IEEE Std 802.11, “Part 11: Wireless LAN medium access control (MAC) and physical layer (PHY) specifications,” IEEE Computer Society, 2012.
K. Chang and Y. Han, “Robust replica correlation-based symbol synchronisation in OFDM systems,” Electronics Letters, vol. 44, no. 17, pp. 1024-1025, Aug. 2008.
K. Chang, P. Ho, and Y. Choi, “Signal design for reduced complexity and accurate cell search/synchronization in OFDM-based cellular systems,” IEEE Transactions on Vehicular Technology, vol. 61, no. 9, pp. 4170-4175, Nov. 2012.
ETRI, “ETRI technical PHY proposal for IEEE 802.15 TG8 PAC standard,” DCN: IEEE 802.15-15-13-0373-01-0008, July 2013.