## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Frame Structure Supporting Multi-hop Communications for PAC]
Date Submitted: [12 March 2014]
Source: [Hongkun Li, Zhuo Chen, Qing Li, Chonggang Wang, Tao Han]
Company [InterDigital Communications Corporation]
Address [781 Third Avenue, King of Prussia, PA 19406-1409, USA]
Voice:[610-878-5695], FAX: [610-878-7885], E-Mail:[Qing.Li@InterDigital.com]
Re: [ Call for Preliminary Contributions]
Abstract: [This document presents frame structures including multi-hop communication on the PHY/MAC system design for 802.15.8 TG]
Purpose: [To discuss technical feasibility of the proposed frame structures for multi-hop communication for 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
It’s essential to develop a frame structure to fully support multi-hop operation at MAC, especially for distributed and infrastructure-less P2P networks (P2PNWs).
Requirement in 802.15.8 TGD [1]:
  5.2 Common communication mode: Common mode (e.g., for discovery and communication) shall be supported for interoperability.
  6.11 Multi-hop Support: IEEE 802.15.8 shall provide at least 2-hop relaying function. Only relay-enabled PD shall relay discovery messages and/or traffic data from PDs in the proximity.
Requirement in 802.15.8 PFD [2]:
  5.14 Multi-hop Operation: To extend the coverage of a PD or group members, a PD or group members relay received data to the destination PD or group members.

## Slide 3: Introduction
Existing frame structures in IEEE 802.11 and 802.15 standards to support multi-hop communication:
  802.11
    Contention free period and contention access period.
    Contention based access is simple but cause too many collisions to those P2PNWs with high density of PDs for both one-hop and multi-hop communication.
  802.15.4
    Most frame structures in 802.15.4 support only one-hop communication. Not suitable for multi-hop communication for distributed and infrastructure-less P2PNW.

## Slide 4: Proposal
To reduce the impact on one-hop communication, which may be required by many use cases in PAC.
To reduce the contention and potential collision among different hops, especially for those high data rate and high QoS applications.
To introduce more flexibility of frame formation for distributed P2PNW.
Propose to insert a dedicated multi-hop period in superframe to support the multi-hop communication.

## Slide 5: Terms and Concepts
PD: Peer Device
Hopper: In the context of multi-hop, a PD that relays or hops a message/messages or data to the other PDs in proximity to extend the radio coverage.
End PD: In the context of multi-hop, a PD that does not relay or hop any message or data to the other PDs in proximity.
Initiator: The first PD to initiate the first service or application in proximity or the first PD to initiate a service or application in proximity.

## Slide 6: Frame Structure 1 Supporting Multi-hop Communication
A Superframe consists of :
  Superframe Beacon is to indicate the start of a superframe and define the superframe structure
  Superframe (SF) Common Period follows the Superframe Beacon, and is shared through contention based access
  One-hop Period contains a frame or multiple frames
  Multi-hop Period is dedicated for multi-hop P2P communications
  Inactive period as the gap or guard time between Superframes

## Slide 7
An Example of Frame Structure 1 Supporting Multi-hop

## Slide 8: Frame Structure 2 Supporting Multi-hop Communication
A Superframe consists of :
  Superframe Beacon to indicate the start of the Superframe
  Superframe (SF) Common Period after the Superframe Beacon for inter-P2P communications
  A Frame or Frames for P2P communications, consisting of One-hop Period and Multi-hop Period
  Inactive period as the gap or guard time between Superframes

## Slide 9
An Example of Frame Structure 2 Supporting Multi-hop

## Slide 10: Conclusion
To reduce the impact of multi-hop communications on one-hop communications, as well as the potential collisions, we propose 2 frame structures to support multi-hop communications for PAC:
  Proposed frame structure 1: a dedicated multi-hop period is inserted at the end of a superframe, to support communications between hopper and its PDs, and/or among its PDs.
  Proposed frame structure 2: a dedicated multi-hop period is inserted at the end of a frame, to support communications between hopper and its PDs, and/or among its PDs.

## Slide 11
References
  [1] PAC TGD: 15-12-0568-08-0008-tg8-technical-guidance-document
  [2] PAC PFD: 15-14-0085-01-0008-tg8-pac-framework-document