## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Reliable Multicast for PAC]
Date Submitted: [12 March 2014]
Source: [Tao Han, Chonggang Wang, Qing Li, Hongkun Li, Zhuo Chen]
Company [InterDigital Communications Corporation]
Address [781 Third Avenue, King of Prussia, PA 19406-1409, USA]
Voice:[610-878-5695], FAX: [610-878-7885], E-Mail:[Qing.Li@InterDigital.com]
Re: [ Call for Preliminary Contributions]
Abstract: [This document presents reliable multicast schemes for 802.15.8 TG]
Purpose: [To discuss technical feasibility of the proposed reliable multicast schemes for 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Requirements
Excerpts from IEEE 802.15.8 TGD [1]:
  6.9 Multicast: “IEEE 802.15.8 may support a reliable multicast transmission including both one-hop and multi-hop cases.”
Excerpts from IEEE 802.15.8 PFD [2]:
  5.6.2 Multicast: “Multicast is a one-to-many data communication to a group or groups of PDs which may be addressed by multicast group ID(s).”

## Slide 3: Motivation
  Group communication is one of the key features required for PAC, which is not fully supported by the current IEEE 802.15.
There are many multicast PAC use cases (e.g., conference meeting), as described in Application Matrix.
PAC multicast reliability needs to be provided in an efficient way.

## Slide 4: Terms and Concepts
Reliable Multicast
  To provide reliable data transmission in multicast from one PD to multiple or all PDs within proximity.

## Slide 5: MAC Multicast Use Cases (1/2)
Centralized One-Hop Multicast (e.g. Conference Meeting)
  The PD 1 controls all transmissions.
  Only PD 1 multicasts data.

## Slide 6: MAC Multicast Use Cases (2/2)
Distributed One-Hop Multicast (e.g. Group Chat)
  PDs manage themselves.
  PDs can directly multicast data.

## Slide 7: MAC Multicast Reliability Management (1/4)
Main Idea
  Using different ACK policies between the sender PD and receiver PDs to achieve multicast reliability in more efficient way.
  ACK Policy:
    All ACK: All PDs (i.e. receivers) need to send ACK.
    Any ACK: ACK is only required from any PD (i.e. receiver).
    Partial ACK: Only some PDs (i.e. receivers) send ACK.

## Slide 8: MAC Multicast Reliability Management (2/4)
All ACK Use Case: Conference Meeting
  PD 1-4 have an important conference meeting.
  PD 1 is the speaker who multicasts data to PD 2-4.
  PD 2-4 are required to send ACK to PD 1 to acknowledge receiving the multicast data.
  PD 1 multicasts new data only after receiving all ACKs from PD 2-4.

## Slide 9: MAC Multicast Reliability Management (3/4)
Any ACK Use Case: Data Backup (Caching)
  PD 1-4 are a group of PDs running a data backup/caching application.
  PD 1 aims to backup its data in one of the PDs in its group.
  Any PDs in group can send an ACK to PD 1 to confirm the data backup.
  PD 1 multicasts new data as long as receiving one ACK from PD 2-4.

## Slide 10: MAC Multicast Reliability Management (4/4)
Partial ACK Use Case: Personalized Advertisement
  PD 1 multicasts its advertisement to a group of targeted customers, PD 2-5.
  PD 1 aims to ensure at least 50% of its targeted customers receive the advertisement.
  1 or more PDs in the group can send an ACK to PD 1.
  PD 1 multicasts new data only after receiving ACKs from at least 50% of the PDs.

## Slide 11: Conclusion
Reliable Multicast Use Cases
  Centralized one-hop multicast
  Distributed one-hop multicast
MAC Multicast Reliability Management
  All ACK mechanism
  Any ACK mechanism
  Partial ACK mechanism

## Slide 12: References
  [1] PAC TGD: 15-12-0568-08-0008-tg8-technical-guidance-document.
  [2] PAC PFD: 15-14-0085-01-0008-tg8-pac-framework-document.