## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Power Control for PAC]
Date Submitted: [12 March 2014]
Source: [Qing Li, Chonggang Wang, Hongkun Li, Zhuo Chen, Tao Han]
Company [InterDigital Communications Corporation]
Address [781 Third Avenue, King of Prussia, PA 19406-1409, USA]
Voice:[610-878-5695], FAX: [610-878-7885], E-Mail:[Qing.Li@InterDigital.com]
Re: [ Call for Preliminary Contributions]
Abstract: [This document proposes power control schemes for 802.15.8 TG]
Purpose: [To discuss technical feasibility of the proposed power control schemes for 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Context-aware Power Control

## Slide 3: PAC Requirements
Excerpt from IEEE 802.15.8 PFD [1]
  5.12 Interference management: Interference among multiple links is managed by the threshold level.
  5.13 Transmit power control: A PD may perform transmit power control based on channel measurement status.
Excerpt from IEEE 802.15.8 TGD [2]
  6.7 Interference Management: IEEE 802.15.8 shall provide the functionality to mitigate interference from other PDs.
  6.8 Transmit Power Control: IEEE 802.15.8 shall support the functionality for PDs to control the transmit power to minimize interference and power consumption.

## Slide 4: Conventional Power Control
  Open-loop or closed-loop power control based on path-loss.
  Provide similar QoS to all the UEs in the cell no matter what kind of applications or services that the UEs are engaged, i.e. chat on social network, or video conference.
Increase power
Decrease power
UE1
UE2

## Slide 5: Context-aware Power Control
  Different applications or services [3] require different power control schemes
         Application-aware or Context-aware

## Slide 6: Inter-P2PNWs Power Control
  Many P2P networks (P2PNWs) coexist within a short radio range of each other without a central controller to manage the transmission power among the P2PNWs, therefore inter-P2PNWs power control is needed.
    For examples:
    What’s the initial transmitting power for a PD when it enters the proximity?
    Is the “Video Conference Meeting” too loud to affect the other P2P communications in proximity?
    What’s the transmitting power that a PD may use if participates in “Chatting” as well as “Gaming”.

## Slide 7: Examples of Context and Power Control Information
Application | Context Info | Power Control Info
Video Conf. Meeting | Service Power Category: e.g. Cat1 – very high data rate & low error rate QoS: 1-to-N group based -- guaranteed or best effort to all PDs Service Range: medium | Max. Tx Power: medium Power Control Interval: long Measurements at Rx: SINR, CQI, etc. Info from Tx: Tx power level, location, etc.
Gaming | Service Power Category: e.g. Cat2 - high data rate & low error rate QoS: distributive group based -- guaranteed to all PDs Service Range: small | Max. Tx Power: medium Power Control Interval: long Measurements at Rx: SINR, CQI, etc. Info from Tx: Tx power level, location, etc.
Chat | Service Power Category: e.g. Cat3 - low data rate & high error rate QoS: average | Power Control Interval: medium Measurements at Rx: SINR, RSSI, etc. Info from Tx: Tx power level, speed, etc.
Keep Alive | Service Power Category: e.g. Cat4 - very low data rate & high error rate QoS: low | Measurements at Rx: RSSI, etc. Info from Tx: Tx power level, speed, etc.

## Slide 8: Context-aware Power Control for PAC

## Slide 9: Conclusions
Context-aware
  Different P2PNWs, formed for different applications or services, conduct different Power Control schemes optimized with different Context and Power Control Information (CPCI).
Co-existence
  Optimized the transmitting power level not only for the individual transmitter or receiver, but also for over all P2PNWs in proximity, i.e. inter-P2P power control to reduce interference to other PDs in proximity.
Infrastructure-less
  No central controller to specify the initial power level and the max. power level, etc.
     CPCI detection in proximity
     Cooperation among PDs in proximity, i.e. Inter-P2PNWs power control

## Slide 10: References
[1] PAC Framework Document (PFD) 15-14-0085-01
[2] Technical Guidance Document (TGD) 15-12-0568r9
[3] Application Matrix 15-12-0684r0

## Slide 11: Thank You!
Any Questions?
 Qing.Li@InterDigital.com