## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Geometry Scenarios for OCC Application ]
Date Submitted: [March, 2014]
Source: [Yu Zeng]
[China Telecom]
Address [Beijing 100035, China]
Voice:[86-10-58552979], FAX: [86-10-58552979], E-Mail:[zengyu@ctbri.com.cn]
Re: []
Abstract: [Geometry Scenarios for Optical Camera Communication Application]
Purpose: [Contribution to IEEE 802.15.SG7a OCC]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15-14- 0164 -00-007a
Notes: doc.: IEEE 802.15-09-0117-00-0007
<month year>

## Slide 2
Geometry Scenarios for OCC Application
Geometry Scenarios for OCC Applications
    Indoor Office environment (small size)
    Indoor Hall environment (medium size)
doc.: IEEE 802.15-14- 0164 -00-007a

## Slide 3
    Indoor - Office environment (small size)
Office environment (small size)
Room geometry (5m x 3m x 2m)
Length x width x height
Transmitter location [3 0.8 2]
Receiver location [2 2 0.8]
Simulation for up to 3 bounces
Line of Sight vs Diffuse
Line of sight
Diffuse
doc.: IEEE 802.15-14- 0164 -00-007a

## Slide 4
    Indoor - Office environment (medium size)
Office environment (small size)
Room geometry (10m x 6m x 4m)
Length x width x height
Transmitter location [6 1.6 4]
Receiver location [4 4 1.6]
Simulation for up to 3 bounces
Line of Sight vs Diffuse
Line of sight
Diffuse
doc.: IEEE 802.15-14- 0164 -00-007a

## Slide 5: Comparison for geometry
Line of Sight (Bounce = 1)
  While double the room size, energy from 1 bounce drops 85% (95 to 14)
  Remark: Size of room geometry can affect received optical power
Diffuse (Bounce > 1)
  While double the room size, energy from diffuse drops 52% (46 to 22)
  Remark: Application employ diffuse links are less sensitive to geometry change.
doc.: IEEE 802.15-14- 0164 -00-007a

## Slide 6: Conclusions
Different geometry setup will affect optical signal.
Diffuse link are more robust compared with direct link.
doc.: IEEE 802.15-14- 0164 -00-007a