## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [CAU Contribution Proposal for IEEE 802.15.8]
Date Submitted: [Mar 12th, 2014]
Source: [Jeongseok Yu, Woongsoo Na, Hyoungchul Bae, Taejin Kim, Yunseong Lee, Juho Lee, Zeynep Vatandas, Hyunsoo Kwon, Changhee Han, Sungrae Cho, and Junbeom Hur]
Company [Chung-Ang University, Korea]
E-Mail:[jsyu@uclab.re.kr, wsna@uclab.re.kr, hcbae@uclab.re.kr, tjkim@uclab.re.kr, yslee@uclab.re.kr, jhlee@uclab.re.kr, zvatandas@uclab.re.kr, srcho@cau.ac.kr, jbhur@cau.ac.kr]
Re: [This is the original document]
Abstract: [Technical Proposal for IEEE 802.15.8]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Technical Proposal for IEEE 802.15.8
Jeongseok Yu, Woongsoo Na, Hyoungchul Bae, Taejin Kim, Yunseong Lee, Juho Lee, Zeynep Vatandas, Hyunsoo Kwon, Changhee Han, Sungrae Cho, and Junbeom Hur
Chung-Ang University

## Slide 3: Contributions of the Proposal on TGD
6.9. Multicast
  Multicast Group Management Technique
  Multicast Group ID Management Technique
  Reliable Multicast Protocol
6.11. Multi-hop support
  Multi-hop Multicast/Unicast Transmission without Heavy Loaded Routing Table
6.14. Security
  Infrastructure based Security Mechanism
  Infrastructureless based Security Mechanism

## Slide 4
Multicast Group Management

## Slide 5: Multicast Group Management
In order to multicast, each PD has same multicast group.
In this parts, we describes the multicast group management technique as the following:
  Finding/Joining/Leaving Multicast Group
  Device Group ID Creation
  Routing Table Creation/Management

## Slide 6: Finding/Joining Multicast Group (1/3)
A multicast group consists of two or more PDs with the same application type ID, application specific ID, application specific group ID, and device group ID.
A multicast group can be formed only if two or more PDs can recognize themselves.
Before a PD joins a multicast group, it has to find the multicast group within K-hop coverage.
  If the PD cannot find the group, then it finds the group periodically.
  In order to find a multicast group, a PD broadcasts an Advertisement Command Frame (ACF) after random timer Tj where the maximum TTL is set to K. Range of Tj is [0, Tjmax ].

## Slide 7: Finding/Joining Multicast Group (2/3)
If a PD receive the ACF,
  It stores the ACF in order to forward it to other PDs,
  It saves backward path in the routing table during expiration timer where is calculated by one-hop RTTand K if it is relay-enabled.
    Backward path: originator of the ACF, one-hop PD sending the ACF, Device Group ID & Application type ID & Application-specific ID & Application-specific group ID.
  It compares the receiving frame’s Device Group ID & Application type ID & Application-specific ID & Application-specific group ID with its own.
    If they all are same, it replies an ARCF (Advertisement Reply Command Frame) to the PD sending the ACF (Reply of the ARCF depends upon the MGNF explained in the following slide).
    If any of them is not same, it decrements the TTL of the ACF and forwards the ACF.

## Slide 8: Finding/Joining Multicast Group (3/3)
In order to limit the duplicate ARCF, PDs replying the ARCF multicast a Multicast Group Notification Frame (MGNF) after random time. (MGNF is explained detail in later section)
Then, the PD multicasting the MGNF replies source PD with an ARCF by using backward path.
A PD receiving both ACF and MGNF does not reply an ARCF.
A PD receiving the ARCF whose destination is not itself saves the route information of
      ID of the source PD sending the ARCF, ID of the one-hop PD sending the ARCF, Device Group ID, Application type ID, Application-specific ID, Application-specific group ID.
      Then, this PD is referred to as “FORWARDING PD.”
A PD receiving the ARCF whose destination is itself saves the route information same as FORWARDING PD.
  Then, this PD is referred to as “JOINED MULTICAST GROUP MEMBER.”

## Slide 9: Flow Chart - Join Scenario
PD 1
Group1
PD 2
Group1
PD 3
Group Join Request (Send ACF)
Group Join Request (Send ACF)
Group Join Reply (Send ARCF)
Send MGNF (Type = 0)
Group Join Complete

## Slide 10: Device Group ID Creation (1/2)
A multicast group is determined by application type ID, application specific ID, and application specific group ID.
Therefore, it is inefficient if transmitting all IDs in a frame and managing routing table.

## Slide 11: Device Group ID Creation (2/2)
Therefore, we propose a device group ID creation scheme.
  Device group ID should be unique and distributed by a PD sending the first ARCF in the group.
  The PD manages/updates group keys for secure and dynamic multicast group communications after authentication procedures described in security section.
  The PD generates device group ID based on its unicast ID.
  Since a PD’s unicast ID is unique, prefix concatenated by PD’s unicast ID is also unique.
Prefix | Unicast ID

## Slide 12: Multicast Group Notification Frame (MGNF) (1/6)
The purposes of MGNF are
  Limiting duplicate ARCF,
  Management of routing table,
  Notifying leaving multicast group,
  Device group ID creation,
  Request for unicast routing,
  Reply for unicast routing,
  Mobility support, and
  Local repair,
  Notification of removed routing entry.
  for relay-enabled PDs.
The MGNF has following eight notification types for above purposes.
0  Limiting duplicate ARCF
1  Management of routing table
2  Notifying leaving multicast
3  Device group ID creation
4  Request for unicast routing
5  Reply for unicast routing
  6  Mobility support
  7  Local repair
  8  Notification of removed routing entry
Notification Type

## Slide 13: Multicast Group Notification Frame (2/6)
Limiting duplicate ARCF (Notification Type=0)
  a PD receiving an ACF multicasts MGNF with notification type set to 0 with random timer Tj. Range of Tj is [0, Tjmax ]
  Although missing MGNF can increase duplicate ARCF, MGNFs are not retransmitted to avoid flooding.
  In this case, payload of MGNF contains source of the ACF.

## Slide 14: Multicast Group Notification Frame (3/6)
Management of routing table (Notification Type=1)
  Assumption: In order to reduce routing entries in the table, each PD maintains entries only for PDs that has exchanged ACFs and ARCFs in its routing table.
  Each PD in multicast group multicasts MGNFs periodically (with notification type set to 1. Range of random timer Tjis [0, Tjmax]
  Upon receiving a MGNF, a forwarding PD updates the entries of the originator of the MGNF and one-hop PD sending the MGNF in its routing table, and forward the MGNF.
  Upon receiving a MGNF, a non-forwarding PD updates the entries of the originator of the MGNF and one-hop PD sending the MGNF in its routing table, but does not forward the MGNF.

## Slide 15: Multicast Group Notification Frame (4/6)
Dst | …
A | …
D | …
E | …
G | …
I | …
Dst | …
A | …
D | …
G | …
I | …
Dst | …
A | …
D | …
E | …
G | …
Dst | …
A | …
D | …
E | …
G | …
I | …
Dst | …
A | …
D | …
E | …
I | …
Dst | …
A | …
D | …
E | …
G | …
I | …
Dst | …
A | …
D | …
E | …
G | …
I | …
Dst | …
A | …
E | …
G | …
I | …
Dst | …
D | …
E | …
G | …
I | …
E
A
B
C
F
G
D
H
I
<If every PD has member
destinations in the table>
Dst | …
A | …
Dst | …
D | …
Dst | …
E | …
Dst | …
G | …
I | …
Dst | …
A | …
D | …
Dst | …
E | …
G | …
Dst | …
E | …
G | …
E
A
B
C
F
G
D
Dst | …
E | …
Dst | …
E | …
I | …
H
I
<Proposed technique can reduce the routing table size>
We assume PDs A, D, E, G, and I are same multicast group.
A  D, E  G, G  I
40
16

## Slide 16: Multicast Group Notification Frame (5/6)
Detection and Routing Table Update for link breakage
  Suppose the link between A and B is broken.
  E does not receive MGNF from A.
  E is aware that the link is broken because A’s MGNF does not arrive before E’s routing table Expiration timer is expired.
  E then removes entry of A from E’s routing table.
E does not
forward MGNF
since E is not a
forwarding PD
Although I does not
update its routing
table for A, I’s multicast
data frame can be
transmitted to group
members
E
A
B
C
F
G
D
H
I

## Slide 17: Multicast Group Notification Frame (6/6)
  Device group ID creation
    Explained in the previous section
Notifying leaving multicast group
  Will be explained in later section
Request for unicast routing
  Will be explained in later section
Reply for unicast routing
  Will be explained in later section
Mobility support
  Will be explained in later section
Local repair
  Will be explained in later section
  Notification of removed routing entry
  Will be explained in later section

## Slide 18: Classification of MGNF types
Duplicate response to the MGNF may cause traffic implosion, so we divided nodes into two types
  ACK-enabled MGNF transmission (Notification type = 2, 3, 4, 5, 8)
    A source node transmitting a MGNF has to receive ACK frame.
  ACK-disabled MGNF transmission (Notification type = 0, 1, 6, 7)
    ACK frame is not required since MGNF with type 0, 1, 6, 7 does not need to be reliably transmitted.
    Without those, multicast group management can still work OK.

## Slide 19: How to reduce MGNF traffic
When a PD belongs to multiple multicast groups, it multicasts MGNF multiple times.
In order to resolve the above problem, a PD may set Destination Address field of MGNF as United Multicast Address (UMA).
The UMA unifies multiple different groups into a single one.
The UMA can reduce the MGNF traffic as the following slides.

## Slide 20: Creation and Management of Routing Table (1/3)
Whenever a relay-enabled PD receives ACF or ARCF, a routing entry is created in the routing table.
Also, the routing table is updated by receiving MGNF.
A routing table contains
  Destination address
  Next-hop address
  Expiration timer
  Number of hops
  Current_SN
  Device Group ID
  Last ACF reception time()

## Slide 21: Creation and Management of Routing Table (2/3)
If MGNF is transmitted periodically, the MGNF (notification type: 1) implosion problem can occurs.
In order to restrict the MGNF implosion problem, we use the UMA-address approach and we proposed adaptive MGNF transmission technique based on distance.
If the distance between nodes become longer (e.g., a node moves away from the networks), the MGNF transmission period get smaller since the link can be break.
The distance can be measured from received signal strength indicator (RSSI).
  (where denotes i-th PD’s RSSI from j-th PD)

## Slide 22: Creation and Management of Routing Table (3/3)
Start
Received MGNF (Type = 1)
no
yes
Source ID is in Routing Entry
Updates routing Entry and sets the TMGNF based on RSSI
End
yes
no

## Slide 23: Reducing # of Routing Entries
When a PD is full of routing entries due to memory constraints, it chooses to remove an entry with the lowest hop count from it in its routing table.
Then, it transmits a MGNF (Notification type : 8) to the chosen PD (the removed entry) and sets timer.
When the chosen PD receives the MGNF (Notification type : 8), it deletes the entry of the sender PD from its routing table, and tries to connect another member of the multicast group by sending an ACF.
If a PD receives the ACF, it replies with ARCF and creates a new link.

## Slide 24: Leaving Multicast Group
There are several reasons for a PD to leave from the network: (1) by its intention, (2) by mobility, (3) by limited resources.
If a PD wants to leave from a multicast group, it multicasts (within K-hop) a MGNF with notification type set to 2. A recipient of MGNF may send rekeying messages to valid group members for forward secrecy.
  Upon receiving the MGNF, a forwarding PD deletes the entry of the originator of the MGNF, and forward the MGNF.
  Upon receiving the MGNF, a non-forwarding PD deletes the entry of the originator of the MGNF, but does not forward the MGNF.

## Slide 25: Flow Chart - Leave Scenario
PD 1
PD 2
PD 3
Group Leave Request (Send MGNF (Type = 2))
Forward MGNF (Type = 0)
PD 1 Leave The Group
Reply ACK
Link Break

## Slide 26: Mobility Support for Multicast (1/4)
Previously, B was 2-hop away from A.
If B moves within the one-hop coverage of A, both of A and B are aware of each other within the one-hop by MGNF’s TTL and update their routing table.
Then, A or B sends a MGNF (notification type = 6) to C.
When C receives that MGNF, C is aware that A and B become closer.
  If C is a multicast group member, it does not do anything.
  If C is a forwarding PD, it deletes routing entries whose destination field is A and B.
B
A
A
C
B
Multicast Group Notification Frame
Move

## Slide 27: Mobility Support for Multicast (2/4)
Since expiration timer is proportional to the number of hops from the impaired PD, the closest multicast group member detects link breakage.
A PD starts local repair if it detects link breakage between multicast group members (due to expiration timer).
Then, the PD multicasts MGNF (notification type = 7) .
If PDs receiving the MGNF create routing entry of originator of the MGNF during Tw .
Then the PD performing local repair broadcasts an ACF within K-hop coverage.
Link
Break
PD
Disappear
Link
Break
Local
Repair
Start
Local
Repair
Start
Advertisement Command Frame

## Slide 28: Mobility Support for Multicast (3/4)
If a PD receiving the ACF then It compares the receiving frame’s Device Group ID & Application type ID & Application-specific ID & Application-specific group ID with its own.
  If they all are same, it finds entry the originator of the ACF in its routing table. And it found the entry then check the expiration timer.
  If the expiration timer is less than Tm then replies an ARCF to the PD sending the ACF. (Tm is threshold time to decide reply)
  In other case, the PD receiving the ACF does not reply.
  If any of them is not same, it decrements the TTL of the ACF and forwards the ACF.
Local repair &
merging groups.

## Slide 29: Mobility Support for Multicast (4/4)
Find/join procedure by using ACFs and ARCFs can help merging disjoint groups.
  If a PD in a group receives a ACF from different disjoint group with the same Device Group ID & Application type ID & Application-specific ID & Application-specific group ID, it can initiate merging process.
  The PD then replies to the ACF originator with ARCF.
  Then, these two disjoint groups are merged by Device ID Creation Scheme.
Local repair by using ACFs and ARCFs also can help merging disjoint groups.
  Each group member performs local repair periodically during TL (long duty cycle) in order to merge disjoint groups.

## Slide 30: Flow Chart - Local Repair
PD 1
PD 2
PD 3
PD 2 Disappear
Send ACF
Link is Broken
Reply ARCF
PD 1 detects the link broken (due to MGNF (Type = 1))
New Link is established

## Slide 31
Multicast/Unicast
With Multi-hop Support

## Slide 32: Multicast Data Transmission(1/2)
If a PD receives a multicast data frame, it has to decide forwarding the frame or not.
The PD receiving the multicast data frame compares the source address of the data frame and next-hop address entries of its routing table.
PD checks the next hop addresses in its routing table. If it finds
  one or more next-hop entries which not overlapped with the source address of the received frame and
  those next-hop entries have same device group ID with the received frame.
  Then, the PD forwards the incoming data frame to other PDs.
Otherwise, the PD do not forward the incoming frame.

## Slide 33: Multicast Data Transmission(2/2)
For the multicast data transmission, we have to know the following information from multicast data frame:
  Destination address
  Source address
  Originator address
  Sequence number
  Time To Live(TTL)
This information should be included in all multicast data frames.
Therefore, the header in multicast data frames should contain the followings.
Destination address | Source address | Originator address | Sequence number | Time To Live(TTL) | Payload

## Slide 34: Unicast Data Transmission
When a PD wants to unicast data frame, the PD finds routing entry of destination address in its routing table.
If the PD finds routing entry of destination address, the PD starts to unicast immediately.
If the PD does not find routing entry of destination address, the PD multicasts a MGNF (Notification type : 4) to group.
When the other PD receives the MGNF,
  It saves a backward route information in routing table during Tw
  It starts to find a routing entry of destination address in its routing table
If a PD receiving MGNG finds routing entry of destination address , the PD unicasts a MGNF (Notification type : 5) to the PD which wants to unicast.

## Slide 35: Prevention Loopback Problem (1/3)
PD prevents multicast/broadcast loopback problem by using SN (Sequence Number) of data frames.
A
C
B
A starts multicast/
broadcast with
K=4 and SN=1
E

## Slide 36: Prevention Loopback Problem (2/3)
When a PD forwards data with SN = n, the PD sets current_SN field in its routing table to n.
A
C
E
B
B sets current _SN=1,
decreases K, and
forwards frame.

## Slide 37: Prevention Loopback Problem (3/3)
If the receiving frame’s SN is not greater than the current_SN , the PD discards the frame.
A
C
B
E
C also sets
current_SN=1,
decreases K, and
forwards frame.
B receives data
with SN = 1 from C,
it discards frame and
does not forward.

## Slide 38
Reliable Multicasting

## Slide 39: Selective Group ACK technique for reliable multicast (1/2)
We propose a selective group ACK technique for reliable multicast to know whether the nodes receive multicast data frame fully or not.
When sender PD sends a multicast data frame, it chooses the groups to acknowledge the frame in the multicast group.

## Slide 40: Selective Group ACK technique for reliable multicast (2/2)
To avoid the feedback implosion problem, a sender forms groups of nodes in its routing table.
Then, the sender transmits multicast data frame including the information of the group which sends their Block ACK.
When the nodes in the group receive all multicast data frames successfully, they transmit Block ACK to the sender by notifying that they received all frames successfully.
If they did not receive any data frame or they did not receive it, they do not transmit Block ACK to the sender.

## Slide 41: Pre-ACK (1/2)
In order to satisfy full reliability, each PD has to receive ACK frame from all nodes in its routing table.
Suppose S has entry for A, A has entry for B, B has entry for C, C has entry for D, and D has entry for E.
Although A, B, C, D, and E is in one-hop range from S, total transmissions is 5
It will take a long time and cause
traffic congestion.
S
B
D
E
C
A
: Multicast Data Frame
: ACK

## Slide 42: Pre-ACK (2/2)
Pre-ACK
  If a PD overhearing a data sent by sender does not have the sender in its routing table, the PD sends pre-ACK to the PDs in the routing table.
  Pre-ACK includes
    Originator Address of Data
    Sequence Number of Data
    Address of Receiver
  If a PD receives pre-ACK, it creates an ACK table.
  If all receivers in the ACK table are acknowledged, the PD doesn’t forward the data.

## Slide 43
Security Mechanism for PAC

## Slide 44: Authentication
Process of verifying ‘who’ is at the other end of the link
Performed for devices (PAC_ADDR)
Achieved by authentication procedure based on the stored authentication key (AUTH_KEY) or by peering (entering a PIN)
Slide 44

## Slide 45: Authorization
Process of deciding if device X is allowed to have access to service Y
Trusted devices (authenticated) are allowed to services
Untrusted or unknown devices may require authorization based on interaction before access to services is granted
Authorization always includes authentication
Technically, key would be derived or given (established) to the authorized user
Slide 45

## Slide 46: Authorization
Device trust levels
Trusted device | The device has been previously authenticated, An AUTH_KEY is stored The device is marked as “trusted” in the device DB
Untrusted device | The device has been previously authenticated An AUTH_KEY is stored But the device is not marked as “trusted” in the device DB
Unknown device | No security information is available for this device This is also an untrusted device
Slide 46

## Slide 47: Security Modes
Security mode 1 (non-secure)
  When a PAC device is in security mode 1, it shall never initiate any security procedure
Slide 47

## Slide 48: Security Modes
Security mode 2 (service level enforced security)
  When a PAC device is in security mode 2, it shall not initiate any security procedure before a channel establishment request has been received or a channel establishment procedure has been initiated by itself
  Whether a security procedure is initiated or not depends on the security requirements of the requested channel or service
  Security mode 1 can be considered as a special case of security mode 2 where no service has registered any security requirements
Slide 48

## Slide 49: Security Modes
Security mode 2 (cont.)
  A PAC device in security mode 2 should classify the security requirements of its services using the following attributes
Authentication required | - Before connecting to the application, the remote device must be authenticated
Authorization required | - Access is only granted automatically to trusted PAC devices, or untrusted devices after an authorization procedure - Always requires authentication to verify that the device is the right one
Encryption required | - The link must be changed to encrypted mode, before access to the service is possible

## Slide 50: Security Modes
Security mode 3 (link level enforced security)
  When a PAC device is in security mode 3, it shall initiate security procedures before the channel is established

## Slide 51: Security Parameters
PAC_ADDR: PAC device address (unique for each device)
AUTH_KEY: used for authentication purposes
ENC_KEY: encryption key (for secure unicast)
GENC_KEY: group encryption key
RAND: frequently changing random or pseudo-random number made by the PAC device itself
Entity | Size
PAC_ADDR | xxx bits
AUTH_KEY | 160 bits
ENC_KEY | 128 bits
GENC_KEY | 128 bits
RAND | 128 bits
Entity | Size
PAC_ADDR | xxx bits
AUTH_KEY | 
ENC_KEY | 
GENC_KEY | 
RAND | 

## Slide 52: Flow Chart for Authentication
Authentication start
Already authenticated
Peering allowed
Peering
Authentication OK
Authentication fail
Link key (AUTH_KEY) available
no
no
no
fail
yes
yes
ok
yes

## Slide 53: Flow Chart for Authorization
Authorization start
Trusted
Create trust
Authorization OK
Authorization fail
Link key (AUTH_KEY) available
no
no
no
fail
yes
yes
yes
Creation of trust allowed?
yes
Authentication succeed?
Slide 53

## Slide 54: Authentication / Authorization Architecture
Infrastructureless architecture
Infrastructure architecture

## Slide 55: Infrastructureless Architecture
No coordinator or AAA (authentication, authorization, accountability) server
Using PIN (symmetric), or certificate (asymmetric) issued by the trusted third party
  Cf) Bluetooth pairing
Slide 55

## Slide 56: Key Derivation
PRF
PRF
PRF
PRF
PIN
PIN
AUTH_KEYAB
AUTH_KEYAB
ENC_KEY
ENC_KEY
Authentication
Encryption
Device A
Device B
During
peering
Slide 56

## Slide 57: PIN Establishment Issue
Offline establishment
  Not scalable
Online establishment
  Not secure in multi-hop environment
    Main-in-the-middle attack
    Replay attack
  E.g., Bluetooth authentication

## Slide 58: PIN Establishment Issue
E.g., Bluetooth Authentication
correspond to
AUTH_KEY
A
B
Pairing
Generate a random number
User A enters
User B enters

## Slide 59: PIN Establishment Issue
Bluetooth Authentication (cont.)
  Function and parameter
    : A 48-bit Bluetooth address
    : A 128-bit random number for generating
    : numeric password which must be shared between
    users who want to authenticate (≤ 128-bit)
    : 128-bit key is used to authenticate
    (corresponds to AUTH_KEY)
    : Hash function which takes , ,
    and generate

## Slide 60: Authentication without Infrastructure 1
Device-to-device connection
Security requirement
  Secure against MITM, replay attack by relaying nodes in multi-hop environment
PIN establishment
  E.g., TLS 1.0/1.2, …
  Out of scope of specification, but spec needs to suggest protocol options allowed

## Slide 61
Slide 61
A
B
Set
User A enters
User B enters
Set
Generate a random number
Secure PIN establishment
(out of specification scope)

## Slide 62: Authentication without Infrastructure 1
Device-to-device connection (cont.)
Function and parameter
  : A information of device B
  : A sequence number
  : 128-bit random number
  : Message integrity code

## Slide 63: Authentication without Infrastructure 2
Device-to-(devices in a specific group) connection
Security requirement
  Secure against MITM, replay attack by relaying nodes and a group manager in multi-hop environment

## Slide 64
Slide 64
A
G
GM
User A enters
User B enters
Set
Generate a random number
Set
B
Group member

## Slide 65: Authentication without Infrastructure 2
Device-to-(devices in a specific group) connection (cont.)
Function and parameter
  : A information of group G
  : A information of device A and B in common
  : A 128-bit random number
  : A sequence number
  : A temporary key shared by device A and B
  : Message integrity code

## Slide 66: Infrastructure Architecture
AAA (authentication, authorization, accountability) server
(Dynamic) Coordinator
  Intermittent connection to the AAA server
Using master key (symmetric) issued by the AAA server, or certificate issued by the AAA server
  Cf) IEEE 802.1x, Kerberos protocol
2G/3G/LTE
AAA server
Server for some services (e.g., advertising)
Authentication &
communication
flow
Communication
flow
coordinator
Slide 66

## Slide 67: Thank you