## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: LB93 Comment resolution for Transmission mask and Adjacent channel rejection level for CMB GFSK PHY
Date Submitted: Apr/20 , 2014
Source:
Kenichi Mori (mori.ken1@jp.panasonic.com), Panasonic; Shinsuke Hara (shinsukehara0122@gmail.com ), QoL-SN; Masahiro Kuroda (marsh@nict.go.jp), QoL-SN&NICT;
Abstract: PSD calculation result of GFSK PHY for 15.4n
Purpose: Clarification of PSD of GFSK Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Abstract
Proposal of transmission spectral mask for CMB GFSK PHY
Proposal of receiver interference rejection

## Slide 3: Background
As shown in the following comment in LB93, the draft 0 does not specify receiver interference rejection level for CMB GFSK PHY.
To fix this issue,
Transmission spectral mask should be specified first.
After that, receiver interference rejection for CMB GFSK should be specified considering the transmission spectral mask.
CID | Page | Sub- clause | Line | Comment | Proposed Change
149 | 25 | 21.2.4 | 9 | I don't see a specification for receiver interference rejection | Add (given requirements of 15-14-0081-01-004n)

## Slide 4
Discussion1
The commenter mentions DCN 14-81r1 to solve these issues, but it does not show receiver interference rejection for CMB GFSK PHY. Hence, referring to DCN14-81r1 is not enough to solve this issue.
A discussion is needed to fix this issue as shown here.

## Slide 5: Discussion2
Normalized frequency should be used to specify transmission spectral mask because CMB GFSK supports multiple data rates. Note: Normalized frequency = Actual frequency / Symbol rate
99% occupation bandwidth (99% OBW) should be considered to determine transmission spectral mask. 99% OBW (normalized frequency by symbol rate) around 1.1 (0.55x2) when modulation index = 0.5 around 1.8 (0.9 x2) when modulation index = 1.0 Note: BT of Gaussian filter = 0.7 => A single normalized frequency offset point (+/-1) is a good point to measure
Resolution bandwidth (RBW) should be determined to measure transmission spectral mask.
Transmission spectral mask should be determined based on the lowest data rate of each modulation index because the lower data rate mode has a bigger impact of the PLL synthesizer noise.
Receiver interference rejection level should be determined based on transmission spectral mask.

## Slide 6: Parameters Influencing Tx PSD
Example parameters influencing eye diagram are
PLL Synthesizer
VCO Phase noise
Charge pump noise
Delta-Sigma circuit noise (in case of fractional synthesizer)
PLL loop filter characteristics
etc.
Others
Parts to parts variation
Voltage variation
Temperature variation
etc.

## Slide 7: Discussion of Transmission Spectral Mask
RBW for transmission spectral mask should be less than 1/10 of the lowest symbol rate to get stable PSD for all data rates. => RBW = 5kHz (50kbps/10)
PVT (Parts-to-parts, voltage, temperature) variation should be considered from actual situation point of view.
10dB degradation of PVT variation is enough.
Red line:
Simulation result Blue dashed line: Rohde&Schwarz SMIQ
Simulation and measurement result (50kbps, Modulation index = 1.0)
w/ PLL synthesizer noise and implementation loss and w/o PVT variation
Based on this simulation model, transmission spectral masks are proposed in this document.

## Slide 8: Proposed spectral mask
RBW = 5kHz
Signal power within +/-1 is used as a reference level of transmission mask.
Orange colored polygonal curve is the proposed transmission spectral mask.
50kbps, mod index=1.0
100kbps, mod index=1.0
200kbps, mod index=1.0
100kbps, mod index=0.5
200kbps, mod index=0.5
Normalized frequency offset | Transmission mask
0 | Reference level (L1 dB)
+/-1 | L1-10 (dB)
+/- 2 | L1-35 (dB)
10dB
10dB

## Slide 9: Receiver Interference Rejection
Based on the previously proposed transmission spectral mask, receiver interference rejection is determined.
Channel bandwidth is 500kHz for all CMB GFSK mode.
Proposed transmission spectral mask is as below
RBW = 5kHz
Normalized frequency offset | Transmission mask
0 | Reference level
+/-1 | -10 [dB] (L1)
+/-2 | -35 [dB] (L2)
Normalized frequency
(Frequency / Symbol rate)
-2 -1 0 1 2
0
L1
L2
Data Rate [kbps] | 50 | 100 | 200
Main Ch/ Adjacent Ch | 28dB | 31dB | 14dB
Main Ch/ Alternative Ch | 28dB | 31dB | 34dB
Channel Leakage Power

## Slide 10: Needed Receiver Sensitivity Level
GFSK receiver sensitivity formula
Data rate [kbps] | 50 | 100 | 200
Modulation index | 1.0 | 0.5/1.0 | 0.5/1.0
Rx sensitivity [dBm] | -91 | -88 | -85
Noise power within a channel
k： Boltzmann constant 1.38e-23 J/K
T： Absolute temperature 290K
Bch： Channel bandwidth 500kHz
NF： Receiver NF 7dB
Data rate [kbps] | 50 | 100 | 200
Modulation index | 1.0 | 0.5 / 1.0 | 0.5 / 1.0
Needed SNR [dB] | 19 | 22 | 25

## Slide 11: Proposed Interference Rejection
Needed Desire and Un-desire signal ratio can be calculated as below based on the previously mentioned needed SNR and transmission spectral mask.
Data rate [kbps] | 50 | 100 | 200
Adjacent channel selectivity (D/U ratio) | 19-28dB = -9dB | 22-31dB = -9dB | 25-14dB = 11dB
Alternative channel selectivity (D/U比 ratio) | 19-28dB = -9dB | 22-31dB = -9dB | 25-34dB = -9dB
Proposed receiver interference rejection
Data rate [kbps] | 50 | 100 | 200
For Adjacent channel | 9dB | 9dB | -11dB
For Alternative channel | 9dB | 9dB | 9dB

## Slide 12: Proposed Text
20.2.4.X Transmit PSD mask
NOTE 1 - In the presence of additional regulatory restrictions, the CMB device has to respect both the regulatory requirements and the mask defined in this section. NOTE 2 - Transmit spectral mask figures in this subclause are not drawn to scale.
For all CMB GFSK transmission spectral masks, the interim transmit spectral mask shall have a 0dBr within +/-1 x symbol rate frequency range of the center frequency, a -10 dBr within a range of from 2 x symbol rate to 1 x symbol rate frequency apart from the center frequency, a -35 dBr at frequency offset apart from more than 2 x symbol rate frequency from the center frequency as shown in the figure 2XX,
where dBr is defined as relative power to measured average transmission power within +/1 x symbol rate frequency range of the center frequency.
The spectrum analyzer settings for this measurement shall be as follows: the resolution bandwidth is 5 kHz,
the video bandwidth is 5 kHz or greater, and the detector is RMS.
Normalized frequency
(Frequency / Symbol rate)
-2 -1 0 1 2
0 dBr
-10dBr
-35dBr
Figure 2XX
Instruction to technical editor: Add this new subclause at an appropriate place and assign the correct subclause number.
Instruction to technical editor: Assign an appropriate figure number for this figure.

## Slide 13: Proposed Text cont.
21.2.4.X Receiver interference rejection
The adjacent designated channels are those on either side of the desired designated channel that are closest in frequency to the desired designated channel. The alternate designated channel is more than one removed from the desired designated channel in the operational frequency band.
The adjacent channel rejection shall be measured as follows: the desired signal shall be a compliant CMB GFSK PHY signal, as defined in 21.2.2, of pseudo-random data at the center frequency of the desired channel. The desired signal is input to the receiver at a level 3 dB above the receiver sensitivity given in 21.2.4.3.
In either the adjacent or the alternate channel, an unmodulated carrier in the center of that channel is input at the following level relative to the level of the desired signal:
— The adjacent channel rejection shall be greater than or equal to 9 dB for 50 kbps and 100 kbps mode, and -11 dB for 200kbps mode.
— The alternate channel rejection shall be greater than or equal to 9 dB.
The test shall be performed for only one interfering signal at a time. The receiver shall meet the error rate criteria defined in 8.1.7 under these conditions.
Instruction to technical editor: Add this new subclause at an appropriate place and assign the correct subclause number.

## Slide 14: Annex

## Slide 15: Proposed spectral mask
100kbps, mod index=1.0
200kbps, mod index=1.0
-500 -300 -100 0 100 300 500 [kHz]
Channel bandwdith
500kHz
-1000 -600 -200 0 200 600 1000 [kHz]
Channel bandwdith
500kHz
Leakage power out of channel is smaller. Leakage power out of channel is larger.
Normalized frequency
Actual frequency