## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed operational scenarios of L2R networks for TG10 TGD
Date Submitted: May, 2014
Source: Soo-Young Chang (SYCA), Jaehwan Kim (ETRI), Sangjae Lee (ETRI), and Sangsung Choi (ETRI) Voice: +1 530 574 2741, E-maill: sychang@ecs.csus.edu
Re: [Subclause 7.1 of 802.15 TG10 TGD]
Abstract: In the TG10 TGD document, operational scenarios are to be included in Subclause 7.1. In the current TGD, 15-13-0753-14, some conflicts may exist between aspects from the scenario described in 7.1 and other TGD requirements. This document is prepared to propose TG10 scenarios which meet all requirements and fit better to real situations.
Purpose: To prepare the operational scenarios to be used for comparison of proposals for TG10.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: contents
Introduction
Requirements for scenarios from TGD, 15-13-0753-14
Proposed operational scenarios for TGD
Conclusions

## Slide 3: Introduction

## Slide 4: INTRODUCTION
Operational scenarios are to be included in the TG10 TGD, which can be used to evaluate/compare proposals with the common parameters and environments.
In this document,
  All requirements from the current TGD, 15-13-0753-14, to establish operational scenarios are identified and summarized.
  All parameters and features which can be applied for these scenarios are defined.
Several operational scenarios are proposed for various topologies and situations:
  Scenario A: Unicast
  Scenario B: Multicast
  Scenario C: Broadcast,
  Scenario D: Many-to-one
  Scenario E: Linear topology

## Slide 5: Requirements for scenarios from tgd, 15-13-0753-14

## Slide 6: REQUIREMENTS FROM TGD (from 15-13-0753-14 Clause 1)
The use of mesh network topologies
  Individual nodes have multiple neighbors within communication range
  Packets traverse the mesh in multiple hops between nodes.
  Packets can be forwarded through the mesh along a number of possible paths.
  Nodes make dynamic decisions of which neighbor to forward a packet to, based on knowledge of the current set of available paths, and metrics related to congestion and signal quality.
Low energy, constrained resource network devices
  Low data rates: less than 1 Kbps to over 27 Mbps with packet lengths up to 2047 octets in the low kbps range
  MAC layer design to optimize for very low duty cycle operation and extended sleep time: Even when more practical packet lengths and data rates are considered, the additional delays for synchronizing sleep cycles and multiple hops could easily result in end-to-end delays exceeding several seconds
  Due to the limited bandwidth of 802.15 networks, the use of broadcast and multicast for establishment and maintenance of bridging operation should be carefully considered, and minimized when possible.

## Slide 7: REQUIREMENTS FROM TGD (from 15-13-0753-14 Clause 4)
Support for multi-hop networks in linear topology for greatest range.
  Using 802.15.4g for one-to-many and many-to-one topologies. Supporting monitoring applications, with low duty cycle.
Support for commercial building automation, interior lighting control, street light control, and similar applications
  These applications have requirements for peer to peer topology (switches or sensors to lights). Many-to-one and one-to-many relationships are required, as well as multicast to support groups of lights. Linear topology is also required for strings of lights. There is sometimes a requirement for mobility to support hand-held controls. There is a requirement for relatively low latency (100mS) for direct manual control of lights.
Dynamic route reconfiguration
  Discovery and addition of new nodes
  Loss and recurrence of routes
  Support broadcast and multicast: one-to-many and many-to-one topologies with multiple concentrators
Support for “sleepy nodes”, “sleepy routers”, and low duty cycle routers
Routing between different PHYs

## Slide 8: REQUIREMENTS FROM TGD (from 15-13-0753-14 Clause 6)
Possible to merge an independent subnet into a larger network when connectivity between them becomes available, providing both are using similar operating parameters.
  It should be possible for a network to operate as a number of independent subnets in the event of failure of parts of the network.
The proposal should provide a method to relearn the network topology in response to changes in the presence of devices, changes in connectivity between devices and changes in the status and quality of the links between devices.
The proposal should not preclude the use of techniques such as receiver duty-cycling to reduce the power consumption of all devices in the network.
  The proposal shall support the use of sleeping end and sleeping routing devices.
It allows data with different properties to be treated differently by the routing algorithm.
  Such as latency-critical properties over lower-latency paths and higher-priority messages to be transmitted before lower-priority messages over the same link

## Slide 9: REQUIREMENTS FROM TGD (from 15-13-0753-14 Clause 6)
Multiple Entry and Exit points
  use of multiple ingress and egress points for data within the network to select the most appropriate entry/exit point for their communications with entities outside the network
Some definitions:
Proactive routing: table-driven routing by maintaining fresh lists of destinations and their routes by periodically distributing routing tables throughout the network
Reactive routing: on-demand routing by finding a route on demand by flooding the network with Route Request packets
Bridging: to allow two or more communication networks, or two or more network segments, to create an aggregate network, in the first two layers, below the network layer
Routing: to allow the networks to communicate independently as separate networks
Gateway: router or a proxy server that routes between networks,
protocol converters, which can operate at any network layer.

## Slide 10: Proposed Operational scenarios for tgd

## Slide 11: OPERATIONAL SCENARIO IN THE CURRENT TGD, 15-13-0753-14 (1)
  7.1 Scenario for performance requirements comparison
The following simplified scenario has been defined for the purposes of the Call for Preliminary Proposals (CfPP). As such, the scenario has locked down several aspects, some which may be in conflict with the requirements in the TGD. Proposers are reminded that proposals shall support all aspects of the TGD, even though the scenario to be used for comparison during the CfPP phase has tied some of those down. For the Call for Final Proposals (CfFP) a more extensive scenario(s) will be defined.
CfPP Scenario
Network Size & Formation
  PAN coordinator is at the center of the grid
  During CfPP use 11x11 and 33x33 node networks (99x99 will be added during CfFP)
  Assume ~static size of network
    Network has already been initialized and all nodes are on the network

## Slide 12: OPERATIONAL SCENARIO IN THE CURRENT TGD, 15-13-0753-14 (2)
  CfPP Scenario (cont’d)
Neighbor Range
  Nodes have visibility of 3 grid points from itself (neighbor consist of 28 nodes around the node)
  Packets are subject to loss through contention or collision
Traffic Pattern
  Max. of 1 packet at the PAN coordinator every sec. for upstream traffic
  127 byte packet lengths are to be used
  No Downstream or peer-to-peer (this will be specified for the CfFP)
  (for CfFP the PAN coordinator will send data to each node – specifying the size of packets in bytes and the rate in packets/sec)
Route Update
  A random terminal is going off the network every 5min and remains off the network for 10min
  Route updates every 1min for 11x11
  Route updates every 10min for 33x33

## Slide 13: TYPES CONSIDERED FOR PROPOSED OPERATIONAL SCENARIOS
Two types networks depending on areas/device densities
  Fixed areas with different device densities
  Fixed device density with variable areas due to the number of devices
Three types of information flow
  Upstream
  Downstream
  Both directions of up and down
Link failure rates considered for loss of a loss and addition of a new node
  They are related to link quality and energy detection information and congestion/contention.
Various types of devices:
  Origin, neighbors, and destination
  PAN coordinator and normal node
  Entry point and exit point
  Fixed device and mobile device

## Slide 14: COMMON FEATURES FOR PROPOSED OPERATIONAL SCENARIO (1)
Basic single PAN network structure
Consists of y x y nodes
A PAN coordinator located at the center of the network
Basic multiple PAN network structure
Consists of z x z single PAN networks
x
x
: Node of a PAN
: PAN network
: PAN coordinator: located at the center of the network
Data entry point
Data exit point

## Slide 15: COMMON FEATURES FOR PROPOSED OPERATIONAL SCENARIO (2)
Traffic pattern
  Thee Data rates: 1 kbps, 200 kbps, and 27 Mbps
  Three packet sizes: 31 octets, 255 octets, and 2047 octets
  Low duty cycle operation and extended sleep time: 100% (fully awake), 50%, 10% and 1%
  Support for “sleepy nodes”, “sleepy routers”, and low duty cycle routers
Packet size \ date rate | Packet length in time (sec) |  | 
 | 1 kbps | 250 kbps | 27 Mbps
31 octets | 0.248 | 0.00099 | 9.185x10-6
255 octets | 2.04 | 0.0082 | 75.56x10-6
2047 octets | 16.376 | 0.0655 | 606.52x10-6

## Slide 16: COMMON FEATURES FOR PROPOSED OPERATIONAL SCENARIO (3)
Signal quality
  Communication range: w m
  congestion and signal quality:
    Link failure rate (LFR) of each node: 10-1, 10-3, and 10-6
  The signal-to-noise ratio (SNR) on the indirect paths to concentrator is small enough for the other devices to consider taking an extra hop along a greater SNR link to get to the concentrator:
    using link quality and energy detection information
A latency-critical message and a high-priority message
  For each scenario, a latency-critical message and a high-priority message are to be tested.
  It allows data with different properties to be treated differently by the routing algorithm.
  Such as latency-critical properties over lower-latency paths and higher-priority messages to be transmitted before lower-priority messages over the same link

## Slide 17: COMMON FEATURES FOR PROPOSED OPERATIONAL SCENARIO (4)
Single and multiple Entry and Exit points
  For each scenario,
  for single entry and exit points
    entry point: first node of the first row
    exit point: last node of the last row
  for multiple entry and exit points
    entry points: first three nodes of the first row
    exit points: last three nodes of the last row
  use of multiple ingress and egress points for data within the network to select the most appropriate entry/exit point for their communications with entities outside the network

## Slide 18: COMMON FEATURES FOR PROPOSED OPERATIONAL SCENARIO (5)
Values applied for Variables
Parameter/description | variable | values
Distance between two nodes in a row (m) | x | 2, 5
Number of nodes in a row and column in a single PAN coordinator network | y | 11, 33, 99
Number of single PAN coordinator networks in a row of a multiple PAN coordinator network | z | 1, 3
Communication range of a node (m) | w | 10
Data rate (kbps) |  | 1, 200, 27000
Packet size (octets) |  | 31, 255, 2047
duty cycle of operation (%) |  | 100, 50, 10, 1
Link failure rate of a node due to poor signal quality |  | 10-1, 10-3, 10-6

## Slide 19: OPERATIONAL SCENARIO A UNICAST (PEER-TO-PEER)
Variables and values for parameters to be used
  Specified in table of the previous slide
Two cases applied for data entry and exit points
  Case for single entry point and single exit point: use one entry point and one exit point specified
  Case for multiple entry and exit points: use one entry point and exit point selected among three entry points and three exit points respectively
Two cases applied to mobile device as a node
  Case to consider a mobile device as a sender: an entry point is a mobile device.
  Case to consider a mobile device as a receiver: an exit point is a mobile device.
  To meet requirement for mobility to support hand-held controls

## Slide 20: OPERATIONAL SCENARIO B MULTICAST
Variables and values for parameters to be used
  Specified in table of the previous slide
Two cases applied for data entry and exit points
  Case for single entry point and single exit point: use one entry point and multicast to three exit points
  Case for multiple entry and multiple exit points: use one entry point selected among three entry points and multicast to three exit points
Two cases applied to a mobile device as a node
  Case to consider a mobile device as a sender: an entry point is a mobile device.
  Case to consider a mobile device as a receiver: an exit point is a mobile device.
  To meet requirement for mobility to support hand-held controls

## Slide 21: OPERATIONAL SCENARIO C BROADCAST
Variables and values for parameters to be used
  Specified in table of the previous slide
Two cases applied for data entry and exit points
  Case for single entry point: use one entry point and broadcast to all other nodes
  Case for multiple entry case: use one entry point selected among three entry points and broadcast to all other nodes
Two cases applied to a mobile device as a node
  Case to consider a mobile device as a sender: an entry point is a mobile device.
  Case to consider a mobile device as a receiver: an exit point is a mobile device.
  To meet requirement for mobility to support hand-held controls

## Slide 22: OPERATIONAL SCENARIO D MANY-TO-ONE
Variables and values for parameters to be used
  Specified in table of the previous slide
Two cases applied for data entry and exit points
  Case for multiple entry points and single exit points: use three entry points to send data to one exit point.
  Case for multiple entry and multiple exit points: : use three entry points to send data to one exit point selected among three exit points.
Two cases applied to a mobile device as a node
  Case to consider a mobile device as a sender: an entry point is a mobile device.
  Case to consider a mobile device as a receiver: an exit point is a mobile device.
  To meet requirement for mobility to support hand-held controls

## Slide 23: OPERATIONAL SCENARIO E LINEAR TOPOLOGY
Linear topology is also required for strings of lights.
Variables and values for parameters to be used
  Specified in table of the previous slide
Two cases applied for data entry and exit points
  Case for single entry point: use one entry point to send data to the first node of the last row of the network. This data packet is delivered to the right hand side neighbor node until it reaches to the exit point.
  Case for multiple entry points: select one entry point among three entry points and apply the same procedure for the single entry point case.
Two cases applied to a mobile device as a node
  Case to consider a mobile device as a sender: an entry point is a mobile device.
  Case to consider a mobile device as a receiver: an exit point is a mobile device.
  To meet requirement for mobility to support hand-held controls

## Slide 24: conclusions

## Slide 25: CONCLUSIONS
In this document, requirements to establish operational scenarios are identified from the current TG10 TGD, 15-13-0753-14.
Five operational scenarios are proposed for comparison of the future TG10 proposals:
  Scenario A for unicast (peer-to-peer)
  Scenario B for multicast
  Scenario C for broadcast
  Scenario D for many-to-one
  Scenario E for linear topology