## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [UWB PHY contribution to TG8]
Date Submitted: [5th May 2014 ]
Source: [Billy Verso, Michael McLaughlin]
Company: [DecaWave]
Address: [Adelaide Chambers, Peter Street, Dublin 8, Ireland]
Voice:[1353 1 6975030] Fax: []
E−Mail:[billy.verso “at” decawave.com, michael.mclaughlin “at” decawave.com ]
Re: [In response to call for contributions to TG8]
Abstract: [ Gives details of UWB PHY for TG8]
Purpose: [Material for discussion in IEEE 802.15 TG8]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: UWB PHY contribution to TG8
Previously proposed a BPM/BPSK IR−UWB PHY based on 4a as a good general purpose PHY option within the 15.8 standard with especial utility in applications that require fast and accurate range and location estimation
This contribution serves to
  Outline the elements of the BPM/BPSK PHY for incorporation into 15.8
  Recommend enhancements to improve the PHY performance
  Show how it sits with the OOK UWB PHY proposed in 15−3−0383
    shared common elements
    shared band plan
    low interference even when operating in same band

## Slide 3: Previous submissions
        IEEE 802.15−3−0278−02−0008−uwb−phy−proposal−to−tg8.pptx
Other related submissions
        IEEE 802.15−3−0383−01−0008−nict−impulse−radio−ultra−wideband−phy−proposal−to−ieee−802−5−8.pdf
        IEEE 802.15−3−0716−01−0008−merged−decawave−and−nict−ir−uwb−phy−proposal−to−ieee−802−5−8.ppt

## Slide 4: UWB PHY Recommendation for 802.15.8
        Doc 15−3−0278−02 details why we recommend a BPM/BPSK IR−UWB PHY based on 802.15.4a to TG8, in summary:
  This PHY meets the specified requirements and has all the necessary characteristics for peer−aware−communications.
    precision ranging support allows peer relative positioning
    immunity to multipath effects
    15 channels cover unlicensed UWB bands from 3 to 10 GHz
    low and high data rates depending on application needs
    efficient spectral usage
    modulation and coding combination close to ideal
    perfect channel sounding
    choice of complexity in receiver implementations
      coherent or non−coherent receiver
      a non−coherent receiver is possible with a simple energy detector
      systematic FEC − convolutional code, and, Reed Solomon code
  Low time to market as commercial implementations are available

## Slide 5: BPM/BPSK UWB PHY MAIN ELEMENTS
MAC FRAME
        UWB PHY Frame Structure:
PREAMBLE
PHR
PHY DATA PAYLOAD
SFD
MAC header
MAC payload
FCS

## Slide 6: Preamble and SFD

## Slide 7: PHR and Data Symbols
Represents 0
Guard interval 0
Represents 1
Guard interval 1
Posn 0
Posn 1
Posn 2
Posn 3
Posn 4
Posn 5
Posn 6
Posn 7
Symbol is split into 2 valid intervals (one for a ‘0’ and the other for a ‘1’)
And two guard intervals to provide protection for the multipath
Each valid interval is subdivided into possible hop positions. Here it is shown divided into 8, other possible divisions are 2 or 32.
Bursts are positioned in these according to a pseudo−random sequence.
The burst can consist of up to 512 pseudo−random pulses or chips. The burst shown here has 16 chips

## Slide 8: Convolutional Coding of Data and PHR
All data bits are encoded with the convolutional encoder
The systematic bit determines the burst position in the symbol (PPM)
The parity bit determines the polarity, i.e. whether or not entire burst is inverted
Represents 0
Guard interval 0
Represents 1
Guard interval 1

## Slide 9: Reed Solomon Encoding
  Applied to data payload only
    The PHR has a SECDED code for error detection and correction
  Bytes reshaped into sextets
  Every 55 sextets has 8 parity sextets added
  Shortened code used for less than 55 sextets

## Slide 10: BPM/BPSK UWB PHY – NEW ELEMENTS
The following new elements (wrt 4a) give improved performance and utility to the BPM/BPSK UWB PHY
  Alternative SFD sequences that give
    6 dB performance boost to 110 kbps data rate at 1% PER, and
    7 dB performance boost in 850 kbps data rate at 1% PER
  A wider set of preamble lengths allowing PSR selection to match data rate and application needs more closely
    64, 128, 256, 512, 1024, 1536, 2048, 4096
  Support for longer PHY data payload for PAC applications needing more throughput or longer messages
  Option to send PHR at 6.8Mbps
  Additional PRF options under consideration

## Slide 11: UWB PHY for 802.15.8
Two IR−UWB modulation schemes have been proposed to TG8
  a BMP/BPSK UWB PHY
  an OOK UWB PHY
These can be considered as complementary UWB operating modes that can sit together in the standard
  Doc: IEEE 802.15−3−0716−01−0008 describes their merger
Essentially:
  Sharing the same concatenated coding scheme
  Operating with a very low level of mutual interference due to having different pulse repetition frequencies and different preamble sequences
  Having a common band plan

## Slide 12: UWB PHY COMMON BAND PLAN
Notes:
Minimum 10 dB bandwidth shall be 400 MHz
For interworking between units that occupy less than the full band width available within a channel, the receiving device needs to know which of the mandatory frequencies are occupied by the transmitting device
It is expected that this will be specified by a channel index number and a single octet bitmap with a bit for each of the mandatory frequencies a to h.
Channel index | Lower band edge (MHz) | Upper band edge (MHz) | Max bandwidth (MHz) | Region | Comment | Available mandatory frequencies
1 | 4200 | 4800 | 600 | China | Low band in China | a
2 | 3100 | 4800 | 1700 | Europe, Korea | Low band in Europe and Korea | a,b,c
3 | 3400 | 4800 | 1400 | Japan | Low band in Japan | a,b,c
4 | 3100 | 5700 | 2600 | USA | Low band in USA | a,b,c
5 | 6000 | 9000 | 3000 | Europe, China | High band in Europe and China | d,e,f,g
6 | 7250 | 10250 | 3000 | Japan | High band in Japan | e,f,g,h
7 | 7200 | 10200 | 3000 | Korea | High band in Korea | e,f,g,h
8 | 6000 | 10600 | 4600 | USA | High band in USA | d,e,f,g,h
9 | 5925 | 7200 | 1275 | USA | Wideband in USA | d
MANDATORY FREQUENCY ALLOCATION (frequencies at which PSD is < 6 dB below max) |  |  | 
Index | Mandatory frequency (MHz) | Index | Mandatory frequency (MHz)
a | 3500 | e | 7500
b | 4000 | f | 8000
c | 4500 | g | 8500
d | 6500 | h | 9000

## Slide 13: BPM/BPSK UWB PHY Simulation Results Note: These all use the new proposed SFDs

## Slide 14: AWGN Performance:110kbps, 1GHz BW, 16MHz PRF
    10% PER Sensitivity : −105.5dBm 1% PER Sensitivity : −104.2dBm
    10% PER Range: 287m 1% PER Range: 245m

## Slide 15: AWGN Performance:110kbps, 500MHz BW, 16MHz PRF
    10% PER Sensitivity : −106.7dBm 1% PER Sensitivity : −105.6dBm
    10% PER Range: 250m 1% PER Range: 220m

## Slide 16: AWGN Performance:110kbps, 500MHz BW, 64MHz PRF
    10% PER Sensitivity : −106.6dBm 1% PER Sensitivity : −105.6dBm
    10% PER Range: 246m 1% PER Range: 220m

## Slide 17: AWGN Performance:850kbps, 500MHz BW, 16MHz PRF
    10% PER Sensitivity : −102.5dBm 1% PER Sensitivity : −101.2dBm
    10% PER Range: 150m 1% PER Range: 135m

## Slide 18: AWGN Performance:850kbps, 500MHz BW, 64MHz PRF
    10% PER Sensitivity : −102.7dBm 1% PER Sensitivity : −101.0dBm
    10% PER Range: 155m 1% PER Range: 130m

## Slide 19: AWGN Performance:6.8Mbps, 500MHz BW, 16MHz PRF
    10% PER Sensitivity : −94.2dBm 1% PER Sensitivity : −92.5dBm
    10% PER Range: 59m 1% PER Range: 48m

## Slide 20: AWGN Performance:6.8Mbps, 500MHz BW, 64MHz PRF
    10% PER Sensitivity : −94.0dBm 1% PER Sensitivity : −93dBm
    10% PER Range: 57.5m 1% PER Range: 51m

## Slide 21: Rx Level Sensitivity Test Results for actual silicon
These agree very well with the preceding Matlab Simulation results

## Slide 22: 15.4a SFD and Proposed SFD
15.4a Length 8 SFD:
0+0−+00−
Proposed Length 8 SFD for optional use at 6.8Mbps:
−−−−+−00
Proposed Length 16 SFD for optional use at 850kbps:
−−−−+−+−−++−−+00
15.4a Length 64 SFD: 0+0−+00−0+0−+00−−00+0−0+0+000−0−0−00+0−−0−+0000++00−−−+−++0000++
Proposed Length 64 SFD for optional use at 110kbps: −−−−−−−+−+−−−−−−+−−+−+−−+−−+−−+−−−++−−−+++−+−+−+−−−+−−+−−−−+++00

## Slide 23
    10% PER Sensitivity : 5.5dB better 1% PER Sensitivity : 8.5dB better
    10% PER Range: 153m vs 80m 1% PER Range: 140m vs 52m
4a SFD vs Proposed SFD:850kbps, 500MHz BW, 16MHz PRF

## Slide 24: 15.4a vs Proposed SFD:850kbps, 500MHz BW, 64MHz PRF
    10% PER Sensitivity : 5.5dB better 1% PER Sensitivity : 8.5dB better
    10% PER Range: 155m vs 83m 1% PER Range: 130m vs 52m

## Slide 25: Option to send PHR at 6.8 Mbps
For location applications data packets are often as small as 12 bytes long
At 6.8 Mbps this takes less time to transmit than the 19bit PHR at 850kbps
If the data rate is set to 6.8Mbps, then the channel can cope with 6.8Mbps
By using 6.8Mbps the packet will be shorter, increasing channel capacity and using less power
The receiver will not be able to select the correct data rate by looking at the PHR data rate bits
  But many, if not most, applications will always use the same data rate for all tags.
Short packets like this can be less than 0.25ms in duration
  This allows them to be sent at 6dBs or more higher power, doubling the range
  The peak to mean ratio of the 850kbps mode if significantly higher than the 6.8Mbps mode
  6dB higher power at 850kbps would violate the peak power regulatory limit but at 6.8Mbps it would not

## Slide 26: Conclusion
This contribution outlined the main elements of the BPM/BPSK UWB PHY, while previous submissions have shown that it gives excellent performance, with operational choices for range vs. data rate, and choices for implementation complexity
The BPM/BPSK UWB PHY has excellent properties for accurate message time−stamping allowing precision location and peer relative positioning
This contribution introduced new elements enhancing the performance of the BPM/BPSK UWB PHY
This contribution presented simulated and actual performance results for the proposed PHY
Finally this contribution also reiterated the merged elements between the BPM/BPSK and OOK modulation modes
<end>