## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: ETRI PHY Proposal for PAC
Date Submitted: May 5, 2014
Source: Kapseok Chang, Byung-Jae Kwak, and Moon-Sik Lee and Byung-Jae Kwak (ETRI)
Company: ETRI
Address: 218 Gajeong-ro, Yuseong-gu, Daejeon, 305-700, Korea
Voice: +82 42 860 1639 Fax: E-Mail: {kschang, bjkwak, moonsiklee}@etri.re.kr , bjkwak, moonsiklee}@etri.re.kr,
Re: TG8 PAC Call for Contributions (CFC), 15-14-0087-00-0008, Jan 23, 2014.
Abstract: This document presents a fully distributed, synchronized PHY proposal for PAC.
Purpose: Proposal and Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: ETRI PHY Proposal for PAC
May 2014
Kapseok Chang, Byung-Jae Kwak,
and Moon-Sik Lee

## Slide 3: PHY Proposal Overview
Supporting transmission mode
  Orthogonal Frequency Division Multiplexing (OFDM)
Providing more precise synchronization compared to IEEE 802.11 [1]
Supporting collision detection in receiving mode
Supporting frame timing-offset indication in receiving mode
Supporting contention-window indication in receiving mode
Supporting coexistence with other 2.4GHz and 5GHz
  Different presentation (IEEE 802.15-14-0249-00-0008)
Supporting data transmission rates up to 54 Mbps: up to 64QAM
Supporting physical-layer security
  Different presentation (IEEE 802.15-14-0252-00-0008)
Supporting discovery with spatial filtering
  Different presentation (IEEE 802.15-14-0133-00-0008)

## Slide 4: OFDM Parameters
Parameter | Value
Carrier frequency | 2.4 GHz, 5 GHz
Channel bandwidth | 20 MHz
FFT Size | 64
Number of data subcarriers | 48 (excluding dc)
Number of preamble subcarriers | 52 (excluding dc)
Number of pilot subcarriers | 4
OFDM sampling time | 0.05 us
Subcarrier frequency spacing | 312.5 kHz
Cyclic Prefix | 16ts = 0.8us
OFDM symbol duration | 4 us

## Slide 5: MAC Frame Structure
Synchronization interval [TBD]
Sync slot
  Providing timing reference, timing-offset indication (TOI), collision detection (CD), and contention-window indication (CWI)
Discovery slot
  Different presentation (IEEE 802.15-14-0254-00-0008)
Data slot (CAP, CFP)
  Different presentation (IEEE 802.15-14-0254-00-0008, IEEE 802.15-14-0249-00-0008)

## Slide 6: Sync Slot Format
Backoff slots
  see IEEE 802.15-14-0249-00-0008.
Preamble
  Consists of short training field (STF) and long training field (LTF).
  Preamble is used for automatic gain control (AGC), carrier sensing, packet detection, time/frequency synchronization, and channel estimation.
  Preamble is common regardless of any slot defined by MAC layer.
Timing-Offset Indication Field (TOIF)
  Contains timing offset information in order for receiving PD to acquire frame boundary, i.e. arrival time+timing offset.
  see IEEE 802.15-14-0249-00-0008.
Contention-Window Indication Field (CWIF)
  used for broadcasting current CW information of transmitter.
  see IEEE 802.15-14-0249-00-0008.
Collision Detection Field (CDF)
  used for detecting a collision caused by multiple PDs in physical layer.
  see IEEE 802.15-14-0249-00-0008.
Guard time
  TBD

## Slide 7: Preamble Format (1/4)
STF
  It is used for carrier sensing, AGC, packet detection, coarse time/frequency synchronization, and partial fine time/frequency synchronization.
  It consists of a set of 5 repetition signals (Ds), where D occupies 32 samples.
LTF
  It is used for final fine time/frequency synchronization and channel estimation.

## Slide 8: Preamble Format (2/4)
STF [2]-[5]
Base sequence
  Modified sequence
  V is set to be 1. The time-domain signal of an effective OFDM symbol is real, which make the complexity of a detector for fine synchronization low by a factor of 2 [4].
  The time-domain signal is inherently immune to carrier frequency offset [4].

## Slide 9: Preamble Format (3/4)
STF
  What is transmitted is signaled using the STF pattern as shown below
    Set (D,D,D,D,D) is configured in the beginning of the Preamble for each of sync slot, request to send (RTS), clear to send (CTS), and acknowledgement (Ack).
    Set (D,D,D,D,-D) is configured in the beginning of the Preamble for data packet.
  Specifically, the discovery indication subslot (see IEEE 802.15-14-0249-00-0008.) comprises the STF pattern (D,D,D,D,D) alone.
  If we perform carrier sensing based on single auto-correlation method with length 64 (corresponding to three Ds), carrier sensing performance can be improved by 6 dB compared to single auto-correlation method with length 16 (e.g. IEEE 802.11a), which is verified by simulation.

## Slide 10: Preamble Format (4/4)
Slide 10
LTF [2]-[5]
Base sequence
  Modified sequence
  Z is set to be 25.
  The time-domain signal is inherently immune to carrier frequency offset [4].

## Slide 11: TOIF Format
Based on tone-hopping
  The code word (Z,Y,X,W) is mapped into the TO ID. Here, Z, Y, X, and W stand for the position indices of upper first-half, upper second-half, lower first-half, and lower second-half feasible subcarriers (N), respectively. Each of Z,Y, X, and W is in range of 0 to N-1.
  The maximum number of code words is N4.
  When the total number of TO IDs needed is less than the maximum number,
    code words shall be selected on the following criterion:
      Hamming distance ≥ 3

## Slide 12: CWIF Format
Based on tone-hopping
  The code word (Z,Y,X,W) in the 1st symbol is mapped into a part of the TO IDs. Each of Z,Y,X, and W is in range of 0 to N-1.
  The code word (Z’,Y’,X’,W’) in the 2nd symbol is mapped into the remaining part of the TO IDs. Each of Z’,Y’,X’, and W’ is in range of 0 to N-1.
  The maximum number of code words is N8.
  When the total number of TO IDs needed is less than the maximum number,
    The 1st code words shall be selected on the following criterion:
      Hamming distance ≥ 3
    The 2nd code words shall be selected on the following criterion:
      Hamming distance ≥ 3

## Slide 13: CDF Format
Based on random 4-tone [4]
  A PD who wants to transmit data using Random Access selects four random subcarriers, one from each group of subcarriers.
  The PD transmits a busy tone in the selected subcarriers in the CDF.
  When a receiver sees more than one tone in any of the groups of subcarriers, collision occurs.

## Slide 14: PPDU Format
Preamble/CWIF/CDF
  same as that in sync slot.
Header
  used for describing the content of the packet data as well as the protocol used to transfer it.
  employing one robust MCS to guarantee reliable reception
PSDU Field
  used for the information intended for the receiver
  employing diverse MCSs to support scalable data rates
Beam Jitter (BJ) Field
  used for Look and Link (LnL)
  see IEEE 802.15-14-0133-00-0008.

## Slide 15: Header
Bit-level scrambling
  Shall be specified.
  Specific method is TBD.
Channel encoding
  Convolutional encoder shall be specified.
  The specification of channel encoder is TBD.
Modulation schemes applied
  Spread BPSK (SBPSK)/Spread QPSK (SQPSK)
    TBD

## Slide 16: PSDU Field
Bit-level scrambling
  Shall be specified.
  Specific method is TBD.
Channel encoding
  Convolutional encoder shall be specified.
  The specification of channel encoder is TBD.
Supports data rates up to ~ 54 Mbps
  Modulation formats: SBPSK, SQPSK/BPSK, QPSK, 16-QAM, and 64-QAM
  Convolutional Coding: rates 1/2(base code rate), 3/4, 5/8
  MCS table corresponding to scalable data rates will appear in next slide.

## Slide 17: MCS Table
MCS index | Modulation | Code Rate | NBPSC | NCBPS | NIBPS | Data Rate (Mbps)
1 | SBPSK | 1/2 | 0.5 | 24 | 12 | 3
2 | SQPSK/BPSK | 1/2 | 1 | 48 | 24 | 6
3 | SQPSK/BPSK | 3/4 | 1 | 48 | 36 | 9
4 | QPSK | 1/2 | 2 | 96 | 48 | 12
5 | QPSK | 3/4 | 2 | 96 | 70 | 17.5
6 | 16-QAM | 1/2 | 4 | 192 | 96 | 24
7 | 16-QAM | 3/4 | 4 | 192 | 144 | 36
8 | 64-QAM | 5/8 | 6 | 288 | 180 | 45
9 | 64-QAM | 3/4 | 6 | 288 | 216 | 54
Info bits per OFDM symbol
coded bits per OFDM symbol
coded bits per subcarrier
* The above MCS sets are changeable according to ensuing evaluation result

## Slide 18: SBPSK/SQPSK Modulation and Mapping
Concatenated spreading:
Phase rotation to suppress peak-to-average-power ratio increasing caused by above spreading:
FYI, the data rate of MCS index 1 is identical to that of BPSK with code rate ¼. Since this new MCS is adopted, additional encoder and decoder are needed, which may make battery drain higher.

## Slide 19: Performance Evaluation
Preamble considered
  Preamble1 (P1): proposed preamble comprising STF and LTF, where STF pattern is [D,D,D,D,-D].
  Preamble2 (P2): proposed preamble comprising STF and LTF, where STF pattern is [D,D,D,D, D].
  Preamble3 (P3): 802.11a preamble, where STF pattern is [B,B,B,B,B,B,B,B,B,B].
  Preamble4 (P4): modified 802.11a preamble, where STF pattern is [B,B,B,B,B,B,B,B,-B,-B].
    Time and frequency synchronization (TFS) is performed by cross-correlation using [B,B,-B,-B] in this preamble, which is called cross-correlation based TFS (CCbTFS).
    This preamble is introduced in order to observe frequency immunity compared to P1 employing cross-correlation using [D,-D].
Synchronization acquisition scheme
  Frequency synchronization (FS) scheme applied
    Single auto-correlation based FS (ACbFS) method with length-16, -32, and -64
  Time synchronization (TS) scheme applied
    Product cross-correlation based TS (CCbTS) method: multiplication of CC out using STF and that using LTF

## Slide 20: Performance Evaluation
Performance measure and setting
  Detection error rate (DER) vs. Es/N0: If estimated sample time offset is out of ±4 samples, an error is declared.
  Mean carrier-sensing (CS) output vs. Es/N0: carrier-sensing output is normalized by 16.
  Collision probability vs. Es/N0(PD1): false alarm in the absence of PD2 and missing in the presence of PD2
  Frame Error Rate (FER) vs. Es/N0
  Peak to Average Power Ratio (PAPR) vs. Es/N0

## Slide 21: Performance Evaluation
Simulation parameters
Parameter | Value
Carrier frequency / bandwidth | 5 GHz / 20 MHz
FFT Size | 64
Number of data subcarriers | 48
Number of preamble subcarriers | 52
Number of pilot subcarriers | 4
OFDM sampling time | 0.05 us
Subcarrier frequency spacing | 312.5 kHz
Cyclic Prefix | 16ts = 0.8us
OFDM symbol duration | 4 us
Channel model: ETSI BRAN | Model A: Office → close to frequency non-selectivity Model E: Large open space indoor/outdoor large delay spread → close to frequency selectivity

## Slide 22: Performance Evaluation
DER vs. Es/N0
Channel model A applied

## Slide 23: Performance Evaluation
DER vs. Es/N0
Channel model E applied

## Slide 24: Performance Evaluation
Mean CS output vs. Es/N0
Channel model A applied

## Slide 25: Performance Evaluation
Mean CS output vs. Es/N0
Channel model E applied

## Slide 26: Performance Evaluation
Collision probability vs. Es/N0(PD1)
Channel model A applied

## Slide 27: Performance Evaluation
Collision probability vs. Es/N0(PD1)
Channel model E applied

## Slide 28: Performance Evaluation
FER vs. Es/N0 (Channel A)
PAPR vs. Es/N0 (Channel A)

## Slide 29: Performance Evaluation
FER vs. Es/N0 (Channel E)
PAPR vs. Es/N0 (Channel E)

## Slide 30: Conclusions
Providing more precise synchronization
Supporting collision detection
Supporting frame timing-offset indication
Supporting contention-window indication
Supporting data transmission rates up to 54 Mbps: up to 64QAM
Supporting coexistence with other 2.4GHz and 5GHz
Supporting physical-layer security
Supporting discovery with spatial filtering

## Slide 31: References
IEEE Std 802.11, “Part 11: Wireless LAN medium access control (MAC) and physical layer (PHY) specifications,” IEEE Computer Society, 2012.
K. Chang and Y. Han, “Robust replica correlation-based symbol synchronisation in OFDM systems,” Electronics Letters, vol. 44, no. 17, pp. 1024-1025, Aug. 2008.
K. Chang, P. Ho, and Y. Choi, “Signal design for reduced complexity and accurate cell search/synchronization in OFDM-based cellular systems,” IEEE Transactions on Vehicular Technology, vol. 61, no. 9, pp. 4170-4175, Nov. 2012.
ETRI, “ETRI technical PHY proposal for IEEE 802.15 TG8 PAC standard,” DCN: IEEE 802.15-13-0373-01-0008, July 2013.
ETRI, “Collision detection based PHY Proposal for PAC,” DCN: IEEE 802.15-14-0132-00-0008, March 2014.
ETRI and Samsung, “MAC proposal for PAC,” DCN: IEEE 802.15-14-0254-00-0008, May 2014.
ETRI and Samsung, “Performance Evaluation of Fully Distributed Synchronization Mechanism for PAC,” DCN: IEEE 802.15-14-0249-00-0008, May 2014.