## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Performance evaluation of CAU proposal]
Date Submitted: [May 05th, 2014]
Source: [Jeongseok Yu, Woongsoo Na, Hyoungchul Bae, Taejin Kim, Yunseong Lee, Juho Lee, Zeynep Vatandas, Hyunsoo Kwon, Changhee Han, Sungrae Cho, and Junbeom Hur]
Company [Chung-Ang University, Korea]
E-Mail:[jsyu@uclab.re.kr, wsna@uclab.re.kr, hcbae@uclab.re.kr, tjkim@uclab.re.kr, yslee@uclab.re.kr, jhlee@uclab.re.kr, zvatandas@uclab.re.kr, khs910504@hanmail.net, manjungs@gmail.com, srcho@cau.ac.kr, jbhur@cau.ac.kr]
Re: [This is the original document]
Abstract: [This documents include simulation result of multi-hop multicast protocol for IEEE 802.15.8]
Purpose: [To provide materials for discussion in 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Performance Evaluation
We proposed reliable multi-hop multicast protocol for PAC. (DCN: 446)
  Multicast group creation/management
  Routing table management
  Selective group ACK and pre ACK based reliable multicast protocol
To evaluate our multicast technique for PAC, we use the OPNET simulator under the one-hop scenario and multi-hop scenario.

## Slide 3: MAC Parameters Used in Simulations
Parameter | Value
ACF Frame Size | 32.75 bytes
MPDU | 512 bytes
MGNF Size | 48 bytes
Data Type | Multicast
Number of Groups | 1
Topology Size | Scenario 1,2 : 50m x 50m Scenario 3: 500m x 500m
PHY | BPSK (1/2)
Number of Channels | 1
General Parameters | TGD Revision 8
# of Nodes | 1~512

## Slide 4: MAC Parameters Used in Simulations
Parameter | Value
Data arrival Rate | Scenario 1: Full Buffer Scenario 2, 3: 2 Frames/sec per transmitter
Mobility | Static Mobility
Drop | 2-stage Drop
Data Rate | 10Mbps
Multi-hop | Supported
 | Multicast
RTS/CTS | Enable
NAV | Enable
ACK/NACK | Enable
CSMA/CA | Exponential increase of CW
Carrier Sensing | Enable
CWmin | 24
CWmax | 210
Retry Limit | 7

## Slide 5: Performance Metrics
Areal sum goodput (Mbps/km2): Total number of packets received by all PDs during 1second, expressed as bits per second per square-kilometer.
Reliability: The number of successful frames divided by the number of frames transmitted excluding retransmissions
Jain’s fairness index: Jain’s index for number of packets received by PDs.

## Slide 6: Simulation Scenarios
Scenario 1:
  1 transmitter (it generates multicast data)
  Full-buffer
  All PDs are located in 1-hop range of transmitter.
Scenario 2:
  Multiple transmitter
  Inter arrival rate: 2 frames/sec (Poisson)
  All PDs are located in 1-hop range of transmitters.
Scenario 3:
  Multiple transmitter
  Inter arrival rate: 2 frames/sec (Poisson)
  All PDs uniformly distributed in 500m x 500m (multi-hop operation)

## Slide 7: Area Sum Goodput (Scenario 1)
No-ACK based scheme
achieves the best
performance.
(There is no collision in
this scenario)
In the proposed scheme,
ACK frame collision is
reduced.

## Slide 8: Reliability (Scenario 1)
In the proposed scheme,
ACK frame collision is
reduced. 
Reliability is improved.

## Slide 9: Fairness (Scenario 1)
Jain’s fairness index is almost 1
  The group-ACK scheme provides fairness receive within 1-hop PDs

## Slide 10: Area Sum Goodput (Scenario 2)
When a data frame collision occurs,
No ACK based scheme does not
retransmit
Proposed scheme achieve the best
performance (reduce ACK transmission)

## Slide 11: Reliability (Scenario 2)
Our scheme:
Best performance
No ACK-based:
No reliability support

## Slide 12: Fairness and Efficiency (Scenario 2)
Jain’s fairness index is almost 1
  The group-ACK scheme provides fairness receive within 1-hop PDs.

## Slide 13: Area Sum Goodput (Scenario 3)
Our protocol achieve the best
performance.
In multi-hop scenario, there are forwarding nodes, if they do not receive the frame successfully.
They do not forward frame
No-ACK based scheme’s
performance are lower than out scheme. If the number of nodes is increased, No-ACK based scheme’s performance is decreases because collision of data frame.

## Slide 14: Reliability (Scenario 3)
Proposed scheme achieve
the best performance in
a large number of nodes.

## Slide 15: Fairness and Efficiency (Scenario 3)
Jain’s fairness index is almost 1
  The group-ACK scheme provides fairness receive within 1-hop PDs.

## Slide 16: Conclusion
The proposed multi-hop multicast protocol provides the best goodput and reliability compared with No ACK based scheme.
All of PDs have same opportunity to receive multicast data. (i.e., the Jain’s fairness index is 1)