## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Frame Structure Supporting Multi-hop Communications for PAC]
Date Submitted: [5 May 2014]
Source: [Zhuo Chen, Hongkun Li, Qing Li, Chonggang Wang, Tao Han]
Company [InterDigital Communications Corporation]
Address [781 Third Avenue, King of Prussia, PA 19406-1409, USA]
Voice:[610-878-5695], FAX: [610-878-7885], E-Mail:[Qing.Li@InterDigital.com]
Re: [ Call for Final Contributions]
Abstract: [This document presents frame structures including multi-hop communications on the PHY/MAC system design for 802.15.8 TG]
Purpose: [To discuss technical feasibility of the proposed frame structures for multi-hop communications for 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction (1/2)
It’s essential to develop a frame structure to fully support multi-hop operation at MAC, especially for distributed and infrastructure-less P2P networks (P2PNWs).
Requirement in 802.15.8 TGD [1]:
  5.2 Common communication mode: Common mode (e.g., for discovery and communication) shall be supported for interoperability.
  6.11 Multi-hop Support: IEEE 802.15.8 shall provide at least 2-hop relaying function. Only relay-enabled PD shall relay discovery messages and/or traffic data from PDs in the proximity.
Requirement in 802.15.8 PFD [2]:
  5.14 Multi-hop Operation: To extend the coverage of a PD or group members, a PD or group members relay received data to the destination PD or group members.

## Slide 3: Introduction (2/2)
Existing frame structures in IEEE 802.11 and 802.15 standards for supporting multi-hop communications:
  802.11
    Contention free period and contention access period.
    Contention based access is simple but cause too many collisions to those P2PNWs with high density of PDs for both one-hop and multi-hop communications.
  802.15.4
    Most frame structures in 802.15.4 support only one-hop communications, which are not suitable for multi-hop communications for distributed and infrastructure-less P2PNWs.

## Slide 4: Proposals
Propose multi-hop frame structures with a dedicated multi-hop period.
  Proposed frame structure 1: a dedicated multi-hop period is inserted at the end of a Superframe.
  Proposed frame structure 2: a dedicated multi-hop period is inserted at the end of a frame.
Propose multi-hop frame structures with time reuse.
  Proposed frame structure 1: Tier based frames structure for inter-Tier time reuse.
  Proposed frame structure 2: Sector based Hopper-subframe structure for intra-Tier time reuse.

## Slide 5: Terms and Concepts
PD: Peer Device
Hopper: In the context of multi-hop, a PD that relays or hops a message/messages or data to the other PDs in proximity to extend the radio coverage.
End PD: In the context of multi-hop, a PD that does not relay or hop any message or data to the other PDs in proximity.
Initiator: The first PD to initiate the first service or application in proximity or the first PD to initiate a service or application in proximity.
Tier: Ring based divisions of two-dimensional space to guarantee peers in non-adjacent Tiers do not interfere with each other.
Sector: Angular divisions of Tiers to guarantee peers in non-adjacent sectors do not interfere with each other.
Hop Distance: The number of hops between two peers.

## Slide 6: Multi-hop Frame Structures with a Dedicated Multi-hop Period
Motivations:
  To reduce the impact on one-hop communication, which may be required by many use cases in PAC.
  To reduce the contention and potential collision among different hops, especially for those high data rate and high QoS applications.
  To introduce more flexibility of frame formation for distributed P2PNW.

## Slide 7: Frame Structure 1 Supporting Multi-hop Communication
A Superframe consists of :
  Superframe Beacon is to indicate the start of a Superframe and define the Superframe structure
  Superframe (SF) Common Period follows the Superframe Beacon, and is shared through contention based access
  One-hop Period contains a frame or multiple frames
  Multi-hop Period is dedicated for multi-hop P2P communications
  Inactive Period as the gap or guard time between Superframes

## Slide 8
An Example of Frame Structure 1 Supporting Multi-hop

## Slide 9: Frame Structure 2 Supporting Multi-hop Communication
A Superframe consists of :
  Superframe Beacon to indicate the start of the Superframe
  Superframe (SF) Common Period after the Superframe Beacon for inter-P2P communications
  A Frame or Frames for P2P communications, consisting of One-hop Period and Multi-hop Period
  Inactive Period as the gap or guard time between Superframes

## Slide 10
An Example of Frame Structure 2 Supporting Multi-hop

## Slide 11: Multi-hop Frame Structures with Time Reuse
Motivations:
  To increase the capacity of the network.

## Slide 12: Tier Based Frames Structure for Inter-Tier Time Reuse (1/2)
Divide the two-dimensional space into Tiers.

## Slide 13: Tier Based Frames Structure for Inter-Tier Time Reuse (2/2)
A PD transmits within its Tier-frame.
PDs in different Tiers that are far way can transmission simultaneously.

## Slide 14: Sector Based Hopper-subframe Structure for Intra-Tier Time Reuse (1/2)
Divide each Tier in to Sectors.

## Slide 15: Sector Based Hopper-subframe Structure for Intra-Tier Time Reuse (2/2)
A PD transmits within its Hopper-subframe.
PDs in different Sectors that are far way can transmit simultaneously.

## Slide 16: An example with Inter-Tier and Intra-Tier Time Reuse

## Slide 17: Simulation Result for Multi-hop Frame Structure with Time Reuse

## Slide 18: General Configuration
Topology:
  The Initiator is placed at the center of the area.
  Other PDs are randomly placed in the area.
Hopper selection:
  A PD selects the neighboring PD with minimum hop distance to the Initiator.
Forwarding model:
  A packet is forwarded to the destination via the shortest path.

## Slide 19: Simulation Parameter
Metrics:
  Network Throughput (number of packets received at all destinations)
Parameter | Value
Slot size | 1 ms
Packet size | 128 bytes
Simulation time | 100 seconds
Bandwidth | 10 MHz
Tx power | 20 dBm
Channel model (Path loss) | As specified in TG8 Technical Guide.

## Slide 20: Use Case 1: Advertisement

## Slide 21: Use Case 1 Configuration
Frame structure:
  Each Hopper and the Initiator get 1 slot to transmit in each Superframe.
Flow model:
  Only the initiator generates packets
  For each generated packet, random choose a PD in the network as the destination.
Traffic model:
  Constant Bit Rate (CBR) traffic and full buffer
Topology:
  Test Case 1: 150 PDs in 250*250 m2 area. (low PDs density in small area)
  Test Case 2 600 PDs in 500*500 m2 area. (low PDs density in large area)
  Test Case 3: 600 PDs in 250*250 m2 area. (High PDs density in small area)
  Test Case 4: 2400 PDs in 500*500 m2 area. (High PDs density in large area)

## Slide 22: Network Throughput: Use Case 1
Number of packets received during 100s
Test Case | No reuse | Inter-Tier Reuse only | Intra-Tier Reuse only | Inter and Intra Tier Reuse
1 | 2382.9 | 2492.78 | 4169.44 | 4466.72
2 | 511.28 | 771.74 | 1618.18 | 3104.22
3 | 1315.2 | 1337.96 | 2266.72 | 2335.14
4 | 286.32 | 440.92 | 918.96 | 1744.74
Observations:
  Multi-hop frame structure with time reuse increases the capacity of the network by
    Almost two times for smaller area networks
    6 times for larger area networks
  Sector based Intra-Tier time reuse performs better than Tier based Inter-Tier time reuse especially in smaller area networks.
  Tier based Inter-Tier timer reuse performs better in larger area networks.

## Slide 23: Use Case 2 (Emergency Service)

## Slide 24: Use Case 2 Configuration
Frame structure:
  Each PD gets 1 slot to transmit in each Superframe.
Flow model:
  Randomly choose 10 source and destination pairs.
Traffic model:
  Constant Bit Rate (CBR) traffic and full buffer
Topology:
  Test Case 1: 150 PDs in 250*250 m2 area. (low PDs density in small area)
  Test Case 2 600 PDs in 500 *500 m2 area. (low PDs density in large area)
  Test Case 3: 600 PDs in 250*250 m2 area. (High PDs density in small area)
  Test Case 4 2400 PDs in 500 *500 m2 area. (High PDs density in large area)

## Slide 25: Network Throughput: Use Case 2 (1/2)
Number of packets received during 100s
Test Case 1: 150 PDs in 250*250 m2 area
Test Case 2: 600 PDs in 500 *500 m2 area.
Observations:
  Multi-hop frame structure with time reuse increases the capacity of the network by
    Almost two times for smaller area networks
    5 times for larger area networks

## Slide 26: Network Throughput: Use Case 2 (2/2)
Number of packets received during 100s
Test Case 3: 600 PDs in 250*250 m2 area
Test Case 4: 2400 PDs in 500 *500 m2 area.
Observations:
  Sector based Intra-Tier time reuse performs better than Tier based Inter-Tier time reuse especially in smaller area networks.
  Tier based Inter-Tier timer reuse performs better in larger area networks.

## Slide 27: Conclusion
To reduce the impact of multi-hop communications on one-hop communications, as well as the potential collisions, we propose 2 frame structures to support multi-hop communications for PAC.
To increase the capacity of multi-hop communications, we propose to divide the two-dimensional space into several areas to achieve time reuse for multi-hop communications for PAC.

## Slide 28
References
  [1] PAC TGD: 15-12-0568-08-0008-tg8-technical-guidance-document
  [2] PAC PFD: 15-14-0085-01-0008-tg8-pac-framework-document
  [3] PAC: 15-14-0258-00-0008-Multi-hop-Frame-Structure-Document-for-Final-Contribution