## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Multi-hop Peering for PAC]
Date Submitted: [5 May 2014]
Source: [Tao Han, Chonggang Wang, Qing Li, Hongkun Li, Zhuo Chen]
Company [InterDigital Communications Corporation]
Address [781 Third Avenue, King of Prussia, PA 19406-1409, USA]
Voice:[610-878-5695], FAX: [610-878-7885], E-Mail:[Qing.Li@InterDigital.com]
Re: [ Call for Final Contributions]
Abstract: [This document presents Multi-hop Peering schemes for 802.15.8 TG]
Purpose: [To discuss technical feasibility of the proposed Multi-hop Peering schemes for 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
Multi-hop Peering is not specified in the current IEEE 802.15.
Excerpts from IEEE 802.15.8 TGD [1]
    6.4 Peering: “IEEE 802.15.8 shall support peering.”
    6.11 Multi-hop support: “IEEE 802.15.8 shall provide at least 2-hop relaying function.”, “Only relay-enabled PD shall relay discovery messages and/or traffic data from PDs in the proximity”
Excerpts from IEEE 802.15.8 PFD [2]
    5.14 Multi-hop operation: “To extend the coverage of a PD or group members, a PD or group members relay received data to the destination PD or group members. ”

## Slide 3: Definitions
CFP: Contention Free Period.
CAP: Content Access Period.

## Slide 4: Terms and Concepts
Peering [2]: “is the procedure to establish a link between a pair of PDs or links among multiple PDs discovered during the discovery procedure.”
Peering Update: is the procedure used for a PD to update peering information of an existing peering relationship with other PDs.
  De-peering [2]: “is the procedure to disconnect the link established by peering.”
  Device-level Peering: is the Peering relationship among different PDs at device level
  Application-level Peering: is the Peering relationship with the same application among different PDs
  User-level Peering: is the Peering relationship among users on same or different PDs.

## Slide 5: Multi-Hop One-to-One Peering (1/3)
Multi-Hop One-to-One Peering Use Case: Conference Meeting
  All PDs have Device-level Peering.
  PD A is the speaker and aims to do peering with PD B-D.
  PD A achieves peering with PD B using multi-hop one-to-one peering.
  PD R is the Hopper that relays the peering messages for PD A and PD B.

## Slide 6: Multi-Hop One-to-One Peering (2/3)
Multi-Hop One-to-One Peering in Transparent Mode
  PD A requests Peering with PD B.
  PD R forwards Peering Request and Peering Response without processing the MAC payload (i.e., transparent mode).
  PD R has Device-level Peering with PD A and B.

## Slide 7: Multi-Hop One-to-One Peering (3/3)
Multi-Hop One-to-One Peering in Proxy Mode
  PD A requests Peering with PD B.
  PD A and PD B do not want to reveal their ID to each other.
  PD R intercepts and processes Peering Request (i.e., proxy mode). PD R anonymize PD A’s ID in the Peering Request and send the request to PD B.
  PD R receives the Peering Response from PD B, anonymizes PD B’s ID in the Peering Response and forwards the responses to PD A.
  PD R has Device-level Peering with PD A and B.

## Slide 8: Multi-Hop One-to-Many Peering (1/2)
Multi-Hop One-to-Many Peering Use Case: Online Game
  All PDs have Device-level Peering.
  PD Z aims to join PD A-C to play the game.
  PD Z achieves the Application-level Peering with PD A-C using multi-hop one-to-many peering using PD R as an Hopper.
  PD R relays the Peering Request from PD Z, aggregates the Peering Responses from PD A-C, and forwards the aggregated response to PD Z.

## Slide 9: Multi-Hop One-to-Many Peering (2/2)
Multi-Hop One-to-Many Peering
  PD Z requests Application-level Peering with PD A - C.
  PD R multicasts the Peering Request to PD A-C.
  PD R aggregates the Peering Responses from PD A-C and forward to PD Z.
  PD R has Device-level Peering with PD A-C and PD Z.

## Slide 10: Multi-Hop Many-to-One Peering (1/2)
Multi-Hop Many-to-One Peering Use Case: Conference Meeting
  All PDs have Device-level Peering.
  PD A-C aims to join PD Z who is hosting a conference meeting.
  PD A-C achieves the Application-level Peering with PD Z using multi-hop many-to-one peering using PD R as an Hopper.
  PD R aggregates and relays the Peering Request from PD A-C, and multicasts the Peering Responses from PD Z to PD A-C.

## Slide 11: Multi-Hop Many-to-One Peering (2/2)
Multi-Hop Many-to-One Peering
  PD A-C requests Application-level Peering with PD Z.
  PD R aggregates the requests and forward the aggregated request to PD Z.
  PD R multicasts the Peering Responses from PD Z and forward to PD A-C.
  PD R has Device-level Peering with PD A-C and PD Z.

## Slide 12: Multi-Hop Peering Update
Multi-Hop Peering Update
  PD A requests Peering Update with PD B.
  PD R forwards Peering Update Request and Peering Update Response for PD A and PD B.
  PD R has Device-level Peering with PD A and B.

## Slide 13: Multi-Hop Peering Update Use Case
Multi-Hop Peering Update: Update Association Lifetime
  All PDs have Device-level Peering.
  PD B requests Peering Update with PD A to update association lifetime.
  PD R relays the Peering Update Request and the Peering Update Response for PD B and PD A, respectively.

## Slide 14: Multi-Hop De-Peering
Multi-Hop De-peering:
  PD A requests De-peering with PD B.
  PD R forwards De-peering Request and De-peering Response for PD A and PD B.
  PD R has Device-level Peering with PD A and B.

## Slide 15: Multi-Hop De-Peering Use Case
Multi-Hop Peering Update: Quit an Online Game
  All PDs have Device-level Peering.
  PD B plans to leave the proximity and requests De-Peering with PD A.
  PD R relays the De-Peering Update Request and the De-Peering Response for PD B and PD A, respectively.

## Slide 16: Multi-hop Peering Simulation

## Slide 17: Simulation Topology
100 PDs are randomly distributed in the green circle. The radius of the circle is 50 m.
The radius of the circle indicates the transmission range of a PD.
All PDs run the same application and aim to Peering with each other. The Peering includes both single hop Peering and multi-hop Peering.
The hopper is randomly selected from the candidate hoppers.

## Slide 18: Implemented Multi-hop Peering Mechanism
Multi-hop One-to-One Peering in Transparent Mode
Multi-hop One-to-Many with Aggregated Peering Requests and Responses

## Slide 19: Simulation Scenarios
Scenario | Channel Access Method | PD Arrival Time
Scenario 1 | CFP | Random from 1th to 20th Superframe
Scenario 2 | CFP | Simultaneous at 1th Superframe
Scenario 3 | CAP | Random from 1th to 20th Superframe
Scenario 4 | CAP | Simultaneous at 1th Superframe

## Slide 20: Performance Metrics
Peering Ratio: is the ratio of the associated PDs over the discovered PDs.
Peering Overhead: is the number of Peering related messages sent by PDs for the Peering.

## Slide 21: Simulation Parameters in Scenario 1 & 2
Parameter | Value
Slot size | 1 ms
Superframe length | 800 ms (800 slots)
Channel access method | CFP
CFP length | 120 ms (120 slots)
Simulation time | 96 seconds (120 Superframe length)
Bandwidth | 10 MHz
Tx power | 20 dBm
CFP allocation | One slot per PD per Superframe
Maximum num. of aggregated response | 10
Aggregation timer | 10 Superframe length
Multi-hop Peering timeout | 20 Superframe length
Single hop Peering timeout | 10 Superframe length

## Slide 22: Simulation Results in Scenario 1
Scenario 1: Average Peering Ratio
  Multi-hop Peering has higher Peering ratio than single hop peering.
  Peering Request and Response Aggregation reduces Peering Latency.
Multi-hop Peering can reach 100% Peering ratio while the Peering ratio of the single hop Peering is only less than 60%.
For multi-hop Peering, aggregating Peering requests and responses significantly reduce the Peering latency. For example, multi-hop Peering without aggregation saves 28 Superframes in reaching 90% Peering ratio.

## Slide 23: Simulation Results in Scenario 2
Scenario 2: Average Peering Ratio
Multi-hop Peering can reach almost 100% Peering ratio while the Peering ratio of the single hop association is only less than 60%.
Multi-hop Peering with aggregation reduces the Peering latency. Within 10 Superframes, multi-hop Peering with aggregation associates with more 90% PDs while without aggregation, the Peering ratio of multi-hop Peering is only about 40%.

## Slide 24: Simulation Results in Scenario 2
Scenario 2: Peering Overhead
  Peering Request and Response Aggregation reduces Peering overhead.
Multi-hop Peering with aggregation significantly reduces Peering overhead.
As the number of PDs increases, multi-hop Peering with aggregation has better scalability. As compared to the multichip Peering without aggregation, the num. of peering message of multi-hop peering with aggregation increases much slower as the num. of PDs increases.

## Slide 25: Simulation Parameters in Scenario 3 & 4
Parameter | Value
Slot size | 1 ms
Superframe length | 800 ms (800 slots)
Channel access method | CAP
CAP length | 200 ms (200 slots)
Backoff window | Random from 2 ms to 400 ms
Channel access priority | Peering Response (high); Relay Peering Request (medium); Peering Request (low).
Simulation time | 200 seconds (250 Superframes)
Bandwidth | 10 MHz
Tx power | 20 dBm
Maximum num. of aggregated responses | 10
Aggregation timer | 10 Superframe length
Multi-hop association timeout | 20 Superframe length
Single hop association timeout | 10 Superframe length

## Slide 26: Simulation Results in Scenario 3
Scenario 3: Average Peering Ratio
  Multi-hop Peering has higher Peering ratio than single hop peering.
  Peering Request and Response Aggregation reduces Peering Latency.
Multi-hop Peering can reach at most 70% Peering ratio while the Peering ratio of the single hop Peering is only around 40%. This is because the Peering Request timeout and retransmission owing to inefficient channel access and the packets loss caused by collisions.
Multi-hop Peering with aggregation saves 35 Superframes in achieving 60% Peering ratio.

## Slide 27: Simulation Results in Scenario 4
Scenario 4: Average Peering Ratio
Multi-hop Peering with aggregation allows a jump start when all PDs arrives the proximity.
Multi-hop Peering with aggregation saves about 90 Superframes in achieving 60% Peering ratio.

## Slide 28: Simulation Results in Scenario 4
Scenario 4: Peering Overhead
  Peering Request and Response Aggregation reduces Peering overhead.
Multi-hop Peering with aggregation significantly reduces Peering overhead.
As the number of PDs increases, multi-hop Peering with aggregation has better scalability. As compared to the multichip Peering without aggregation, the num. of peering message of multi-hop peering with aggregation increases much slower as the num. of PDs increases.

## Slide 29: Conclusion
Multi-Hop Peering
  Multi-hop one-to-one Peering: transparent mode, proxy mode, and hybrid mode.
  Multi-hop one-to-many Peering: the Peering requesting PD converges the Peering requests and the Hopper aggregates Peering Response. The convergent and aggregation processes reduce the Peering latency and overhead.
  Multi-hop Many-to-one Peering: the Hopper aggregates Peering Request and multicasts Peering Responses, and the Peering responding PD converges the Peering responses. The convergent and aggregation processes reduce the Peering latency and overhead.
Multi-Hop Peering Updates
Multi-Hop De-peering

## Slide 30: References
  [1] PAC TGD: 15-12-0568-08-0008-tg8-technical-guidance-document.
  [2] PAC PFD: 15-14-0085-01-0008-tg8-pac-framework-document.