## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Response to the call for preliminary proposal to TG10]
Date Submitted: [11 May, 2014]
Source: * [Verotiana Rabarijaona, Fumihide Kojima], †[Hiroshi Harada]
Company *[NICT], †[Kyoto University]
Address *[3-4, Hikarino-oka, Yokosuka, 239-0847 Japan], †[36-1 Yoshida-Honmachi, Sakyo-ku, Kyoto 606-8501 Japan]
Voice:[+81-46-847-5075], FAX: [+81-46-847-5089], E-Mail:[rverotiana@nict.go.jp]
Re: [Call for Preliminary Proposals.]
Abstract: [This contribution presents a preliminary proposal for the TG10.]
Purpose: [Preliminary proposal to TG10.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Hierarchical Mesh Tree Routing
Verotiana Rabarijaona, Fumihide Kojima (NICT), Hiroshi Harada (Kyoto University)

## Slide 3: Outline
This proposal includes the following features:
Hierarchical Mesh Tree formation, maintenance update
HMT Routing
High reliability
Data aggregation

## Slide 4: Typical Use cases
Smart metering
Environment monitoring
Structure monitoring
Parking monitoring

## Slide 5: Motivation
The current 802.15.4 builds a cluster tree topology
Data frames can only be sent between device and coordinator
Even when a routing protocol is applied from the upper layer, it is constrained at the MAC layer by the cluster tree topology
The D2D function in 15.4m allows devices associated to the same coordinator to send packets to each other directly but does not provide routing capability to distant nodes

## Slide 6: HMT formation
Each node is required to associate with a coordinator after performing an active or passive scan as described in Section 5.1.3.1 of IEEE Std 802.15.4-2011
Each node has a depth representing the distance of that node to the root of the tree (PAN coord) in number of hops
The depth of the root is 0
The depth of a coordinator is carried in the association response frame
After association, the depth of a node is initialized to the depth of its coordinator + 1.
Once associated, a node starts to broadcast enhanced beacons(EB) periodically

## Slide 7: HMT formation (2)
A node holds a neighbor table filled based on the information contained in the EBs
A neighbor is categorized according to its depth. If the depth of a node M is DM and the depth of a neighbor N is DN
  If DM > DN  N is a parent
  If DM = DN  N is a brother
  If DM < DN  N is a child
A node starts filling up its neighbor table only after association. It ensures that only nodes from the same PAN are recorded as neighbors
After the HMT formation, a node can join the network by performing an active or passive scan. The node shall associate with the neighbor with the lowest depth. After association, it fills up its neighbor table according to the other beacons received
Neighbor ID | Neighbor Depth | Metric 1 | … | Metric n

## Slide 8: HMT formation (3)
The HMT formation time is the time required to have every nodes of the network associated to the PAN
Example of a HMT
-1
-1
C
R-0
A
B
D
F
G
H
J
K
L
N
-1
-1
-1
I-2
-2
-2
-2
-2
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
Parent-child link
Brotherhood link

## Slide 9: HMT maintenance and update
The neighbor table is maintained through periodic beacon broadcasts
A node’s depth and the neighbor table is updated according to the changes in the network reflected by the presence/absence of beacons
If a node is disassociated to its coordinator, it either tries to re-associate or tries to associate with another parent in the neighbor table.
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
Parent-child link
Brotherhood link
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
Parent-child link
Brotherhood link

## Slide 10: HMT Routing (MP2P)
Link cost-based (BER, success rate, latency…)
Reactive routing through parents and/or brothers with priority given to the parents through a Link Cost Threshold (LCT) set by the PAN coord regarding the chosen metric and broadcast in EBs
A node holds the list of TAs and RAs of a packet with a given SN and SA. In order to avoid loops, a node shall select a next hop that is not in that list. The list shall be erased after a TBD time
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
8.67
3.03
10.71
3.89
5.51
6.34
6.8
11.12
7.15
1.6
5.81
3.12
4.72
8.34
9.4
6.28
5.24
1.21
10.67
3.5
7.65
0.61
0.21
4.05
3.58
0.66
4.09
1.22
LCT = 4
No LCT

## Slide 11: HMT Routing (P2MP)
When a node receives a packet to forward or a beacon, it fills a routing table
Example of routing table at R
A packet is routed through the next hop with the best metric
Destination | Next Hop | Metric 1 | … | Metric n
Node originating the frame, Src | Node from which I received the frame |  |  | 
Destination | Next Hop | SINR
A | A | 7.65
F | F | 0.61
… | … | …
F | A | 7.65
L | A | 7.65
M | A | 7.65
… | … | …
Entries from the beacons
Entries from data packets

## Slide 12: High reliability option
If the high reliability option is on, the AR field must be set to 1. If an acknowledgment is not received after a packet transmission, the packet is forwarded through another neighbor
R
A
B
C
D
E
I
J
L
G
H
K
F
M
N
Depth
0
1
2
3
8.67
3.03
10.71
3.89
5.51
6.34
6.8
11.12
7.15
1.6
5.81
3.12
4.72
8.34
9.4
6.28
5.24
1.21
10.67
3.5
7.65
0.61
0.21
4.05
3.58
0.66
4.09
1.22
MST = 4

## Slide 13: Data aggregation (1)
A node aggregates the packets collected from its neighbors with its own packet before forwarding them.
Reduce collisions
Reduce the bottleneck effect as we get closer to the root of the tree
The number of aggregated packets is limited by the maximum size of a frame

## Slide 14: Data aggregation (2)

## Slide 15: HMT Routing IE
Bit: 0 - 6 | 7 - 14 | 15 | Octets: Variable
Length | Element ID | Type = 0 (Header) | IE content
Octets: 0/2 | 0/2/8 | 0/2 | 0/2/8
Final Destination PAN ID (D) | Final Destination address (D) | Origin Source PAN ID (D) | Originl Source address (D)
Octets: 1 | 0/Variable | Bits: 0 | 1 | 2 | 3-6 | 7 | Octets: variable | … | Octets: variable
Depth | Addressing fields | High reliability (B - C) | Data aggregation (B - C) | Flow (0: Up, 1: Down) | Number N of metrics (B - C) | Reserved (B - C) | Metrics 1 (B -C) | … | Metrics N (B -C)
Bits: 0-3 | 4-7 | 0/Variable | 0/Variable
Metric ID | Metric Priority | Metric threshold | Metric value
B: field present in a EB
C: field present in a command (ex: association response)
D: field present in a data frame

## Slide 16: Data aggregation IE
Bit: 0-10 | 11-14 | 15 | Octets : variable
Length | Group ID | Type = 1 (Payload) | IE content
Bits: 0-3 | 6-7 | Octets: 1 | … | 1
Number N of aggregated packets | Reserved | Size of the aggregated packet 1 | … | Size of the aggregated packet N

## Slide 17: Preliminary results (1)
  Packet birth: 2 packets /s
  Packet birth: 2 packets/5s
 | No LCT | LCT = 3.0 | LCT = 7.0
E2E success ratio (%) | 49.209 | 58.948 | 76.037
Average E2E delay (s) | 0.020254 | 0.023117 | 0.03998
Average Number of hops | 2.142 | 2.501 | 4.430
 | No LCT | LCT = 3.0 | LCT = 7.0
E2E success ratio (%) | 99.290 | 98.948 | 98.753
Average E2E delay (s) | 0.017359 | 0.019462 | 0.039918
Average Number of hops | 2.101 | 2.356 | 4.683
Number of nodes: 11x11 | Simulator: Qualnet
Metric: SINR | 

## Slide 18: Preliminary results (2)
Number of nodes: 33 x 33
Metric: SINR
  Packet birth: 2 packets /s
  Packet birth: 2 packets/5s
 | No LCT | LCT = 3.0 | LCT = 7.0
E2E success ratio (%) | 49.851 | 58.000 | 80.959
Average E2E delay (s) | 0.051 | 0.059 | 0.113
Average Number of hops | 6.017 | 7.015 | 13.054
 | No LCT | LCT = 3.0 | LCT = 7.0
E2E success ratio (%) | 84.606 | 85.037 | 87.820
Average E2E delay (s) | 0.048 | 0.057 | 0.105
Average Number of hops | 5.627 | 6.588 | 12.451

## Slide 19
Thank you
Q/A