## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [SC Closing Report for May 2014 Session]
Date Submitted: [16 May2014]
Source: [Patrick Kinney] Company [Kinney Consulting LLC]
Address [Chicago area, IL, USA]
Voice:[+1.847.960.3715], E-Mail:[pat.kinney@ieee.org]
Re: [SC Closing Report for May 2014 Session.]
Abstract: [Closing Report for the May Session]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Meeting Goals (Agenda 15-14-0255-00)
Slide 2
SC Maintenance
  Monday 18 Mar, AM2: Review resolutions and mentor documents, including 15-14-224-03 comments
  Tuesday, 13 May, PM1:Revision drafting
  Thursday 15 May, AM1: 802.15.4 Revision drafting
  Thursday 15 May, AM2: 802.15.4 Approval of editing changes, seek approval for comment review and WG LB
  SC WNG
  No presentations
Notes: May 14
Page 2

## Slide 3: SC Maintenance Detailed Agenda
Slide 3
Monday 12 May, AM1:
  review timing issues and resolutions
  review 15-12-367-08 corrigenda
Tuesday, 13 May, PM1
  review 802.15.4 roll-up
  TG28 changes: slides 9 - 11
Thursday 15 May, AM1:
  Review editing
Thursday 15 May, AM2:
  802.15.4 Revision drafting: Approval of edits, approval to send draft out for comment review, approval from TG to LB draft after resolutions to comments from comment review
Notes: May 14
Page 3

## Slide 4: Timing Status
Document in progress (15-14-0111-00-0mag) lists all the attributes, constants and parameters that specify or affect specification of MAC timing.
  Color coded table - what it is and where it came from
    Red means serious issue probably can’t ignore
    Yellow means may need attention
    Blue means minor issues (editorial or other obvious fixes)
  To include discussion of the issues
    Problem statement (conflict, unclear, etc.)
    Proposed fixes (eventually)
Resolution
  Time previously represented as tack is now described as AIFS

## Slide 5: Method
Search standard for PIB attributes, constants and SAP parameters that may control or affect MAC timing
  802.15.4-2011
  802.15.4e-2012
  802.15.4f-2012
  802.15.4g-2012
  802.15.4j-2013.
  802.15.4k-2013
  802.15.4m-2014
  802-15-4p-2014
Examine definition and use of each
  Look for complex entanglements (dependencies or complex specs)
  Look for conflicts amongst amendments
  Consider history – what’s been confused and debated
Non-trivial task

## Slide 6: Red Zone
Acknowledgement Timing
  Complex, PHY specific definitions, some with mixed units
  Depends on a number of constants and other attributes that have been touched a lot
  Specified in more than one way in the standard
  Reference point for timers unclear
  When/if to use CSMA
    More than 4 different CSMA scenarios need addressing
LIFs and SIFs
  Suggestion to replace with single IFS specification
  Ripples a lot (including into Ack timing)
  Backwards compatibility issues?

## Slide 7: Yellow Zone
macResponseWaitTime
  Complex definition dependent on attributes and constants that have changed throughout amendments
  Should review to ensure still valid for all PHYs
macMaxFrameTotalWaitTime
  Complex definition dependent on a bunch of things
aBaseSlotDuration and aBaseSuperframeDuration
  Used a lot of places, needs review
aUnitBackoffPeriod and aCCATime
  Used in a number of places where it is maybe should not be;
  PHY specific but maybe should not be;
  Differing styles in amendments
  aUnitBackoffPeriod not changed by PHY amendments but maybe should have been?

## Slide 8: Blue Zone
PHY dependent timings (6.4.3): some things stated as UWB PHY dependent are really ALOHA dependent
macSyncSymbolOffset needs clean-up
Duty cycle control
  macTxControlActiveDuration, macTxControlPauseDuration and macTxTotalDuration
  Intended to provide control of transmit duty cycle
  Specification unclear (no MAC or PHY function uses them)
  macTxTotal Duration: should be read-only except can be reset (i.e. not any value written)
  No harm done?

## Slide 9: TG28 Changes ETSI TC ERM change requests
Slide 9
1) Frame ID Extension
SC-M agreed to recommend defining the last reserved Frame ID value (0b111) to indicate an Extended Frame ID format consisting of 5 additional bits (total 8-bit Frame ID). IEEE will manage the assignment of the extended Frame ID space to IEEE task groups or SDOs. The value 0b111 111 was agreed to be assigned to TIA to ratify the TR51 Frame ID, giving TIA effectively 4 Frame IDs.
The frame format associated with extended Frame ID values is to be defined with each Frame ID as usual.
Notes: May 14
Page 9

## Slide 10: TG28 Changes ETSI TC ERM change requests
Slide 10
2) ID Management
SC-M agreed to recommend that IEEE should manage the allocation of various resource IDs including IE IDs. The re-definition of 'unmanaged' ID ranges to 'Reserved' will be coordinated with vendors who have already used 'unmanaged' range values in their products.
Requests for resource values by external SDOs should be via the MOU channel between IEEE and the external SDO. IEEE will review the request and may suggest alternate solutions instead of assigning resource identifiers where appropriate. The timescale for response to a request should cover 2 IEEE meetings (i.e. of the order 2 months).
A liaison response to ETSI should be generated to report on progress on discussions of resource allocation management.
Notes: May 14
Page 10

## Slide 11: TG28 Changes ETSI TC ERM change requests
Slide 11
3) IE Descriptor Format
SC-M agreed to recommend that the last version number value (0b11) for 15.4-2011 frame types (Beacon, Data, ACK, MAC Command) should be used to indicate that IEs use TLV descriptor format. Version 0b10 frames (current 15.4e values) use LTV descriptor format.
Similarly, Version 0b01 Multipurpose frames use TLV descriptor format. Existing 0b00 Version Multipurpose frames use LTV descriptor format.
Any future changes to 15.4-2011 frames can be accommodated by the large available extended frame ID space.
A final note was also agreed that the one remaining reserved bit in 15.4-2011 frames should be assigned if possible when the new version is defined - otherwise it will not be possible to use the bit as there is no further version number space
Notes: May 14
Page 11

## Slide 12: 15-14-0224 Comments
Slide 12
Focus is on high severity, technical comments:
Resolutions are captured in 15-14-0224-06
Notes: May 14
Page 12

## Slide 13: 802.15.4 Revision Schedule
Slide 13
Comment collection
  Start 23 May
  End 6 June
Letter Ballot
  Start 14 June
  End 13 July (San Diego)
Recirculations
  Start 27 July
  End 14 Oct
Sponsor Ballot
  Start 17 Nov
  Ends 17 Dec
Recirculations
  Start 5 Jan 2015
  End 2 Mar 2015
EC submittal 13 March 2015 (Berlin)
RevCom 5 June 2015
Notes: May 14
Page 13

## Slide 14: SCm motions
Slide 14
Approve draft for release to SCm reflector for comments:
Move that SCm forward document P802.15.4-REVb-DF0.pdf, edited in accordance with the instructions in document 15-14-0224-06, for an informal comment review by the SCm.
BRC:
SCm requests that 802.15 WG approve the formation of a Ballot Resolution Committee (BRC) for the WG balloting of the 802.15.4 Revision draft standard with the following membership: Pat Kinney, J Gilb, B Rolfe, C Powell, Fumihide Kojima, and P Wete. The 802.15.4 Revision BRC is authorized to approve comment resolutions and to approve the start of balloting the 802.15.4 Revision draft on behalf of the 802.15 WG. Comment resolution on recirculation ballots between sessions will be conducted via reflector email and via teleconferences announced to the reflector at least 7 days in advance.
Notes: May 14
Page 14

## Slide 15: SCm motions to WG15
Slide 15
BRC:
Move that 802.15 WG approve the formation of a Ballot Resolution Committee (BRC) for the WG balloting of the 802.15.4 Revision draft standard with the following membership: Pat Kinney James Gilb, Benjamin Rolfe, Clint Powell, Billy Verso, Kunal Shah, Dalton Victor, Phil Beecher, Fumihide Kojima, and Patrick Melet. The 802.15.4 Revision BRC is authorized to approve comment resolutions and to approve the start of balloting the 802.15.4 Revision draft on behalf of the 802.15 WG. Comment resolution on recirculation ballots between sessions will be conducted via reflector email and via teleconferences announced to the reflector at least 7 days in advance.
Moved by Pat Kinney
(no second needed)
Notes: May 14
Page 15

## Slide 16: SCm motions to WG15
Slide 16
Next Conference Call:
Monday, 9 June at 15:00 PDT, 17:00 CDT, 22:00 GMT
Tuesday, 10 June at 06:00 Beijing, 07:00 Tokyo
Notes: May 14
Page 16