## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Issues with CSMA-CA in 802.15.4]
Date Submitted: [26 June 2014]
Source: [Patrick Kinney] Company [Kinney Consulting LLC]
Address [Chicago area, IL, USA]
Voice:[+1.847.960.3715], E-Mail:[pat.kinney@ieee.org]
Re: [Justification for changes to 802.15.4]
Abstract: [Errors and corrections to CCA terms and definitions]
Purpose: [To assist in the comment resolutions to CSMA-CA]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Revision to 802.15.4-2011 with roll-ups of:
802.15.4e-2012
802.15.4f-2012
802.15.4g-2012
802.15.4j-2013
802.15.4k-2013
802.15.4m-2014
802.15.4p-2014
And corrigenda as per 15-12-0367, changes requested by ETSI, and clarifications to such entities as timing for Acknowledgment frames, et al.
802.15.4-2015

## Slide 3: Clarifications of Timing Terms (for more details see 15-14-110-02, 15-14-0244-00)
Interframe spacing:
  SIFS Same, no changes
  LIFS Same, no changes
  AIFS New term, Ack Inter-Frame Spacing (The value of AIFS is 1ms for the SUN PHYs, LECIM PHYs or TVWS PHYs. The value of AIFS is equal to macSIFSPeriod for all other PHYs)
Tack Deleted
macEnhAckWaitDuration Deleted
macAckWaitDuration Deleted (note: remove from 20.1)
aTurnaroundTime RX-to-TX or TX-to-RX turnaround time (1ms
for SUN, TVWS, LECIM, 12 symbols for all else)

## Slide 4: Clear Channel Access (CCA)
Intent is to provide a mechanism to share (i.e. coexist) the medium with other devices by using a Listen Before Talk (LBT) algorithm, i.e. don’t interrupt someone when they are talking.
802.15.4 has two methods of determining if the channel is busy:
  Carrier detect: detect if a similar device (i.e. uses the same modulation and spreading) is currently transmitting on the channel
  Energy detect: detect if any device is transmitting on the channel
Carrier detect requires more time to identify the signal than an energy detection

## Slide 5: CCA detection time
There are many different terms used in 802.15.4 to describe the duration of the CCA operation:
aCCATime - units of symbols, for all PHYs other than MR-OQPSK, the duration of 8 symbol periods. For the MR-O-QPSK PHY, this value is either 4 or 8 symbol periods.
phyCCADuration: units of symbols, for PHYs operating in the 920 MHz band or the 950 MHz band
CCA detection time (Preamble sense): units of symbols, for HRP UWB PHY, this value is 40 symbol periods
macTsCCA – units of μs and value range of 0 – 0xFFFF, used by TSCH regardless of PHY

## Slide 6: CCA detection time
ETSI 300 328 (2.4 GHz devices) states in 4.3.2.6.3.2.3 the following limit for minimum listening time required for devices using LBT:
Before a transmission or a burst of transmissions, the equipment shall perform a Clear Channel Assessment (CCA) check using energy detect. The equipment shall observe the operating channel for the duration of the CCA observation time which shall be not less than 18 μs.
By only bounding the minimum detect time, this clause gives a media access advantage to those devices with short CCA times, such as 802.11 devices over devices with longer CCA times such as the 8 symbols (128 μs) stated in 802.15.4

## Slide 7: CCA detection time
ETSI 300 220 (<1 GHz devices) states in 9.2.2.2 the following limit for minimum listening time (required for devices with transmit duty cycles > 0.1%):
The total listen time, tL, consists of a fixed part, tF, and a pseudo random part, tPS, as the following: tL = tL + tPS
a) The fixed part of the minimum listening time, tF, shall be 5 ms.
b) The pseudo random listening time tPS shall be randomly varied between 0 ms and a value of 5 ms or more in equal steps of approximately 0.5 ms
This detect time regulation of 5 – 10+ ms is significantly longer than the 8 symbols (128 μs) stated in 802.15.4

## Slide 8: CCA detection time recommended change
To better accommodate regulations such as ETSI 300 328 and 300 220, and to consolidate detection times; change from using the constant aCCATime to a PIB such as macCCATime with units of μs and a range of 0 – 16,000

## Slide 9: CCA threshold values
The CCA threshold level (TL) is that point where the medium is judged to be clear or busy:
CD TL is not defined in 802.15.4
ED TL is defined:
  All PHYs (except for MR-O-QPSK): at most 10 dB greater than the specified receiver sensitivity for that PHY (9.2.7)
  MR-O-QPSK PHY: the ED threshold shall not exceed -90 dBm (21.6.13)

## Slide 10: CCA threshold values
However ETSI 300 328 (2.4 GHz devices) states:
The [ED] detection threshold shall be proportional to the transmit power of the transmitter: for a 20 dBm e.i.r.p. transmitter the detection threshold level (TL) shall be equal or less than -70 dBm/MHz at the input to the receiver (assuming a 0 dBi receive antenna). For power levels below 20 dBm e.i.r.p., the detection threshold level may be relaxed to TL = -70 dBm/MHz + (20 dBm - Pout e.i.r.p.)/1 MHz (Pout in dBm).

## Slide 11: CCA threshold values
Then again, 300 220 (< 1 GHz devices) states:
The maximum value of the LBT threshold for the receiver in the listen mode is:
RX BW | TX < 20 dBm | TX < 27 dBm | Max TX on Time
6.25 kHz | -102 dBm | -106 dBm | < 1 second
12.5 kHz | -99 dBm | -103 dBm | 
20, 25 kHz | -96 dBm | -100 dBm | 
50 kHz | -93 dBm | -97 dBm | 
100 kHz | -90 dBm | -94 dBm | 
200 kHz | -87 dBm | -91 dBm | 
500 kHz | -83 dBm | - | 
600 kHz | -82 dBm | - | 

## Slide 12: CCA threshold value recommended change
To allow for these regulations, change 9.2.7 to read: “Except for the MR-O-QPSK PHY, unless otherwise stipulated by the controlling regulation, ED threshold shall correspond to a received signal power of at most 10 dB greater than the specified receiver sensitivity for that PHY…”

## Slide 13: Summary
Roll-up of 7 amendments show that many amendments used different terms to address common behaviors
CCA durations and threshold levels need to be flexible to be in line with regulatory specification such as ETSI 300 328 and ETSI 300 220